## Slide 1: ILD Status
100th ILC@DESY meeting
Ties Behnke, DESY 18.10.2013

## Slide 2: ILD: where are we?
2013: delivery of the ILD DBD as part of the ILC TDR
Fairly sophisticated system design, no complete engineering design
First “complete” estimate of the cost
2013: site decision in Japan, but no overall decision yet on the project
2013: positive statements around the world supporting an ILC in Japan,
European strategy process
Snowmass process in the US
We are in a transition period between pre-project (concept) phase and project (collaboration) phase
For the near future R&D will remain our main goal, but we need to prepare to shift gears rapidly once the project is approved.

## Slide 3: Concepts at the ILC
1998
2006
2007
2009
2009
2013
2004
TESLA and GLD detectors publish first documents
2001
TESLA TDR
WWS starts concept studies
Detector concept reports:
LDC, GLD, SiD, 4th
LDC and GLD merge into ILD
LOI
delivered
SiD, ILD validated
2003
SiD is first proposed at ALCPG
LOI phase
DBD/ TDR delivered
TDR/ DBD phase

## Slide 4: The current ILD concept
Started as a combination of GLD and LDC in 2007
(LCWS 2007 at DESY)
Some detailed optimization work done, but main parameter choices were “ad hoc” (politics) as much as physics driven
Now is the time to re-open the box and look at all choices:
There are no forbidden areas There are no prejudices

## Slide 5: Window of Opportunity
We might have some limited time to
Look carefully into our fundamental design choices
Take costs more fully into account than we have done so far
Question Choices and prejudices
Do fundamental studies on – in particular – the impact on physics
Once ILC is a real project we might not have this chance again!
Lets use it wisely!
Situation in Japan: see talk by Satoru/ Hitoshi later today.
Window of opportunity NOW

## Slide 6: ILD Costs
Costing exercise as part of DBD
Needs significant more work and checking, but main messages are clear.
Huge effort by LLR group for the DBD

## Slide 7: ILD cost scaling
Cost scaling law with different systems radius
Potentially large impact on the cost
Careful optimization of cost –performance benefit is needed

## Slide 8: The inner system
Do we understand our performance requirements?
VTX detector
Silicon tracking?
Readout speed might be an important variable to control background and complexity:
Are the ambitious enough in ILD in this respect?
Do we understand / do we have a proper design of the beamtube etc?
We propose a big Silicon system for ILD: are we sure of its parameters?
What about the outer Silicon system? How much of this is baseline?
Design of the VTX detector
Role and merrit of double layer
Alternative geometries?

## Slide 9: Vertex detector
Excellent impact parameter resolution better than (5⊕10/p sin3/2 Θ ) μm is required for efficient flavor tagging
3 layers of double ladders (ca 1 mm apart) (6 pixel layers)
  Effect on pair-background rejection is expected, but not demonstrated yet
Barrel only: |cosΘ|<0.97 for inner layer and |cos Θ |<0.9 for outer layer
Point resolution <3um for innermost layer
Material budget: 0.3%X0/ladder=0.15%X0/layer
Sensor options: CMOS, FPCCD, DEPFET, others?

## Slide 10: TPC: ILD
Time Projection Chamber: The central tracker of ILD
Tracks can be measured with many (~200/track) 3-dimensional r-f-z space points
srf<100um is expected for all drift distances
dE/dx information for particle identification
Two main options for gas amplification: GEM or Micromegas
Readout pad size ~ 1x6mm2  106 pads/side
Pixel readout R&D as a future alternative
Material budget: 5%X0 in barrel region and <25%X0 in endplate region
Cooling by 2-phase CO2
Momentum resolution: 2 10^-5

## Slide 11: Tracking System
Overall system optimization:
Aspect ratio
Outer radius
Role of Silicon
Role of material e.g. in the TPC system
Forward tracking
Momentum resolution:
Current parameter is strongly driven by Higgs Mass measurement: are these arguments still valid?
If we can relax the requirements: what is the impact on TPC/ Silicon?
  Complex interplay of TPC, inner and outer Silicon

## Slide 12: Tracking System
Overall system optimization:
Aspect ratio
Outer radius
Role of Silicon
Role of material e.g. in the TPC system
Forward tracking
Momentum resolution:
Current parameter is strongly driven by Higgs Mass measurement: are these arguments still valid?
If we can relax the requirements: what is the impact on TPC/ Silicon?
  Complex interplay of TPC, inner and outer Silicon
Purity of ZH->llcc

## Slide 13: Material
Material issues System thickness
Silicon tracker - ECAL/ HCAL thickness
TPC tracker - choice of material?
And never forget:

## Slide 14: Material
Material issues System thickness
SiD material: this might be aggressive, but we are not - ECAL/ HCAL thickness better… - choice of material?
And never forget:

## Slide 15: Questions: a possible list
What is the right outer diameter for the VTX?
Are we confident about performance in the forward direction
What is the minimum momentum we need to reconstruct
Does the data size have an impact on design of the VTX?
Where do we need highest momentum resolution
  Higgs mass, invisible higgs, branching ratios?
How important are systematic effects to the final performance
Do we understand possible biases in the momentum estimation
Do we understand the relative roles of TPC and Silicon?
What is the impact of material on the physics performance
  Barrel
  Endcap

## Slide 16: Pflow as a driving force
Pflow has been at the core of the definition of ILD
Size
Calorimeter performance
Tracking performance

## Slide 17: Pflow: Impact
W/Z separation:
Key ingredient to define the requirement on particle flow performance
Impact on actual physics studies: typically less clear than thought:
Most studies show little to no sensitivity to the exact performance But: how poorly do we do with a significantly deteriorated particle flow performance?

## Slide 18: Imaging Calorimeter
Calorimetry is clearly a main part of ILD
Can we make our calorimeter cheaper?
Can we make the step from ECAL to HCAL less severe?
Can we find an intelligent way to stage the system?
Si for the ECAL is a very attractive, but also very expensive option

## Slide 19: Overall Detector size
Outer radius of Yoke:
Defined from push-pull condition on field < 50 mG
Is this the correct requirement
Changing this will have a huge impact on size (and cost)
Other constraints:

## Slide 21: ILD Organisation
The Plan:
At the ECFA meeting May 2013:
Proposed and discussed new structure for ILD
At Cracow: iterate the organisation structure, further disucssions are needed
LCWS 2013: initiate the new ILD structure formally.
Document describing the new structure is on the indico WEB site under the Thursday meeting
Comments are welcome.

## Slide 22
ILD operations board (>20)
Detector Coordinator
Physics Coordinator
MDI
VTX
TPC
ECAL
HCAL
Coil/ Yoke
top
Higgs
…
ILD Management group (4)
Speaker (2)
Publication office
FCAL
SI
Institute Assembly
Integration
Software/ Tools
muon
DAQ
Central design group
Physco, detco, 2 free members
Detector systems groups organize the connection to the R&D collaborations
Documentation
Central groups
….

## Slide 23: ILD
We have a good and clear starting point
The next step will be a re-optimization of the detector
We will need to make sure that we have an adequate and appropriate structure.