## Slide 1
Beam Instrumentation for Linear Colliders
What is special about the beam instrumentation
of a Linear Collider ?
What are the main Instrumentation needs?
Details on: - Measurement of nm beam positions
- Measurement of um transverse beam sizes
- Measurement of fs-scale long profiles - Beam synchronization at the fs-scale - Keeping the beams in collision
LC school 2013 H.Schmickler, CERN
With a big “Thank You” to T. Lefevre for many splendid slides....
3hours B-course at the 2013 LC school Antalya, Hermann Schmickler, CERN-BE-BI

## Slide 2
Luminosity of high energy Collider
A linear collider uses the beam pulses only once:
Need to accelerate lots of particles
Need very small beam sizes
e+
e-
nb
1/frep
N
  nb = bunches / train N = particles per bunch frep = repetition frequency sx,y = beam size at IP HD = beam-beam enhancement factor
Collider luminosity [cm-2 s-1] is approximately given by

## Slide 3
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
The small beam size challenge
Adapded from S. Chattopadhyay, K. Yokoya, Proc. Nanobeam `02
LEP: sxsy  1306 mm2
ILC: sxsy  500(3-5) nm2

## Slide 4
Luminosity issue with intense beams - Disruption
beam-beam characterised by Disruption Parameter:
Enhancement factor (typically HD ~ 1.5 ÷ 2) is given by:
sz = bunch length
Field of the opposite particle will distort the other beam during collision:
- Pinch effect (can become instable if two strong)
– Beam-beam deflections – use to adjust beam overlap and luminosity

## Slide 5
Luminosity issue with intense beams - Disruption
For LC, typical value of HD ~ 1-2

## Slide 6
Luminosity issue with intense beams - Beamstrahlung
High energy Beamstralung photons can convert in strong field into e+/e- pairs: background for the detector
  Coherent e+e- pairs
    Direct photons conversion in strong fields
    Negligible for ILC but high for CLIC : Few 108 particles per Bunch crossing
  Incoherent e+e- pairs
    Photons interacting with other electron/photon
    Few 105 particles/Bunch crossing
Generation of Synchrotron Radiation photons of particles in the strong EM field of the opposite bunch
e+ e- pairs
Beamstrahlung photons
e+
e-

## Slide 7
Beam size for minimizing beamstrahlung
rms relative energy loss
induced by Beamstrahlung
we would like to make (sx sy) small to maximise luminosity
and keep (sx + sy) large to reduce dSB
Rule:
Make sx large to limit dBS
Make sy as small as possible to achieve high luminosity.
Trick: use “flat beams” with sx >> sy
dBS ~ 2.4% @ ILC -- dBS ~ 29% @ CLIC

## Slide 8
Hour glass effect – Bunch length
For achieving small Beta function ( small beam size) at IP, the beta function rapidly increases as the particle move away from the collision point
Variation of beam size along the bunch

## Slide 9
Hour glass effect – Bunch length
Rule: Keep by ~ sz
From Nick Walker for TESLA

## Slide 10
A final luminosity scaling for Linear collider ?
high RF-beam conversion efficiency hRF and RF power PRF
small normalised vertical emittance en,y
strong focusing at IP (small by and hence small sz)
with
Extremely small beam spot at Interaction Point beam delivery system, stability
  Generation of small emittance damping rings
  Conservation of small emittance wake-fields, alignment, stability
  Generation and acceleration of short bunches Bunch compressor

## Slide 11
What‘s in the CLIC CDR for BI?
MB Instruments | Surface | Tunnel | Total
Intensity | 86 | 98 | 184
Position | 1539 | 5648 | 7187
Beam Size | 34 | 114 | 148
Energy | 19 | 54 | 73
Energy Spread | 19 | 4 | 23
Bunch Length | 17 | 58 | 75
Beam Loss | 1936 | 5854 | 7790
Beam Polarization | 11 | 6 | 17
Tune | 6 | 0 | 6
Luminosity |  | 2 | 2
DB Instruments | Surface | Tunnel | Total
Intensity | 38 | 240 | 278
Position | 1834 | 44220 | 46054
Beam Size | 32 | 768 | 800
Energy | 18 | 192 | 210
Energy Spread | 18 | 192 | 210
Bunch Length | 24 | 288 | 312
Beam Loss | 1730 | 44220 | 45950
Notes: Big variarity of instruments more the ~ 111k instruments
Every measurable is described with the requirements in the different parts of the machine, as well as their number.

## Slide 12
Beam Position Monitors - Baseline
High accuracy (5um) resolution (50nm) BPM in Main Linac and BDS
Very high numbers of BPMs for the DB decelerator
Various range of beam pipe diameters from 4mm to 200mm all over the complex (to minimize resistive wakefield effects)
Notes: The much challenging requirements comes from the main Linacs.
Not only to the big numbers of instrument to beb build and maintained.
For the main linac we need 4000 high resolution/high accuracy BPMs. With 50 nm resolution. In the BDS down to 3nm. Resoultions in the order of 10nm has been demonstrated but with high Q cavity BPMs …we cannot due to the required time resolution. In ATF2 the highest number of cavity BPMs in history 30pc
For the DB more than 40000 which demands a close eye on costs and simplicity both for manufaturing and maintenance…1% down means 400 BPMs down
Outside the main linacs we have another 8000 BPMs almost 10 times more than LHC

## Slide 13
Beam Position Monitors - Baseline
Design by Manfred Wendt & co (FNAL)
Designed by Steve Smith
Notes: Challenges CLIC Main Beam 50n with 10ns time resolution, low Q stainless steel
Three BPM types and three different acquisition system types
Cavity BPM 14GHz
Damping ring BPM 2 GHz
Direct sampling 2-500MHz
Calibration is mandatory to obtain the high demands on accuracy, which increas the complexity significantly.

## Slide 14
Transverse Profile Monitors - Baseline
Critical Issue on micron resolution beam profile measurements (> 100 monitors)
Relatively big number of Instruments ~ 1000
Imaging of high energy spread beams at the end of the decelerator
Charge density limitation problems in many places / Strong need for non-interceptive devices : two systems required to cover the total dynamic range
The thermal limit for ‘best’ material (C, Be, SiC) is 106 nC/cm2
Notes: Challenges CLIC Main Beam

## Slide 15
Transverse Profile Monitors - Baseline
Most of the systems based on the combined use of OTR screens and Laser Wire Scanners
- OTR used almost everywhere for commissioning (replaced by synchrotron radiation in rings)
- LWS 1um resolution required for the Main beam
- LWS used in the Drive Beam injector complex for high charge beams (full charge)
Non-interceptive monitor based on Diffraction radiation as a cheap alternative to LWS for both Drive and Main Beams
Notes: Challenges CLIC Main Beam

## Slide 16
Now we treat in detail:
- Measurement of nm beam positions
- Measurement of um transverse beam sizes
- Measurement of fs-scale long profiles - Beam synchronization at the fs-scale - Keeping the beams in collision (IP feedback)

## Slide 17
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Conserving small Emittance along the Main Linac
  Wakefields in accelerating structures (damping of high order mode)
D
t
b
Bunches passing through an accelerating structure off-centre excite high order modes which perturbs later bunches
    Tolerances for acc. Structures alignment
    Cavity alignment at the 300 mm level @ ILC compared to 5 mm @ CLIC
    Need wakefield monitor to measure the relative position of a cavity with respect to the beam

## Slide 18
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Proposed correction scheme
Girder
Girder
Movers
AS with WFM
Electron bunch
Wakefield kicks from misaligned AS can be cancelled by another AS
One WFM per structure (142000 monitors) and mean offset of the 8 AS computed
WFM with 5um resolution
Need to get rid of the 100MW of RF power at 12GHz present in the structures
D. Schulte

## Slide 19
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
WakeField Monitor design
Monopole mode
Opposite ports signals are in phase
Dipole mode
Opposite ports signal have opposite phase
E Field
E Field
When we substract the opposite port signals, the monopole mode is cancelled and the dipole mode amplitude is increased
F. Peauger

## Slide 20
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Regular cells with SIC load
Middle cell with WFM
SIC Load
Coaxial connector
12GHz accelerating cavity
Long Waveguide
Cut-off at 12GHz
18.19 GHz
11.95 GHz
14.81 GHz
Recombined port signal amplitude
F (GHz)
F. Peauger
WakeField Monitor design

## Slide 21
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Conserving small Emittance along the Main Linac
  Dispersive emittance dilutions : offset of quadrupoles
    Beam based alignment to define a precise reference using high precision BPM (50nm resolution)
    Dispersion free-steering - Align quadrupoles precisely
    High resolution cavity BPM (50nm for CLIC)
    Long linac  large number of BPMs: 2000@ILC – 4000@CLIC

## Slide 22: Improving the Precision for Next Generation Accelerators
Standard BPMs give intensity signals which need to be subtracted to obtain a difference which is then proportional to position
  Difficult to do electronically without some of the intensity information leaking through
    When looking for small differences this leakage can dominate the measurement
    Typically 40-80dB (100 to 10000 in V) rejection  tens micron resolution for typical apertures
Solution – cavity BPMs allowing sub micron resolution
  Design the detector to collect only the difference signal
    Dipole Mode TM11 proportional to position & shifted in frequency with respect to monopole mode
f / GHz
U / V
Frequency Domain
TM01
TM11
TM02
U~Q
U~Qr
U~Q
Courtesy of D. Lipka,
DESY, Hamburg
TM01
TM11
TM02

## Slide 23: Today’s State of the Art BPMs
Obtain signal using waveguides that only couple to dipole mode
  Further suppression of monopole mode
Prototype BPM for ILC Final Focus
  Required resolution of 2nm (yes nano!) in a 6×12mm diameter beam pipe
  Achieved World Record (so far!) resolution of 8.7nm at ATF2 (KEK, Japan)
Monopole Mode
Dipole Mode
Courtesy of D. Lipka,
DESY, Hamburg
Courtesy of D. Lipka & Y. Honda

## Slide 24
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Cavity BPM
“Pillbox” cavity BPM
  Eigenmodes:
  Beam couples to dipole (TM110) and monopole (TM010) modes
  Common mode (TM010) suppression by frequency discrimination
  Orthogonal dipole mode polarization (xy cross talk)
  Transient (single bunch) response (QL)
  Normalization and phase reference

## Slide 25
General idea:
- low Q-factors
- monopole modes decoupling
BPM parameters:
- Cavity length
- Waveguide dimensions
- Coupling slot
- Coaxial transition
3. Parasitic signals:
- monopole modes
- quadruple modes
5. Tolerances calculation:
- coupling slots
  waveguide to cavity
- cavity to pipe
Cavity spectrum calculations:
- Frequency
- R/Q, Q
- TM11 output voltage
Cavity BPM design steps
4. Cross coupling:
- waveguide tuning
- 2 ports vs 4 ports
loop
loop
1
1
1
1
1

## Slide 26
R4
R12.05
2
1
7
2
14
20
25
BPM Geometrical Dimensions

## Slide 27
Waveguide to coaxial transition
5.05
5

## Slide 28
BPM Cavity Modes
Mode TM01
Mode TM02
Mode TM21
Mode TM11

## Slide 29
Waveguide Low-Q resonances
Mode WG_TM11
Mode WG_TM21

## Slide 30
Multi-bunch Regime Rejection
Single Bunch Signals :
TM11 signal
TM01 signal
TM21 signal
Rejection:
Rejection:
Multi-bunch regime (2 GHz)
TM01, TM11, TM21
Time, [s]

## Slide 31
Monopole Mode Coupling due to Mechanical Errors
Slot Rotation
Slot Shift
Hφ
Hz
∆α
Strong Magnetic Coupling
~∆αx
∆x
Hφ
Hz
Slot Tilt
Weak Electric Coupling
Weak Magnetic Coupling
+
2. Slot tilt causes the non zero projection of TM01 azimuth magnetic (Hφ) and longitudinal electric (Ez) filelds components in the cavity to a transverse (Hx) and vertical (Ey) components of TE10 mode in the waveguide. Because both Hx and Ey are close to zero near the waveguide wall tilt error causes the weak electric and weak magnetic coupling of monopole mode to waveguide.
∆θ
Hφ
Ey
Ey
Hx
Slot rotation causes the non zero projection of TM01 azimuth magnetic field component (Hφ) in the cavity to a longitudinal one (Hz) of TE10 mode in the waveguide. Small slot shift is equivalent to rotation with angle: αx ~ arctan(Δx/Rslot). Therefore both slot rotation and shift cause strong magnetic coupling of monopole mode to waveguide.

## Slide 32
TM01 Mode Leak (tolerances calculations)
∆x
a)
∆α
c)
Slot Rotation
Slot Shift
TM01 normalized signals
∆θ
Waveguide Tilt

## Slide 33
Now we treat in detail:
- Measurement of nm beam positions
- Measurement of um transverse beam sizes: OTR, ODR, laser wire scanner (LWS)
- Measurement of fs-scale long profiles - Beam synchronization at the fs-scale - Keeping the beams in collision (IP feedback)

## Slide 34
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Measuring small beam size in a Linear Collider
Small beam size
High beam charge
Required high precision from the Damping ring to the Interaction Point (IP)
  Beam energy ranges from 2.4GeV  1.5TeV
  Tens of km of beam lines – Big number of instruments
High Charge Densities
> 1010 nC/cm2
Flat Beams (ex >> ey) : Think of a flat noodle !
The thermal limit for ‘best’ material (C, Be, SiC) is 106 nC/cm2
 | ILC | CLIC
Beam Charge (nC) | 7875 | 190
Hor. Emittance (nm) | 655 | 40
Ver. Emittance (nm) | 5.7 | 1

## Slide 35
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
‘Beam Profile Horror Picture Show’
Intercepting devices limited to single (or few) bunch mode
Wire Scanner
200mm thick mirror polished Si and CVD SiC wafer
Optical Transition Radiation

## Slide 36
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
High Resolution Imaging System using OTR
Diffraction effect would determine the resolution limit of the measurements
Camera
Charged
Particle
OTR screen
Lens
X. Artru et al, NIM AB 145 (1998) 160-168
C. Castellano and V.A. Verzilov, Physical Review STAB 1, (1998) 062801
OTR angular distribution: Peak at 1/g but large tails
  Problem for very high energy particles
Aperture of the focussing lens : q >> 1/g
Large tails

## Slide 37
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
High Resolution Imaging System using OTR
Classical OTR configuration :
90o observation angle
Charged
Particle
OTR screen
  Depth of field limits the resolution because the image source is not normal to the optical axis
Make Df > sy
sy
Camera
Df

## Slide 38
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
High Resolution Imaging System using OTR
Imaging small beam size  large magnification  short Depth of field (Df)
Smaller Df  Tilt the screen
Camera
sy
OTR screen
Df

## Slide 39
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Diffraction Radiation
Charged
Particle
Two slits DR target
Camera
Radiation wavelength
Beam energy
h impact parameter
Measuring the angular distribution of the interference pattern between the DR emitted by the two slits
Non destructive alternative for beam size measurement (not imaging anymore)
After the Damping ring the beam has few GeV and ODR is generated for reasonable values of h

## Slide 40: Approach for the beam size measurements
Assume a Gaussian beam profile
y is the electron beam size and
is its offset with respect to the slit center

## Slide 41: Beam size effect
Projection
Projected vertical polarization component
 = 2500
y=0
y=30m
x – x detector angular acceptance
x
Intensity (arb. units)

## Slide 42
l = 0
l = /10
l = /4
 = 1/ = 0.4mrad
ax = 0
ax=0.05mm
ax = 0.1mm

## Slide 43: Target configuration
A silicon wafer covered with a thin gold foil

## Slide 44: Target configuration E. Chiadroni, et al., NIM B 266 (2008) 3789 E. Chiadroni, et al., DIPAC’09

## Slide 45: Method for the beam size determination
max
min

## Slide 46
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Diffraction Radiation
P. Karataev et al., Physical Review Letters 93 (2004) 244802
P. Karataev et al, Physical Letters A345 (2005) 428
Beam size measured by ODR (mm)
Beam size measured with Wire Scanner (mm)
Investigation on the low emittance beam at ATF, KEK, Japan
E=1.28GeV ; l=445nm ; h=70mm

## Slide 47
 | E (GeV) | σH (µm) | σV (µm)
CesrTA | 2.1 | 320 | ∼9.2
 | 5.3 | 2500 | ∼65
To design and test an instrument to measure on the micron-scale the transverse (vertical) beam size for the Compact Linear Collider (CLIC) using incoherent Diffraction Radiation (DR) at UV/soft X-ray wavelengths.
Project aim : Exp. Validation of ODR transverse profile measurements in a circular machine (CESR-Ta, Cornell)
D. Rubin et al., “CesrTA Layout and Optics”, Proc. of PAC2009, Vancouver, Canada, WE6PFP103, p. 2751.
Cornell Electron Storage Ring Test Accelerator (CesrTA) beam parameters:
http://www.cs.cornell.edu
DR
xBSM
vBSM

## Slide 48: Project phases
Phase 1: (2013)
UV - Optical wavelengths
Measurement of beam size σy ≤ 50 µm
Observation of beam lifetime
Phase 2: (2014-2016)
Relocate experiment to beam waist in L3 straight section of CesrTA
Soft x-rays
Measurement of beam size σy ≤ 10 µm

## Slide 49
Vacuum chamber assembly
Gate valve to disconnect CESR vacuum for target changeover
Target mechanism: rotation + translation IN/OUT
LHS = Left Hand Side
RHS = Right Hand Side
LHS : CHESS operation
RHS: DR experiment
Optical system connected to DR viewport

## Slide 50
Far-field Condition:
 | 2.1 GeV | 5 GeV
200 nm | 0.54 m | 3.18 m
400 nm | 1.08 m | 6.37 m
given γ and λ:
L = distance from source of DR to detector
Compact optical system is in the prewave zone therefore a biconvex lens is used with detector in back focal plane to obtain the angular distribution.
(Pre-wave zone effect in transition and diffraction radiation: Problems and Solutions -P. V. Karataev).
DR from viewport
f
2. Bi-convex lens to reduce prewave zone effect
OR
achromatic lens to image target
3. Bandpass filter
4. Polarizer
6. UV Camera
1. Mirror
Optical System
Gated ICCD camera

## Slide 51
“Bonding by molecular adhesion (either ‘direct wafer bonding’ or ‘fusion bonding’) is a technique that enables two substrates having perfectly flat surfaces (e.g., polished mirror surfaces) to adhere to one another, without the application of adhesive (gum type, glue, etc.).”
Patent US 8158013 B2
Molecular adhesion target (2mm version shown here). 1mm aperture version was used at CesrTA.
Coplanarity measurement:
Metrology by Winlight Optics
Molecular adhesion target

## Slide 52
T. Aumeyr et al., IBIC2013, WEPF18.
Left peak
DR intensity decays exponentially from slit edge
SR intensity uniform over small regions
From simulations, max SR intensity (vert. pol.) does not occur at slit edge
DR intensity [ph/e-]= k * SR intensity [ph/e-]
DR vert. pol. ph/e-
SR. vert. pol. ph/e-
Identification of DR in target imaging

## Slide 53: DR target imaging
2.1 GeV
1 mA single- bunch beam
400 nm DR observation wavelength
Data broadening possibly due to:
data taken for theoretical model and Zemax : single e-
Polariser misalignment → some horiz. pol. DR and synchrotron radiation (SR)
10 ± 2 nm bandwidth → data smearing (small)
15 ms exposure time (CesrTA rev. period ) → smearing from beam jitter
Theory-
D. Xiang et al., Phys. Rev. ST Accel. Beams, 10 (2007) 062801.
Zemax-
T. Aumeyr et al., IBIC2013, WEPF18.

## Slide 54: Mask
4 mm
2 mm
mask
target
Technical drawings by N. Chritin,
Metrology by L. Remandet
Silicon Carbide
Laser machining
Not etched (orientated perpendicular to beam)
Mask aperture = 4 * target aperture → avoid destructive interference (ODRI)
Specification | Location 1 (in µm or in µrad) | Location 2 (in µm or in µrad)
Maximum to minimum | ≈ 10 µm | ≈ 80 µm
Tilt in X direction | 0 µrad | -1897 µrad
Tilt in Y direction | 0 µrad | -13913 µrad
LOCATION 1
LOCATION 2
Y
X

## Slide 55
Vert. pol.
Horiz. pol.
Total intensity at 400nm, 10%bw
= 4.31643e+09 ph/s
Total intensity at 400nm, 10%bw
= 2.30315e+10 ph/s
A. Jeff
SRW simulations

## Slide 56
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Laser Wire Scanner
Baseline solution for linear collider: high spatial resolution would rely on Laser Wire Scanner
e-
hnsc=2 g02 hn0
(bsc, gsc)
hn0
(b0 ,g0)
q  1/g0
Y=/2
Thomson/Compton scattering
e- beam
High power laser
Scanning
system

## Slide 57
Laser Beam
l0 : Laser wavelength
w0 : Laser waist size
ZR : Rayleigh range
ZR
Electrons Beam
sy : ver. beam size
sx : hor. beam size
w0
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Laser Wire Scanner
The number of X-rays produced is given by
with A the interaction area, Ne and Nlaser are the number of electrons and photons in A
2w0
w0
x
y

## Slide 58
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Laser Wire Scanner
High spatial resolution need very focused laser beam: Need a optimum Focusing system
Lens defined by a focal length f, and diameter D :
Smaller F# is better
Performance of Laser : M2=1 for pure Gaussian distribution
Diffraction
Minimize spherical aberration using several lenses
For the single lens,
small F# makes spherical aberration large.
Spherical aberration

## Slide 59
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Laser Wire Scanner
Design for ATF2 LWS by G. Blair et al

## Slide 60
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Laser Wire Scanner
Design for ATF2 LWS by G. Blair et al
GO to smaller wavelength to do better (green  UV)

## Slide 61
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Laser Wire Scanner
At high energy, the Compton cross section gets smaller
0 = 6.65 10-24 cm2
The number of interaction produced is given by
Increase the Laser Power (10MW and more)

## Slide 62
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Beam size monitoring with Laser Wire Scanner
At high energy (>10GeV) the detection system can be easily done either using the scattered photons or the scattered electrons

## Slide 63
Now we treat in detail:
- Measurement of nm beam positions
- Measurement of um transverse beam sizes
- Measurement of fs-scale long profiles - Beam synchronization at the fs-scale - Keeping the beams in collision (IP feedback)
 | ILC | CLIC linac | XFEL | LCLS
Beam Energy (GeV) | 250 | 1500 | 20 | 15
Linac RF Frequency (GHz) | 1.3 | 12 | 1.3 | 2.856
Bunch charge (nC) | 3 | 0.6 | 1 | 1
Bunch Length (fs) | 700 | 150 | 80 | 73

## Slide 64
Short bunch length measurements
Optical Method
Bunch Frequency Spectrum
RF manipulation
Laser-based beam diagnostic
Produce visible light
Analyse the light pulse using dedicated instruments
Use RF techniques to convert time information into spatial information
The shorter the bunches, the broader the bunch frequency spectrum
Using short laser pulses and sampling techniques
Radiative techniques
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 65
1- Longitudinal Profile   RMS or FWHM values
    More precise information on the beam characteristic
2- Single shot measurements   Sampling measurements
    Do not care about the beam reproducibility
    No additional problem due to timing jitter
3- Non interceptive   Destructive Devices
    Can be used for beam study and beam control for on-line monitoring
    Beam Power : No risk of damage by the beam itself
s
1
n!
Beam instrumentation
CAS intermediate level - Trondheim– 2013
T. Lefevre
Notes: Beam power

## Slide 66
Can we do non intercepting, single shot, beam profile measurement in an easy way ?
1
+
+
=
All in red  ‘perfect system’
Beam instrumentation
CAS intermediate level - Trondheim– 2013
T. Lefevre
Notes: Easy and cost effective

## Slide 67
Radiative techniques
‘Convert particles into photons’
T. Lefevre
CAS intermediate level - Chios– 2011

## Slide 68
Coherent / Incoherent Radiation
At wavelength much shorter than the bunch length, the radiation is emitted incoherently because each electron emits its radiation independently from the others without a defined phase relation
A coherent enhancement occurs at wavelengths which are equal to or longer than the bunch length, where fixed phase relations are existing, resulting in the temporal coherence of the radiation
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 69
S() – radiation spectrum
Sp() – single particle spectrum
N – number of electrons in a bunch
F() – longitudinal bunch form factor
 (s)– Longitudinal particle distribution in a bunch
Radiation Spectrum
Incoherent term
Coherent term
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 70
Limitations :
Use a lot on electrons (for visible light: E > 100 MeV)
Limited to very high energy proton or heavy ion beams
SR appears when a charged particle is bent in a magnetic field
Critical frequency :
Beam curvature
Beam energy
Optical Synchrotron Radiation
g charged particle Lorentz-factor
 is the bending radius
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 71
Cherenkov radiation
‘Equivalent to the supersonic boom but for photons’
Threshold process: Particles go faster than light b > 1/n
n is the index of refraction (n>1)
b is the relative particle velocity
qc is the Cherenkov light emission angle
d the length of the cherenkov radiator
The total number of photons proportional to the thickness of the Cherenkov radiator
T. Lefevre
n
Charged
Particle
Cherenkov photon
d
Limitations :
Using transparent material (Glass n=1.46) : thermal and radiation hardenss issues
Time resolution limited by the length of the radiator
CAS intermediate level - Chios– 2011

## Slide 72
‘TR is generated when a charged particle passes through the interface between two materials with different permittivity (screen in vacuum)’
Optical Transition Radiation
Radiation wavelength
Beam energy
Number of OTR photons per charge particle
~ 5 10-3 in [400-600]nm
Using good reflecting material
The thermal limit for ‘best’ screens (C, Be, SiC) is ~ 1 106 nC/cm2
M. Castellano and V. Verzilov, Phys. Rev. ST-AB 1, 062801 (1998
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 73
‘DR is generated when a charged particle passes through an aperture or near an edge of dielectric materials, if the distance to the target h (impact parameter) satisfies the condition :
Limitations :
Not enough photons in the visible for low energy particles : E < 1 GeV for a decent impact parameter (100mm)
T. Muto et al, Physical Review Letters 90 (2003) 104801
Radiation wavelength
Beam energy
Optical Diffraction Radiation
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 74
Optical method with Incoherent radiation
‘Convert particles into visible photons’
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 75
Time Correlated Single Photon Counting
n!
Geiger-mode Avalanche photodiode converts photon to electrical pulse
Time to Digital converter records pulse arrival time
Visible photon
Precise trigger synchronized with the beam
Sampling Method allowing very high dynamic range if you measure long enough
Avalanche photodiode have deadtime and are subject to afterpulsing
State of the art TDC typically limited to 10ps sampling
D.V. O’Connor, D. Phillips, Time-correlated Single Photon Counting, Academic Press, London, 1984
C.A. Thomas et al., Nucl. Instr. and Meth. A566 (2006) p.762
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 76
Longitudinal profile of the entire LHC ring (89us) with 50ps resolution using SR light
A very large dynamic range should make it possible to see ghost bunches as small as 5e5 protons / 50ps with long integration
A. Jeff
Time Correlated Single Photon Counting
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 77
1
Mitsuru Uesaka et al, NIMA 406 (1998) 371
200fs time resolution obtained using reflective optics and 12.5nm bandwidth optical filter (800nm) and the Hamamatsu FESCA 200
  Limitations : Time resolution of the streak camera :
  (i) Initial velocity distribution of photoelectrons : narrow bandwidth optical filter
  (ii) Spatial spread of the slit image: small slit width
  (iii) Dispersion in the optics
‘Streak cameras uses a time dependent deflecting electric field to convert time information in spatial information on a CCD’
Streak Camera
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 78
Streak camera examples
Observation of 5MeV electron bunch train using cherenkov
Sweep speed of 250ps/mm
s = 8.9ps (2.7 mm)
s = 4.5ps (1.4 mm)
Sweep speed of 10ps/mm
Measure of bunch length using OTR and OSR
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 79
Bunch Length measurement with Coherent Radiation
‘The shorter in time, The broader in frequency’
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 80
Bunch Form Factor for Gaussian distribution
Coherent radiation appears when the bunch length is comparable to or shorter than the emitted radiation wavelength
Assume N = 1010 e/bunch
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 81
Measuring Radiation Spectrum
S() – radiation spectrum ((known in the experiment)
N – number of electrons on the bunch (known from the experiment)
F() – bunch form factor (what you want to find out)
Sp() – single particle spectrum (should be known)
P. Kung et al, Physical review Letters 73 (1994) 96
Coherent Transition Radiation (CTR)
B. Feng et al, NIM A 475 (2001) 492–497 ; A.H. Lumpkin et al, NIM A 475 (2001) 470–475 ; C. Castellano et al, Physical Review E 63 (2001) 056501
T. Watanabe et al, NIM A 437 (1999) 1-11 & NIM A 480 (2002) 315–327
Coherent Diffraction (CDR) or Coherent Synchrotron (CSR)
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 82
1
‘The polychromator enables to get the spectrum directly by a single shot. The radiation is deflected by a grating and resolved by a multi-channels detector array’
T. Wanatabe et al., NIM-A 480 (2002) 315-327
H. Delsim-Hashemiet al., Proc. FLS, Hamburg 2006, WG512
Bunch Frequency Spectrum by Coherent Radiation
B. Schmidt, DESY
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 83
Bunch Frequency Spectrum by Coherent Radiation
Long. Bunch profile S(z)
Long Form Factor
|F(w)|
Spectral Intensity
A(w)
Time Domain
Frequency Domain
Inverse Fourier Transform for symmetric bunch distribution
Extrapolation
(high and low frequencies)
Correction
(transfer function of detection system)
R. Lai and A.J. Sievers, NIM-A 397 (1997) 221 -231
Kramers-Kronig relation
for non symmetric bunches
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 84
RF techniques
‘How to transform time information into spatial information’
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 85
Bunch Shape Monitor - Feschenko monitor
1
1 - Target (wire, screen, laser for H- ) : Source of secondary electrons
2 - Input collimator
3 - RF deflector (100MHz, 10kV) combined with electrostatic lens
4 - Electron Beam detector (electron multiplier, ..)
DT
DX
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 86
Bunch Shape monitor - Feschenko monitor
Longitudinal Bunch profile @ SNS
A. Feschenko et al, Proceedings of LINAC 2004, Lübeck, p408
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 87
RF Deflecting Cavity
eV
z
j < 0
eV0
e
e
-
-
s
s
z
z
s
s
y
y
bc
á
á
D
D
y
y
ñ
ñ
D
D
y
y
»
»
6
6
0
0
°
°
bp
1
Betatron phase advance
(cavity-profile monitor)
Beta function at cavity
and profile monitor
Beam energy
RF deflector
wavelength
Deflecting Voltage
Bunch length
sinΔψ = 1, βp small
Make βc large
Beam profile RF on
Beam profile RF off
P. Emma et al, LCLS note LCLS-TN-00-12, (2000)
Old idea from the 60’s
RF Deflector ~ relativistic streak tube
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 88
CTF3
RF Deflecting Cavity
LOLA @ Flash
Courtesy: M. Nagl
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 89
Calibration of RF Deflector
RF Phase (o)
Beam Position (mm)
Monitor the Beam Position on (or close to) the Profile monitor to calibrate the deflection angle
RF Deflecting Cavity
DX(mm)
Dj(°)
DT(ps)
RF deflector phase
Beam offset on the screen
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 90
RF by Deflecting Cavity
sz=2ps
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 91
LOLA off:
LOLA on:
→ Resolution of 4fs/pixels
RF by Deflecting Cavity
Bunch length measurement @ Flash
M. Hüning et al, Proceeding of the27th FEL conference, Stanford, 2005, pp538
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 92
1
‘The electron energy is modulated by the zero-phasing RF accelerating field and the bunch distribution is deduced from the energy dispersion measured downstream using a spectrometer line’
RF accelerating structures
DT
DE
DX
CAS intermediate level - Trondheim– 2013
T. Lefevre
Notes: Moved to last position

## Slide 93
RF accelerating structures
D. X. Wang et al, Physical Review E57 (1998) 2283
84fs, 45MeV beam but low charge beam
Limitations
RF non linearities
Beam loading and wakefield for high charge beam
RF off
RF on
CEBAF injector, Newport News
T. Lefevre
1st SRF module
2nd SRF module
used for zero-phasing
45MeV spectrometer dipole
Beam profile monitor
CAS intermediate level - Chios– 2011
Notes: fautes

## Slide 94
Laser based techniques
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 95
Sampling Techniques
Sampling
Principle
Longitudinal
Beam profile
Limitation
Laser-beam synchronization jitter (50fs)
Using a short laser pulse to scan through the beam profile
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 96
Laser Wire Scanner : Photo-neutralization
H- beam
High power laser
Scanning
system
H-
Y=/2
Photo-neutralization
H
e-
(b, g)
hn0
Detection system based on
The measurement of released electrons using a magnet and a collector (faraday cup, MCP,..)
Measured the conversion of H- into H with a current monitor
First ionization potential for H- ions is 0.75eV
Photo-neutralization cross section : s ~ 4.10-17 cm2
n!
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 97
Mode Locked Laser Longitudinal Measurements @ SNS
2.5 MeV H-, 402.5 MHz bunching freq, Ti-Sapphire laser phase-locked @ 1/5th bunching frequency
Collected electron signal plotted vs. phase
Measured and predicted bunch length vs. cavity phase setting
Laser Wire Scanner : Photo-neutralization
S. Assadi et al, Proceedings of EPAC 2006, Edinburgh, pp 3161
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 98
n!
Laser Wire Scanner – Compton scattering
e-
hnsc=2 g02 hn0
(bsc, gsc)
hn0
(b0 ,g0)
q  1/g0
Y=/2
Thomson/Compton scattering
e- beam
High power laser
Scanning
system
Detection system based on
The measurement of the scattered photons
The measurement of degraded electrons
0 = 6.65 10-24 cm2
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 99
T. Lefevre
Laser Wire Scanner – Compton scattering
Using a 10TW Ti:Al2O3 laser system. Detecting 5.104 10-40 keV X-rays using either an X-ray CCD and Ge detector.
W.P. Leemans et al, PRL 77 (1996) 4182
ALS @ LBNL
CAS intermediate level - Chios– 2011
Notes: W.P.

## Slide 100
n!
‘Non linear mixing uses beam induced radiation, which is mixed with a short laser pulse in a doubling non linear crystal (BBO,..). The resulting up frequency converted photons are then isolated and measured’
Non linear mixing
M. Zolotorev et al, Proceeding of the PAC 2003, pp.2530
15-30ps electron bunches (ALS, LBNL) scanned by a 50fs Ti:Al2O3 laser
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 101
‘This method is based on the polarization change of a laser beam which passes through a crystal itself polarized by the electrons electric field’
Electro Optic Sampling
n!
e beam
Coulomb field
probing laser pulse
EO crystal
E-field induced birefringence in EO-crystal : Pockels effect
Relative phase shift between polarizations
increases with the beam electric field
CAS intermediate level - Trondheim– 2013
T. Lefevre
Notes: Index of refraction

## Slide 102
Electro Optic Sampling
Delay line
Using 12fs Ti:Al2O3 laser at 800nm and ZnTe crystal 0.5mm thick and a beam of 46MeV, 200pC, 2ps.
X. Yan et al, PRL 85, 3404 (2000)
EOS @ FELIX
CAS intermediate level - Trondheim– 2013
T. Lefevre
Notes: Suppress the wollaston prism

## Slide 103
Electro Optic based bunch length monitors
1. Sampling:
multi-shot method
arbitrary time window possible
2. Chirp laser method, spectral encoding
laser bandwidth limited~ 250fs
Wilke et.al., PRL 88 (2002) 124801
3. Spatial encoding:
imaging limitation ~ 30-50 fs
Cavalieri et. al, PRL 94 (2005) 114801
Jamison et. al, Opt. Lett. 28 (2003) 1710
Van Tilborg et. al, Opt. Lett. 32 (2007) 313
4. Temporal decoding:
laser pulse length limited ~ 30fs
Berden et.al, PRL 93 (2004) 114802
1
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 104
Electro Optic Temporal decoding
Courtesy: S. Jamison et al.
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 105
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
ringing artefacts
Encoding Time resolution
Bandwidth limitation
  Thin crystal (>10mm)
  Consider new materials GaSe, DAST, MBANP ..... or poled organic polymers?
W.A. Gillespie & S. Jamison

## Slide 106
T. Lefevre
“Beam Instrumentation for Linear Collider” - 2nd Ditanet School on Beam diagnostic - Stockholm– 2011
Encoding Time resolution
ZnTe
Spectral limitations of the Crystal
GaP
Phonon resonances
W.A. Gillespie & S. Jamison

## Slide 107
Optical radiation
  Cherenkov / OTR radiation X
  ODR / OSR Radiation X
  Streak camera X 200fs
Coherent radiation : Bunch spectrum
  Interferometry X X
  Polychromator X X
RF techniques
  ‘Feschenko’ monitor X X X Hadron, 20ps
  RF Deflector X X X 10fs
  Zero phasing techniques X X X 10fs
Laser based Method
  Sampling X Jitter (50fs)
    Non linear mixing X
    Thomson/Compton scattering X X Electron
    Photo-neutralization X X H-
    Electro-Optic Sampling X X
  E-O Spectral decoding X X X ~ 200fs
  E-O Spatial decoding X X X ~ 50fs
  E-O Temporal decoding X X X ~ 50fs
s
1
n!
Limitations
Summary
CAS intermediate level - Trondheim– 2013
T. Lefevre

## Slide 108
Now we treat in detail:
- Measurement of nm beam positions
- Measurement of um transverse beam sizes
- Measurement of fs-scale long profiles - Beam synchronization at the fs-scale - Keeping the beams in collision (IP feedback)

## Slide 109: Synchronization of (distant) accelerator components down to the femtosecond
Speed of light:
= 3*10^8 m/s = 0.3 um/ fs
Clock stability
Distribution over length

## Slide 110
Nobel Lecture
Passion for Precision
Theodor W. Hänsch December 8, 2005, at Aula Magna, Stockholm University.
http://nobelprize.org/nobel_prizes/physics/laureates/2005/hansch-lecture.html

## Slide 111: Master Oscillator: Passively Mode-Locked Er-fiber lasers
Ippen et al. Design: Opt. Lett. 18, 1080-1082 (1993)
diode pumped
sub-100 fs to ps pulse duration
1550 nm (telecom) wavelength for fiber-optic component availability
repetition rate 30-100 MHz

## Slide 112: Master Oscillator Timing Jitter
Scaled to 1 GHz
Limited by photo
detection
Theoretical limit ~1 fs
Agilent Signal Analyzer 5052a
f0=1 GHz
Very stable operation
over weeks !

## Slide 113: Why fiber transmission?
Fiber offers THz bandwidth, immunity from electromagnetic interference, immunity from ground loops and very low attenuation
However, the phase and group delay of single-mode glass fiber depend on its environment
  temperature dependence
  acoustical dependence
  dependence on mechanical motion
  dependence on polarization effects
These are corrected by reflecting a signal from the far end of the fiber, compare to a reference, and correct fiber phase length.
Two approaches: CW and pulsed

## Slide 114
Stabilized fiber link
Frequency-offset Optical Interferometry
Technique used at ALMA
64 dishes over 25 km footprint, 37 fsec requirement
Principle: Heterodyning preserves phase relationships
1 degree at optical = 1 degree RF
1 degree at 110 MHz = 0.014 fsec at optical
Gain 105 leverage over RF-based systems in phase sensitivity

## Slide 115: Thermal control of critical components
Peltier Coolers
Baseplate
Some components
Complete
Aluminum Chamber
Insulating Jacket

## Slide 116: Measurement: Bunch arrival monitor (S)
A Sub-50 Femtosecond bunch arrival time monitor system for FLASH; F. Loehl, Kirsten E. Hacker, H. Schlarb (DESY, Hamburg) DIPAC07

## Slide 117
Now we treat in detail:
- Measurement of nm beam positions
- Measurement of um transverse beam sizes
- Measurement of fs-scale long profiles - Beam synchronization at the fs-scale - Keeping the beams in collision (IP feedback)

## Slide 118: Beam Control Stability Issues
Degradation of the luminosity due to IP beam jitter
Sources of IP beam jitter: ground motion, additional local noise (e.g. cooling water)
IP jitter control:
“Cold-RF” based LC (e.g. ILC)
A fast intra-train FB systems at
the IP can in principle recover
> 90% of the nominal luminosity
The linac+BDS elements jitter
tolerance and tolerable ground
motion are not determined from
IP jitter, but from diagnostic
performance and emittance
preservation
“Warm-RF” based LC (e.g. CLIC)
IP beam stability mainly provided from:
- Selection of a site with sufficiently small
ground motion
- Pulse-to-pulse FB systems for orbit
correction in linac and BDS
- Active stabilisation of the FD quadrupoles
In this case a fast intra-train FB system is
thought as an additional line of defence to
recover at least ~ 80% of nominal luminosity
in case of failure of the above stabilisation
subsystems.
A fast FB system can also help to relax the
FD subnanometer position jitter tolerance

## Slide 119: IP-FB Systems
ILC (500 GeV)
Beam time structure:
  Train repetition rate: 5 Hz
  Bunch separation: 369.2 ns
  Train length: 969.15 µs
Intra-train (allows bunch-to-bunch correction)
Digital FB processor (allows FPGA programming)
Large capture range (10s of σ)
IP position intra-train FB system + Angle intra-train FB system (in the FFS)
CLIC (3 TeV)
Beam time structure:
  Train repetition rate: 50 Hz
  Bunch separation: 0.5 ns
  Train length: 0.156 µs
Intra-train (but not bunch-to-bunch)
Analogue FB processor
No angle intra-train FB system due to latency constraints

## Slide 120: Beam-beam deflection curve
Linear approximation in the range [-10, 10] σ*y:
The analysis of the beam deflection angle caused by one beam on the other
is a method to infer the relative beam-beam position offset at the IP
The convergence range is limited by the non-linear response of beam-beam deflection

## Slide 121: Bunch train structure comparison
For CLIC 738 times smaller bunch separation and 6212 times smaller bunch
train length than for ILC !
IP intra-pulse FB is more challenging.
Cold LC
Warm LC

## Slide 122: Analogue FB system Basic scheme
+
PROCESSOR
G
ΔG
Delay
loop
KICKER
BPM
Stripline 1
Stripline 2
Splitter
Σ
Δ α Q Δy
beam
Δy
Amplifier
Attenuator
Kick:
Equipment:
  BPM: to register the orbit of the out-coming beam
  BPM processor: to translate the raw BPM signals into a normalised
  position output
  Kicker driver amplifier: to provide the required output drive signals
  Fast kicker: to give the required correction to the opposite beam

## Slide 123: CLIC IP-FB system latency issues
Comparison of tentative latency times for a possible CLIC IP-FB system with the latency times of FONT3
Irreducible latency:
  Time-of-flight from IP to BPM: tpf
  Time-of-flight from kicker to IP: tkf
Reducible latency:
  BPM signal processing: tp
  Response time of the kicker: tk
  Transport time of the signal BPM-kicker: ts
Study and test of an analogue FB system for ‘warm’ linear colliders: FONT3:
P. Burrows et al. “PERFORMANCE OF THE FONT3 FAST ANALOGUE INTRA-TRAIN BEAM-BASED FEEDBACK SYSTEM AT ATF”, Proc. of PAC05.

## Slide 124: CLIC IR IP-FB BPM and kicker positions
If FONT elements 3 m apart from IP, then beam time-of-flight = 10 ns
The choice of the position of the IP-FB elements is a compromise between:
  Reduction of latency
  Avoiding possible degradation of the BPM response due to particle
  background/backsplash and possible damage of electronics components

## Slide 125: Luminosity performance
Simulation time structure:
Simulation applying a single random seed of GM C
For the simulations we have considered a correction iteration every 30 ns. The systems performs approximately a correction every 60 bunches (5 iterations per train)