## Slide 1: Steering algorithm experience at CTF3
Davide Gamba
davide.gamba@cern.ch
13 December 2013
(Slides from previous presentation at The International Workshop on Future Linear Colliders LCWS13)

## Slide 2: Outlook
CTF3: the CLIC Test Facility at CERN.
Steering necessities.
A general feedback algorithm and its implementation.
  Preliminary results and issues.
Work in progress: new tools.
  Dispersion measurement from Jitter.
  “Jitter free steering.”
Summary.

## Slide 3: CTF3: the CLIC Test Facility at CERN.
Factor 2
Recombination
Drive Beam
Gun
Factor 4
Recombination
Probe Beam
Photo-Injector
Two Beam Test Stand (TBTS)
Dogleg Experiment
Deceleration Test Beam Line (TBL)
Photo Injector Tests
XBOX
experiment
CR
84 [m]
DL
42 [m]
Building 2001
Building 2013
Building 2010
Building 2003
CLEX area

## Slide 4
  Steering necessities

## Slide 5: Steering necessities.
For machine operation and optimization we need a general tool to control the orbit of the beam.
It has to deal with some intrinsic limitations
  Data acquisition is affected by noise
    White noise
    Not null dispersion and energy jitter
  Non responsive control system
    Delicate Front-Ends
  Instable beam (mainly coming from RF instabilities)
  Beam position may not be a well defined measurement in case of losses
  Challenging machine
    MADX model not always accurate
    Aperture limitations
Algorithm to measure the response matrix needed
  Has to be “fast” compared to machine faults and drifts
  Has to be able to follow slow drifts of the machine

## Slide 6: Steering necessities.
Special case: during recombination, different section of the initial train take different paths.
Only one section over two is delayed into the Delay Loop
They don’t necessarily come back on the same trajectory.
Initially we only have a long train “divided” into 8 sections, each 140 ns long
Projected emittance blow-up.
Increased losses.
In the Combiner Ring all the 8 sections can end up in having different orbits

## Slide 7: Steering necessities.
First stage: match orbits of delayed and not-delayed trains.
Use correctors in Delay Loop
Force the same orbit in the next Transfer Line (TL1)
In principle only two correctors with the right phase advance are needed.
  Aperture limitations may impose to use more correctors.

## Slide 8
  The feedback algorithm

## Slide 9: The algorithm
Solving a linear system of equations

## Slide 10: The algorithm
SVD
Synchronization

## Slide 11: The algorithm
Measure the response matrix based on a simple concept:
  Randomly excite all the correctors
  Read the Beam Position at all the interested points
  Invert the same linear system of equations, but the Response Matrix is now the unknown:
  Keep a history of last setting/observations pairs of variable length
  Also during beam corrections outcome data can be used to improve Response Matrix.

## Slide 12
N correctors = 8
N BPMs = 12
correctors excitation σ = 1[A]
correctors noise σ = 0.01[A]
BPMs noise σ = 0.1[mm]
dispersion induced jitter σ = 1 [mm]
number of iterations: 100
history size: n = 30.
Real response matrix
Computed response matrix
Computed – Real
Testing the response matrix measurement algorithm

## Slide 13: The algorithm: implementation and test
Developed a Matlab application for generic linear feedbacks.

## Slide 14: The algorithm: implementation and test
Example of correction of beginning orbit of the linac.

## Slide 15: The algorithm: implementation and test
Example of use to control end of linac orbit:

## Slide 16: The algorithm: implementation and test
Example of use to control end of linac orbit:

## Slide 17: The algorithm: implementation and test
Example of use to control end of linac orbit:

## Slide 18: The algorithm: implementation and test
Example of use to control end of linac orbit:

## Slide 19: Preliminary results
Back to the main goal:
  use the tool to match “delayed” and “straight” orbits in TL1.
Use correctors in Delay Loop
Force the same orbit in the next Transfer Line (TL1)

## Slide 20: Preliminary results
“Orbit matching” in TL1

## Slide 21: Preliminary results
A first issue: straight and delayed beam have different energy
From a rough estimation, this offset is related to a
  Δp/p = -0.03 of the delayed beam.
Note: the injector was not properly optimized. These results were not obtained in normal condition of operation.

## Slide 22
  Work in progress

## Slide 23: Interlude: beam jitter induced by energy jitter
We are affected by a natural jitter of the energy.
Beam energy along the pulse is also not always flat.
Thanks to generality of our feedback tool we can use it to shape the RF power of last linac structure to try to compensate the second effect.
After summer shutdown: looking at energy jitter markup in beam position in dispersive region.
Note: 3Ghz beam for factor 4 recombination,
i.e. different setup respect to previous slide!

## Slide 24: Dispersion measurement from Jitter
Developed an application to passively measure dispersion by beam jitter.

## Slide 25: Jitter free steering
The first area where we have dispersion is at the end of Drive Beam linac, where a chicane is installed.
Nominally dispersion free
Nominally
non zero dispersion

## Slide 26: Jitter free steering
Using the same feedback application and measuring dispersion as jitter.
Change correctors inside chicane to reduce jitter (i.e. dispersion) downstream.
Acquiring 30 beam pulses for each iteration.
Main disadvantage: RM measurement and correction takes longer time.
Preliminary results!

## Slide 27: New ideas
Other ideas to get read of energy jitter to measure Response Matrices?
Even better: use it in a different way to get Dispersion Response Matrix.
Can we guess the beam main characteristics ( x0 ; x0’ ; Δp/p ) only looking at the orbit of the beam in few BPMs upstream, and predict the orbit downstream?
What if in the mean time a corrector is changed (and so the dispersion)?
Use as indipendent variables the BPMs readings in TL1
In the mean time randomly excite downstream correctors
(also indipendent variables)
Measure response matrix downstream
In a system like this, at first order, beam position in a downstream BPM seems to linearly depend on:
x0 ; x’0 ; Δp/p ;
(Δp/p x0) ; (Δp/p x’0) ;
IC1 ; (Δp/p IC1) ; … ; ICN ; (Δp/p ICN)
We don’t have any of this information, but they may be expressed in terms of upstream beam positions.

## Slide 28: New ideas

## Slide 29: New ideas
If we suppose that within two shots we only change correctors and energy.
… Work in progress to verify this is correct …
Δ(Δp/p) can be measured from the jitter on a BPM.

## Slide 30: Summary
What has been done:
  Developed and tested a generic linear feedback.
  Smart way to measure the response matrix: it can work in quasi-parasitic mode and/or during orbit correction.
  First results and characterization of possible limitations.
What is ongoing:
  Dispersion measurements from jitter.
  “Jitter free” steering.
  Comparison of the response matrix with machine model (MADX).
    e.g.: found a corrector with inverted polarity.
    Model optimization using LOCO procedures.
What is next:
  Demonstrate the possibility to match the two orbits in TL1 within noise level.
  Apply the feedback for the full closure of CR.
  Measure the improvement in beam emittance and power production stability.

## Slide 31
  Thank you.

## Slide 32
  Appendix slides

## Slide 33: Measured Linac RM with errors (Appendix)

## Slide 34: DL layout (Appendix)

## Slide 35: TL1 layout (Appendix)

## Slide 36: DL -> Tl1 Response Matrix (Appendix)
MADX and Measured RM

## Slide 37: DL -> Tl1 Response Matrix (Appendix)
MADX and Measured RM

## Slide 38: DL -> Tl1 Response Matrix (Appendix)
MADX and Measured RM

## Slide 39
MADX and Measured RM
DL -> Tl1 Response Matrix (Appendix)

## Slide 40: DL -> Tl1 Response Matrix (Appendix)
MADX and Measured RM

## Slide 41: DL -> Tl1 Response Matrix (Appendix)
MADX and Measured RM

## Slide 42: DL -> Tl1 Response Matrix (Appendix)
MADX and Measured RM

## Slide 43: DL -> Tl1 Response Matrix (Appendix)
MADX and Measured RM