## Slide 1: TL2 Optics Measurements FONT Meeting 20th Dec 2012
Jack Roberts

## Slide 2: Overview
Changes to the TL2 lattice.
Nominal optics from MADX matching.
Nominal optics in the machine.
Kick measurements

## Slide 3: Where/What is TL2?
TL2

## Slide 4: Old TL2 Lattice
DHF/DVF 0175
DHD/DVD 0125
DHF/DVF 0225
DHF/DVF 0253
DHF/DVF 0345
DHF/DVF 0435
DHF/DVF 0525
DHF/DVF 0615
DHF/DVF 0655
DHF/DVF 0765
DHF/DVF 0855
CORRECTORS

## Slide 5: New TL2 Lattice
DHF/DVF 0175
DHD/DVD 0125
DHF/DVF 0225
DHF/DVF 0265
DHF/DVF 0345
DHF/DVF 0465
DHF/DVF 0525
DHF/DVF 0615
DHF/DVF 0655
DHF/DVF 0765
DHF/DVF 0855
CORRECTORS

## Slide 6: TL2 Ideal Nominal Optics
Dispersion closed
Dxy < 1.2m
Betas < 80m but >0.5m
Alphas < 20m
Low betas (<15m) in long (7m) drift in girder 2.
R56 = 0.0, +0.2, -0.2 through horizontal dog leg.
These constraints are relaxed for the phase feedforward optics to obtain larger R52 etc.
MADX matching…

## Slide 7: Matched Nominal Optics: Start to Vertical Chicane Exit

## Slide 8: Matched Nominal Optics: Start to Vertical Chicane Exit

## Slide 9: Matched Nominal Optics: Start to Vertical Chicane Exit

## Slide 10: Matched Nominal Optics: Horizontal Dog Leg

## Slide 11: Matched Nominal Optics: Horizontal Dog Leg

## Slide 12: Matched Nominal Optics: Horizontal Dog Leg

## Slide 13: Matched Nominal Optics: Horizontal Dog Leg

## Slide 14: Matched Optics in the Machine
Lose all the beam by the end of TL2…

## Slide 15: Full Transmission Through TL2
Magnet | Model | Machine | Difference
cc.qfh0210 | 41.02 | 40.99 | 0%
cc.qdh0220 | 39.71 | 39.68 | 0%
cc.qfh0230 | 15.20 | 15.18 | 0%
cc.qfl0270 | 14.12 | 13.61 | -4%
cc.qdl0280 | 22.38 | 21.36 | -5%
cc.qdl0330 | 24.48 | 23.45 | -4%
cc.qfh0350 | 40.14 | 40.10 | 0%
cc.qdl0370 | 24.47 | 23.45 | -4%
cc.qdl0430 | 16.13 | 18.11 | 12%
cc.qfl0450 | 18.83 | 19.82 | 5%
cc.qdh0490 | 23.11 | 27.09 | 17%
cc.qfl0530 | 24.42 | 24.09 | -1%
cc.qdl0550 | 9.28 | 9.27 | 0%
cc.qfl0570 | 9.12 | 9.11 | 0%
cc.qfl0620 | 10.10 | 10.09 | 0%
cc.qdl0650 | 12.47 | 11.46 | -8%
cc.qfl0680 | 5.51 | 5.51 | 0%
cc.qfl0730 | 5.85 | 5.85 | 0%
cc.qdl0750 | 10.89 | 10.88 | 0%
cc.qdh0790 | -47.35 | -47.32 | 0%
cc.qdd0820 | 36.15 | 46.10 | 28%
cc.qfd0840 | 35.29 | 49.98 | 42%
cc.qfl0910 | -11.13 | -11.70 | 5%
cc.qdl0920 | -12.24 | -14.23 | 16%
One of the girder 4 quads (430/450/490) was found to have incorrect polarity. Cables were swapped back to correct it.
Tweaks made to quad currents to get full transmission (left).
Quad scan measurements still showed large emittance blow up in TL2.
Kick measurements to identify location and magnitude of errors in the machine/model.

## Slide 16: Kick Measurements
Use the correctors to kick the beam (horizontal and vertical with different amplitudes).
Record the beam position in the BPMs as a result of the kick.
Compare the measured kicked orbit to the MADX model.
Identify where the discrepancies are and try to fix them.

## Slide 17: Example: Corrector 265, Horizontal

## Slide 18: Example: Corrector 265, Vertical

## Slide 19: Possible Errors
Dipole focusing: vertical edge focusing and horizontal focusing.
L type quadrupole strength.
Quadrupole polarity.
Corrector scaling.
BPM scaling.
Try to correct by hand or with MADX matching using measurements as constraints.

## Slide 20: Data Sets
All quads on.
Girder 5,6,7,8 quads off (bend 600/700 focusing).
Girder 4,5,6,7,8 quads off (bend 500/800 focusing).
Girder 2,3,4 quads off (bend 300/400 focusing).
Only 1 quad on in horizontal dog leg (quad strength/polarity).

## Slide 21: Girder 5,6,7,8 Quads Off – Corrector 525 Horizontal
LOSSES

## Slide 22: Girder 5,6,7,8 Quads Off – Corrector 525 Vertical
LOSSES

## Slide 23: 600 and 700 Bend Focusing Matching
With the girder 5,6,7,8 quads off data with multiple correctors the following parameters were matched in MADX:
  Global corrector scaling (kick strength): 0.68
  Bend 600/700 pole face rotation angle (rbend/sbend): 0.62*(bendAngle/2).
  Bend 600/700 FINT (vertical edge focusing) = 1.28
  Bend 600/700 HGAP (vertical edge focusing) = 0.005 m.

## Slide 24: Girder 5,6,7,8 Quads Off – Corrector 525 Horizontal AFTER MATCHING
LOSSES

## Slide 25: Girder 5,6,7,8 Quads Off – Corrector 525 Vertical AFTER MATCHING
LOSSES

## Slide 26: Girder 5,6,7,8 Quads Off – Corrector 615 Horizontal AFTER MATCHING
LOSSES

## Slide 27: Girder 5,6,7,8 Quads Off – Corrector 615 Vertical AFTER MATCHING
LOSSES

## Slide 28: BPM/Kicker Scaling
With the quads off the section from corrector 615, through BPM 645 and BPM 685 is a drift (no bends, no quads).
Assuming model positions are correct, can use this to find the correct BPM and kicker scaling.
DHF0615
BPI0645
BPI0685

## Slide 29: Vertical Corrector/BPM Scaling
SCALED
ORIGINAL
Corrector 615 scaling: 0.89 +/- 0.08
BPM 645 scaling: 1.05 +/- 0.09
BPM 685 scaling: 1.02 +/- 0.03

## Slide 30: Horizontal Corrector/BPM Scaling
BPM 645 scaling: 0.77 +/- 0.09
BPM 685 scaling: 0.97 +/- 0.07
ORIGINAL
BPMs SCALED

## Slide 31: Summary
Quadrupoles, correctors and BPMs moved in TL2 to accommodate phase feedforward kickers.
New nominal optics derived from MADX matching.
Matched MADX values need a lot of tweaking to get full transmission in the machine.
Kick measurements to identify errors in the machine/model are ongoing and far from conclusive so far.