## Slide 1
Timepix-3 test as gaseous (GridPix) detector
Naked TimePix-3 chip
Framed Micromegas on top
Sealed with framed cathode foil at 8 mm distance from chip
Timepix-3 test
All-ceramic InGrid
The focusing TPC

## Slide 2
Today, Dec 11, 2013, a gaseous detector formed by a TimePix-3 chip and
a Micromegas became operational. Below, you find pictures of the ‘open’
chamber, showing the framed Micromegas, pressed on the TPX-3 chip by two strings.
The chamber is sealed by a framed gas foil, also acting as (drift) cathode. Drift gap: 8 mm
The chamber unit is read out by a Spidre prototype.
Two events are shown, clearly indicating the drift time, coded by the color
of the hit pixel.
Micromegas: 50 μm pillars, square pitch of holes: 60 μm
Pixel Chip: Timepix-3, first batch, read out by Spidre prototype
No protection layer: Micromegas-on-naked-chip.
Gas: He/ibutane 95/5
Source: 90Sr
HVgrid: 340 V
HVcathode: 700 V
Nikhef Detector R&D group: Niels, Jan, Martin, Fred, Harry
+ Joop, Bas, Vladimir, Francesco, Ruud, Wim, Henk

## Slide 6
Analysis: Els Koffeman and Stergios Tsi.
Strong non-homogeneous drift field: 2nd order fit
Time coding not yet fully settled
[Time (arrival) measurement OK confirmed by Xavii (Seoul IEEE Oct 2013)

## Slide 7
So far: Timepix-3 works as expected (not aware of any problem)
Prototype Spidre works (firmware!)
DAQ works
Data represents something good
Yet much work to do on software

## Slide 8: The all-ceramic InGrid
Why?
Double Discharge protection (like Resistive Plate Chambers)
Equal coefficient of thermal expansion throughout InGrid: needed
for operating in cryogenic environments
Plastics (like SU8) outgas. These materials can never be used
in ultra clean (cryogenic) environments

## Slide 11
Thick layers of SiO2 (50 μm) made by Victor Blanco Carballo @ MESA+
New way to make thick layers: changedirection of growth by 90 deg.

## Slide 14
Octopuce: multi-chip array. Attempt to minimize dead regions
- very hard to exchange broken chips (and we will have broken chips)
- uncontrolled distortion of drift field
The Focusing TPC

## Slide 15
Focus drift field by means of guard electrode to:
have control over the non-homogeneous) drift field
avoid dead regions

## Slide 16
Strong focusing
cover only 25 of fiducial surface with active pixel chip
  saves $$
  saves power, thus cooling, thus radiation length
But:
larger effective pixel pitch (256 x 256 pixels @ 55 μm x 55 μm)
110 μm x 110 μm Moore’sLaw: smaller pixels in future
region of amplified diffusion
in B-field: E x B effect: amplified (coupled) diffusion

## Slide 17
work:
pcb
focusing electrode
cooling (ReLaXd)

## Slide 18: ReNext: ReLaXd for gaseous detectors
Quad timepix carrier board for gaseous detectors
Provides gas enclosure
Relaxd readout board as mezzanine

## Slide 19
Focusing drifter for Quad TimePix on ReNexd

## Slide 20
Extract copper pattern for 3D field calculations

## Slide 21
Flat Cable with 16 leads: external potential settings

## Slide 25
Autocalibration
get initial f(X,Y) (X’,Y’) from 3D e-field
make scatter plots of residials
modify f(X,Y) until residuals are minimized
Basic correction: X’ = C X, Y’ = C Y
+ E x B effect

## Slide 26
Performance
requires knowledge of local vectors E, B
effective pixel size related to electron diffusion
E x B effect, although correctable, may worsen resolution
Plans
Quad Focus Drifter under construction (finished)
2x Sci 30 mm x 40 mm to be constructed
Chamber support + rotator (around Z axis) ready
HV distribution box (16 channels!) ready
Testbeam @ DESY in Oct 2013
  Data analysis, Monte Carlo simulation, correction procedure
Collaboration with Bonn

## Slide 27
Q64: an assembly of 16 Quads
Number of chips is not a variable