## Slide 1: Summary of the Calorimeter/Muon Session
José Repond
Argonne National Laboratory
Americas Workshop on Linear Colliders
Fermilab, Batavia, IL, U.S.A.
May 12 – 16, 2014

## Slide 2
Activities in the Calorimeter/Muon Session
 | Calorimeter | Talks
Imaging calorimeters | ECAL | 3
 | HCAL | 5
 | FCAL | 1
Dual readout | Fibers | 1
 | Fibers+ glass | 1
Muon system |  | 0
Total |  | 11
Development
of systems specifically
for the LC
Generic
calorimeter R&D

## Slide 3
Status of Imaging Calorimetry
 | Project | Prototypes | At this conference
ECAL | CALICE Si-W | Built and tested | Towards scalable prototypes
 | CALICE Scin-W | Built and tested | 
 | SiD Si-W | 9 layers built and first tests | 
HCAL | Scintillator | Built and tested | GEANT4 comparisons + scalable prototype
 | RPCs (DHCAL) | Built and tested | Calibration
 | RPCs (SDHCAL) | Built and tested | 
 | Micromegas | 4 layers built and tested | 
 | GEMs | Smaller prototypes | 
FCAL |  | R&D on components | Physics with the FCAL
Proof of principle

## Slide 4
Comments to the ECALs
Performance of the CALICE Scintillator – W ECAL
Scintillator strips 45 x 5 x 1 mm3
Strip Splitting Algorithm SSA to achieve smaller effective segmentation
Similar performance to Si-W with 5 x 5 mm2 pads
B) Progress with the CALICE Si – W scalable prototype
Embedded front-end electronics
Front-end ASIC embedded into readout board
Beam tests of several layers
Progress with the SiD Si – W ECAL
First beam tests successful
Identification of a number of issues
(crosstalk , monster events…)
Katsu Coterra
Taikan Suehara
Marty Breidenbach

## Slide 5
Comments to the HCALs
Calibration of the Fe-DHCAL and the W-DHCAL
Equalization of the response of individual RPCs
Turned out to be very challenging (depends on particle type, density of hits!)
Procedure now complete with 3 different schemes (differences at high energies)
        Progress with the Scintillator HCAL
WLS-fiber less tiles
Embedded electronics
Several layers tested in test beams
Scalable to large detector
Comparison with GEANT4 (Scintillator HCAL)
Measurements of shower shapes
Parameterization of shapes
Important information for simulation of hadronic showers
e.g. Indication of overestimation of π0 production in first
inelastic interaction (important feedback to GEANT4!)
40 GeV μ
f… Fraction
of ‘short’
longitudinal
component
Burak Bilki and
Christian Grefe
Huong Lan Tran and
Katja Krüger
Marina Chadeeva and Felix Sefkow

## Slide 6
Dual Readout Calorimetry
Goal
Optimization of the hadronic energy resolution through the measurement
of both Scintillator and Čerenkov light
Underlining assumption
Scintillator light produced by all charged particles depositing energy in the calorimeter
Čerenkov light only produced by relativistic particles (i.e. mostly electrons and positrons)
Use of Scintillator/Čerenkov information
Either: determine the ‘electromagnetic fraction fem’ of hadronic showers and apply
appropriate weights
Or: exploit correlation in signals to improve resolution

## Slide 7
(SUPER)DREAM
Clear fibers → Čerenkov light
Scintillating fibers → Scintillation light
All embedded in a metal absorber (Pb, Cu, W)
→Results from an (almost complete) prototype
TOTAL ABSORPTION
2 → 20 cm3 sized Crystals with 2 sensors
→ Simulation studies
ADRIANO
Glass as absorber → Čerenkov light
Scintillating fibers → Scintillation light
→ Simulation studies
→ Small scale R&D on glasses etc.
3 DR Projects
John Hauptman
Corrado Gatto
Alexander Conway

## Slide 8
SUPERDREAM
Constructed large prototype
11 modules (Cu and Pb-absorber)
Several metric tons
Tested
CERN SPS test beam in 2012
Electron response at 80 GeV
Simple sum of S and Č signals
(not dual readout algorithm)
Corresponds to 17.7%/√E
(comparable to ZEUS)
John Hauptman

## Slide 9
SUPERDREAM’s Hadronic Response
Corresponds to 60 - 70%/√E
(factor of 2 worse than ZEUS)
Dual readout reconstruction
→ and it is not due to leakage!
John Hauptman

## Slide 11
Thank you for your attention