## Slide 1
ILC Machine Status and
Energy Staging Scenarios
Helmholtz Alliance Linear Collider Forum
Bonn, April 29, 2014
Benno List, DESY
Higgs & Co
Powered by
250 GeV
…you gotta have Mass!
© Nick Walker

## Slide 2: Outline of for this talk
The proposed site in Kitakami
Plans for the pre-construction phase, current activities
Fixing the Interaction Point location: horizontal vs. vertical access to experimental hall
Fixing the length: energy and gradient
Scenario for a 250GeV first stage
Outlook

## Slide 3: The Kitakami Site
T. Sanuki

## Slide 4: Kitakami Site
T. Sanuki

## Slide 5: Geology and Topography
T. Sanuki

## Slide 6: Perspective View
T. Sanuki

## Slide 7: Candidates for the Interaction Point location

## Slide 8: Current / Recent Activities
April 8-10: Workshop in Tokyo between CFS (Conventional Facilities & Siting) and ADI (Accelerator Design & Integration) groups
Agenda: https://agenda.linearcollider.org/conferenceDisplay.py?confId=6342
Focus: Pre-construction plan for the Kitakami site
24 participants, 50/50 international/Japan

## Slide 9
We are here, but need more funds in Japan
M. Miyahara

## Slide 11: Options studied
Y. Nisimoto, J-Power
Access scheme (horizontal or vertical) determines location

## Slide 12: (My personal) summary of the situation in Japan
Japan is really serious about the ILC, but nothing is decided yet
Planning resources very limited till FY 2015 (April 2015)
Pre-construction phase is 5 years – construction could start 2019/20
Detailed investigations (geology and environmental impact) have to start as soon as money is available
This requires decisions on
  Location of IP / experimental hall
  Total length of accelerator
  by the end of this year

## Slide 13
Staging
All the world’s a stage, and we are merely players in it…

## Slide 14: A Remark
A common misconception from the circular collider days: Even a little more energy costs a lot of money and watts, and reduces performance (lumi, beam lifetime, availability)
This is not true for a linear collider!
At a linear collider: a little more energy costs a little more money and a little more watts, at equal or improved performance (lumi goes up with E_beam)
For a helical undulator source: Around its design threshold energy, higher (“drive” beam) energy drastically improves performance (more production margin)
This means: The best operating energy for a Linear Higgs Factory is not necessarily “as close to threshold as possible”, in contrast to a circular machine! -> 270GeV may be easier than 235GeV
And: a 250GeV machine neither saves a huge fraction of money, nor does it produce a lot of luminosity easily! It is not a “Higgs factory”

## Slide 15: Motivation for a 250GeV 1st Stage
Higgs discovery triggered interest in ILC as Higgs-Factory
Higgs Production maximal around 235 GeV
Save initial cost and time by starting at ~250 GeV
This was proposed by JAHEP in Oct 2012
Questions:
What is the expected performance at 250?
How much money and time can one save?
Needs an Answer to this Question:
What is the “first stage” exactly?

## Slide 16
Slide: Toshi Mori, at LCWS 12, Arlington, TX
JAHEP statements: http://www.jahep.org/office/doc/201202_hecsubc_report.pdf update: http://www.jahep.org/office/ doc/201210_ILC_staging_e.pdf

## Slide 17: Scope: What is the first stage exactly?
Report has to make some basic assumptions
based on JAHEP Statement:
Running at 250GeV for Higgs production (“Higgs factory”)
Machine shall be upgraded to ~500GeV -> Build tunnel for full (500GeV) machine right away
Machine shall be extensible to 1TeV -> Keep the full-scale BDS
The report considers a 250GeV first stage of the TDR baseline design for 500GeV, with the footprint of the full 500GeV configuration.
It is assumed that machine runs at ~1+4 years at 250GeV, then is upgraded to 500GeV in a single step, taking ~1 year.
A big cliff avoided!
Does this make sense?

## Slide 18: Basic Configuration

## Slide 19: Report to the LCC Directorate
https://ilc-edmsdirect.desy.de/ilc-edmsdirect/file.jsp?edmsid=D00000001046475&fileClass=native
Presented recently to directorate
Discusses technical issues of possible staging scenarios – neither physics not political pros and cons are considered

## Slide 20: Performance (Luminosity) Estimate
Peak lumi: ℒ=0.75E34cm-2s-1 -> assumed to be the same as for full linac at 250GeV in baseline design
Assume 4 year ramp-up of luminosity (plus year 0): 10%, 30%, 60%, 100% -> Σyears 1-3 = 1 full year
Assume 8 months running @ 75% availability per year -> 1.6E7 seconds per year
4 years result in 240fb-1
Consistent with “rule of thump”: first 4 years give 250fb-1 at 250GeV, 350 at 350, 500 at 500…
But note: after commissioning, one gets these data sets every 2 years!
240fb-1
50fb-1

## Slide 21: Scope: Questions to the Parameters Group
A fuller analysis, and a realistic design, require input from the parameters group.
What is the real energy for the full machine? 500? 550? 600?
How much integrated luminosity is needed at 250GeV?
How fast should one upgrade the energy? 3 years? 4?
What is the next energy step? 350? 500?
What is the first upgrade? Energy or luminosity (at 250 GeV)?
-> Report from Parameter’s Group tomorrow morning by Jenny

## Slide 22
MAIN LINAC

## Slide 23: Main Linac Configuration
3 cryomodules form “1 Main Linac Unit” (38m long, 26 cavities, 1 quad)
2 klystrons power 3 ML units (9 cryomodules)
3 ML units supplied by one cold box -> 1 “Short Cryo String” (116m, 9cryomodules, 3 quads, 2.54GeV)
Short cryo strings are basic unit

## Slide 24
Schematic Main Linac Tunnel Layout
Electron flight direction
Bunch Compressor
Positron
Source
Undulators
Main Linac Cryomodules
Cryo Plants
PM-8
PM-10
PM-12
Access Halls

## Slide 25
Scenario A: Fill from upstream
Scenario B: Fill from downstream
Scenario C: Fill from Shafts
Basic Choices

## Slide 26: Beam Dynamics: Emittance Growth
Baseline: γεy =20nm (DR exit) -> 35nm (IP) ML adds 5nm
Emittance growth scales as 1/γ
-> accelerate beam asap
Disfavours scenario B (increases emittance by 5nm to 40nm at IP, 6% luminosity reduction)
Above 40 GeV (2km), growth is moderate
Scenarios A and C look OK

## Slide 27
Scenario A: Fill from upstream
Optimal for beam dynamics
Scenario B: Fill from downstream
Worst for beam dynamics
Scenario C: Fill from Shafts
OK for beam dynamics
Beam Dynamics

## Slide 28
Scenario A: Fill from upstream
Optimal for beam dynamics
Helium transfer line needed
No spare cryo capacity at PM12
Scenario B: Fill from downstream
Worst for beam dynamics
Helium transfer line needed
No spare cryo capacity at PM8
Scenario C: Fill from Shafts
OK for beam dynamics
No helium transfer line
Spare cryo capacities
Cryogenic Spare Capacity

## Slide 29: Cryogenic Plants
Scenarios A and C have each 2x2 cryoplants that are not needed for first stage
Will installation of these plants be staged?
  2 plants per shaft have operational advantages:
    faster cooldown
    Redundancy (during maintenance work)
    -> Risk reduction
  In scenario C, spare cryo power can be distributed over full Main Linac
    makes accelerator operation easier (more operational margin)
    Could be used to increase current / luminosity
    Is that technically feasible? Cryoplant issues, Cryomodule specifications! -> needs study
  Acquisition of plants at 500GeV upgrade would save some initial cost
  What would be schedule impact if 2x2 plants are installed during upgrade work in addition to cryomodule installation?

## Slide 30
Scenario A: Fill from upstream
Optimal for beam dynamics
Helium transfer line needed
No spare cryo capacity at PM12
Scenario B: Fill from downstream
Worst for beam dynamics
Helium transfer line needed
No spare cryo capacity at PM8
Scenario C: Fill from Shafts
OK for beam dynamics
No helium transfer line
Spare cryo capacities
Initial Installation

## Slide 31: Installation
Installation has not been not thoroughly investigated yet
Material (cryomodules) has to run through access tunnels
TDR install rate: 1600 CM / 1 year / 6 access shafts - ~ 1 CM / (day*shaft) -> not trivial
Installation would get easier (or faster) in staged scenario if still 6 shafts are used, but for reduced number of cryomodules
Same applies to upgrade to 500GeV
Assumption: Best to install cryomodules such that a free path to access shafts is left (start at center between shafts, work towards shafts)

## Slide 32: Baseline Configuration

## Slide 33: Scenario C: Hybrid
Scenario C: Fill from Shafts
PM±12: 1 full cryoplants
PM±10: 1 full cryoplant
PM±8: 1 ML cryoplant at 62/60%
Installation of all cryoplants allows running at 10Hz rep rate
This is the preferred scenario which will be used as basis for future work, in particular lattice design

## Slide 34: Cryomodule Production Schedule / Logistics
Energy staging changes schedule: Need 877cryomodules for 250 GeV, (500GeV baseline: 1841)
Production rate: 2/day x 3.5 years -> 1/day x 7 years
Cavities & cryomodules account for ~1/3 of the ILC cost -> cannot afford to make them more expensive!
Experience from industry: reducing production quantity by factor 2 increases the price per item by 5-10% (learning curve)!
Ordering only half of the cavities and cryomodules would increase the overall project cost (for 500GeV) by several % (several 100M$)!
If cryomodule production is not stopped, cryomodules are available <3.5 years after end of installation (“year 0” + 2.5 years)

## Slide 35: Energy Overhead and Gradient
At 31.5MV/m gradient, all cryomodules online: e- beam reaches 129.3 GeV, 1% above (125+3.1)GeV needed e+ beam reaches 126.8 GeV, 1.5% above 125GeV
TDR baseline has 1.5% overhead to account for component failures
125GeV is close to
  Physics threshold
  Operation threshold for positron source
-> falling 10% below design gradient would have very serious impact
Define additional safety margin to reduce risk
Re-evaluate assumed gradient? (is final gradient available from year 1 on?)

## Slide 36
POSITRON SOURCE

## Slide 37: Positron Source Overview
Positrons are produced from electron beam via helical undulator radiation -> requires minimum electron energy of 150GeV
Below 150 GeV, operation becomes difficult

## Slide 38: Positron Production
e- linac
Uses primary electron beam to generate ~30 MeV photons in a SC helical undulator
Photons converted into e+e- pairs in “thin” titanium target
Positron production yield dependent on e- beam energy (and therefore Ecm)
e- to IP

## Slide 39: Positron Source: Operation at low energies
Baseline Positron Source: Requires 150GeV beam (300GeV CME)
TDR assumes “10Hz scheme” for CME below 250GeV: alternate electron beam for physics (< 125GeV) with 150GeV beam for positron production
10Hz scheme uses excess cryo power available when running a 250GeV accelerator at 125/150 GeV (half gradient)
=> 10Hz scheme at a staged machine requires
  Running electron Main Linac at full gradient at 10Hz
  -> needs doubling of cryogenic power
  Needs also 25GeV additional beam energy for e- linac
Also: 10Hz mode is challenging for machine operation, and requires more power -> not attractive

## Slide 40: Positron Source: Yield
Required: yield 1.5e+ per 1e-, i.e. 50% operational margin
Yield drops to ~1 at 125GeV -> could run, but no margin
TDR baseline: 147m long undulator, 231m available space
Could install more undulator modules (43->66) in available space
Would permit operation at 250GeV without need for 10Hz scheme
Energies below 250GeV still challenging -> is this needed?

## Slide 41: Positron Source: Summary
Proposal: Increase undulator length to 231m
Does not change footprint of machine compared to TDR
Allows “regular” operation with 125GeV electron beam
Increases cryo power needed for undulators
Operation below 200-250 GeV requires alternating beams for physics and e+ production (“10Hz scheme”), at full ML gradient
needs doubled cryogenic power in ML, or reduced pulse frequency -> reduce luminosity by factor 2
An additional, electron-driven source would be most valuable in this first stage: risk reduction, easier operation

## Slide 42: Baseline Schedule

## Slide 43: Study for Staged Schedule (M. Gastaal, CERN)
Expected shortening of construction period: ~9 months
May put detectors on critical path!

## Slide 44: Major systems costs
~50%
x 0.47
- 23%

## Slide 45: Spending Profile
Reduce cryomodule and HLRF spending rate
Extend spending by 4 years
Peak spending rate drops by 200MILCU/year (16%)
Increase of overall budget due to transfer line and larger undulator ~1.1%

## Slide 46: Conclusions
Staging scenario considered:
  full tunnel for 500GeV machine, full BDS for 1TeV operation
  53% cryomodules in ML for 1st stage
  Extended undulator for positron production at 250GeV
  Running at 250GeV for ~5 years gives 250fb-1, but more cryomodules may be ready after 3years, i.e. ~50fb-1!
  Then upgrade in one step to 500GeV, about 1 year shutdown
  Cryomodule production is never stopped
Physics requirements (exact energy, integrated luminosity) needed from parameters group
Design decisions: ML configuration, cryoplant staging?
Revised / refined production and installation schedule needed for CFS requirements: storage/staging areas, transport capacities
Cryomodule production plan has large impact

## Slide 47: Staging: My personal summary
Drive for a initial 250GeV stage is more political than accelerator driven (which makes the 250GeV stage more likely…)
A 250GeV stage reduces peak funding profile, and reduces necessary cryomodule production capacity: risk reduction
But it drags out cryomodule production time: companies may go out of business, labs may change priorities -> increased risk
Stopping cryomodule production after 250GeV will make a 500GeV machine much more expensive, and less likely (and indicates lack of commitment to go for 500GeV?)
Continuing cryomodule production means that after ~2 years of data taking (50fb-1) an upgrade is possible
Is a dataset with 50fb-1 at 250GeV useful?

## Slide 48: Summary
The most pressing questions for the Japanese site:
  Where is the IP? Needs decision on access tunnel scheme
  How long is the accelerator? Needs decision on maximum energy, assumed gradient and overhead -> discussion initiated by Physics&Detectors Deputy Director (H. Yamamoto) -> Parameter’s group -> be careful not to look the gift horse into its mouth…
  Answers needed by end of 2014 -> ALWC in May at Fermilab is time for arguments, ECFA WS in Belgrade might see the result
Japan needs 5 years pre-construction, plus 10 years construction -> have the 5 years already started? Not clear
A 250GeV first stage is likely, but it is unclear how long it will last

## Slide 49
BACKUP

## Slide 50: Towards a design for a staged machine
A design for a staged machine entails:
Top-level parameters for the envisaged stages (Ecm, L, …)
Cost estimate for the initial stage and upgrade costs
Schedule for initial stage and upgrade
This requires a lattice for the staged machine
What are the questions to be answered before the lattice can be designed?

## Slide 51
Scenario A: Fill from upstream
Optimal for beam dynamics
Helium transfer line needed
Scenario B: Fill from downstream
Worst for beam dynamics
Helium transfer line needed
Scenario C: Fill from Shafts
OK for beam dynamics
No helium transfer line
Helium Transfer Lines

## Slide 52: Helium Transfer Lines
ILC Concept: Cryomodules have integrated helium transport -> avoids “external” helium transfer lines in Main Linac tunnel
Helium transfer lines are expensive: ~15k$ / m
Not much less than an “empty” cryomodule vessel without cavities
More expensive than a simple beam transfer line!
Conclusion: Avoid additional helium transfer lines if possible
-> Install cryomodules close to shafts

## Slide 53
Scenario A: Fill from upstream
Optimal for beam dynamics
Helium transfer line needed
No spare cryo capacity at PM12
Scenario B: Fill from downstream
Worst for beam dynamics
Helium transfer line needed
No spare cryo capacity at PM8
Scenario C: Fill from Shafts
OK for beam dynamics
No helium transfer line
Spare cryo capacities
Upgrade Installation

## Slide 54: Baseline Configuration

## Slide 55: Scenario A: Install from Upstream End
Scenario A: Fill from upstream
PM±12: 2 full cryoplants -> no spare cryo power
PM±10: 1 cryoplant, 77/74% + 2 x 1km Lhe transfer line
PM±8: no ML cryoplant (but PS/BDS)

## Slide 56: Beam Transfer Lines
There is no lattice design yet for warm transfer lines that replace the cryomodules in a staged scenario
Assumptions:
  Use similar magnets and vacuum system as in BDS right behind the Main Linac -> 16mm aperture magnets
  Use lattice similar to Main Linac: FODO lattice, one quad/corrector/BPM every 40m
  -> Quads are about 2m long (Q16L1992), 1ton each, about 1.5kW
Transfer lines are much simpler and less expensive (~7k$/m) than SC linac
But still requires girders, stands, power supplies, instrumentation
-> design is needed, but expect little impact on CFS or schedule

## Slide 57: Summary Main Linac
Scenarios A and C look viable -> Decision in Tokyo: Pursue C
Open Issues:
What is the real target energy (+ overhead) and assumed gradient?
Install full Cryoplants at once? Could machie make use of increased cryogenicpower?
How does a realistic cryomodule production schedule look like? What are demands on storage, staging, testing areas & infrastructure?
How would removal of transfer line and installation of new cryomodules proceed for a 500GeV upgrade? Can cryomodules efficiently be transported past installed CMs?
Is a helium transfer line needed? What is the design?