## Slide 1: Building blocks 0.18 µm XFAB SOI
Calice Meeting - Argonne 2014
CALIIMAX-HEP

## Slide 2: XFAB SOI 0.18 µm
SOI Silicon On Insulator ;
Recent technology (2011) ;
Cheaper than the 0.35 µm AMS technology ;
Better for digital electronics.
Disclaimer: The following is a study for building blocks in this technology, not a chip.

## Slide 3: Simplified schematic

## Slide 4: Specifications
Adjustable feedback capacitor from 500 fC to 7.5 pC ;
Slow shapers’ shaping time of 180 ns ;
Fast shaper’s shaping time of 30 ns ;
2 slow shapers: slow shaper high gain with a gain of 10, slow shaper low gain with a gain of 2/e (≈0.74) ;
Fast shaper gain 100 ;
No fancy adjustable parameters, the building blocks are as simple as it could be, there will be different versions of these ;
For all the following simulations, the feedback capacitance had been chosen to be 6 pF.

## Slide 5: Analog outputs – simulation results
Preamp output = 600 uV
Ssh10 = 6 mV
Ssh2/e = 430 µV
Fsh100 = 70 mV
discriminator

## Slide 6: Linearity
1% linearity up to 2300 MIP at preamplifier output and 2200 MIP at low gain slow shaper output.
1 MIP = 3.8 fC => 1% linearity up to 8.36 pC (with a 6 pF preamplifier feedback capacitance)

## Slide 7: Discriminator efficiency
Less than 5 ns of trigger time

## Slide 8: Monte Carlo
The dispersion is mainly due to the feedback capacitance of the preamplifier (+/- 10% accuracy)

## Slide 9: Noise issues
Noise contributions not understood. (doesn’t seem to fit the theory)
6 pF doesn’t give enough first stage gain to have a nice noise behaviour. 2 pF is preferable but the handled charge range will be reduced.

## Slide 10: Different preamplifier design options
A Nmos common source was used for these simulations.
Differential amplifier and Pmos common source have been studied too.
Differential:
  Differential preamplifier works well and permits high gain in open loop (2-stages) and so 1/1000 linearity.
  More noise and consumption.
  Bigger surface (2 input transistors, adjustable compensation capacitor)
Pmos common source:
  Preamplifier architecture of skiroc2.
  Standard cascode reduces the dynamic range, so folded cascode is used instead, leading in a drop in open loop gain and thus degrading closed loop linearity.
  Potentially the same issues with power supply than in skiroc2.

## Slide 11: Different building blocks design options
Bandgap
Shaper amplifiers
Analog memories

## Slide 12: Schedule
Tape-out in May
Back in october
First results expected in december
Possibly a new skiroc prototype on 0.18 µm

## Slide 13: Thanks for your attention