## Slide 1: FPCCD VTX R&D Status and Prospects
Yasuhiro Sugimoto
KEK
2014/9/8 @ILD meeting

## Slide 2: R&D issues
FPCCD sensor
Readout electronics
  Front-end ASIC
  Peripheral circuit
Engineering R&D
  Support structure including ladders
  Cooling system

## Slide 3: FPCCD Sensor
R&D Goal | Achievement | Prospect
Pixel size; 6um  5um | 6um fabricated, under evaluation | 5um after ILC approval
Chip size; 1x6.25cm2  2x12.5cm2 | 1.2x6.24cm2 achieved, to be evaluated | 2x12.5cm2 after ILC approval
Chip thickness; 50um | 50um achieved for 1.2x6.24cm2 chip | 
Speed; >10Mpix/s | Under investigation  Improved clock circuit needed | New clock circuit/cable in coming 2~3 years
Power; <10mW/ch | Achieved in design | To be verified soon
Radiation tolerance; >1x1013e/cm2 |  | Neutron irradiation test soon (2014/Oct.)
12x62.4mm, 50um thick CCD

## Slide 4: Readout electronics
R&D Goal | Achievement | Prospect
ASIC speed; >10Mpix/s | OK | 
ASIC power; <6mW/ch | OK | 
ASIC noise; <30electrons | OK | 
3-value clock driver |  | To be developed in 2~3 years
Low mass FPC |  | To be developed in 2~3 years
Data compression circuit |  | To be developed in 2~3 years

## Slide 5: Engineering R&D
R&D Goal | Achievement | Prospect
Low mass ladder |  | To be developed in 2~3 years
2-phase CO2 cooling system; −40C using gas compressor | Principle demonstrated | More stable and practical system in 2~3 years
Support structure |  | To be developed in 2~3 years
Engineering prototype |  | To be developed in 3 years
2-phase CO2 cooling system
for proof of principle
−40C here

## Slide 6: Backup slides

## Slide 7: FPCCD VTX