## Slide 1
European Organization for Nuclear Research
International Linear Collider
INTERNATIONAL WORKSHOP ON FUTURE LINEAR COLLIDERS
ЛЦВС14
Vinča Institute of Nuclear Sciences, Belgrade, Serbia
Long option for ILC Final Focus System
Design and Tunability of a short Traditional FFS scheme with = 8 m
Fabien Plassard, Rogelio Tomas Garcia,
Andrea Latina , Hector Garcia Morales
1,3
Polytechnic Institute of Applied Sciences (IPSA) , France
Royal Holloway University of London, UK
CERN, Switzerland
1
2
3
3
3
2,3
October 2014
LCWS14
ILC FFS
slide 1/21

## Slide 2
slide 2/21
OUTLINE
1
3
2
4
LCWS14
ILC FFS
ILC Final Focus System
Review of the traditional design
Long option for ILC Final Focus
Tuning simulation using extra sextupoles
Tuning set up
Alignment procedure (A. Latina algorithm)
Steps before tuning the FFS
Tuning preliminary results
Traditional lattice design and optimization for 8 m
Comparison for shorter design
Design optimization and results
Summary and conclusions

## Slide 3
1
LCWS14
ILC Final Focus System
Review of the traditional design
ILC FFS
slide 3/21
Review of the FFS chromaticity correction
Bending magnet
Sextupoles
QF1
QD0
IP
CCX
CCY
Bending magnet
QF1
QD0
IP
- I
- I
- I
- I
- I
- I
Traditional design
Local Chromaticity correction
Chromaticity corrected in dedicated section but not in the Final Telescope
Chromaticity corrected at the Final Doublet

## Slide 4
1
LCWS14
ILC Final Focus System
Review of the traditional design
ILC FFS
slide 4/21
Review of the FFS chromaticity correction
Key parameter | Symbol | Value | Unit
Beam energy |  | 250 | GeV
FFS length |  | 500 | m
Last Drift |  | 8 | m
Normalized emittances |  | 10 / 0.035 | μm
IP β-functions | / | 11 / 0.48 | mm
Nominal beam sizes | / | 474 / 5.87 | nm
RMS bunch length |  | 300 | μm
RMS energy spread |  | 0.125 | %
Bunch population |  | 2 | 
Numbers of bunches |  | 1312 | 
Collision rate |  | 5 | Hz
Nominal total luminosity |  | 1.5 | 
Fraction of luminosity in top 1% | / | 58.3 | %
Key parameter | Symbol | Value | Unit
Beam energy |  | 250 | GeV
FFS length |  | 500 | m
Last Drift |  | 8 | m
Normalized emittances |  | 10 / 0.035 | μm
IP β-functions |  | 11 / 0.48 | mm
Nominal beam sizes |  | 474 / 5.87 | nm
RMS bunch length |  | 300 | μm
RMS energy spread |  | 0.125 | %
Bunch population |  |  | 
Numbers of bunches |  | 1312 | 
Collision rate |  | 5 | Hz
Nominal total luminosity |  |  | 
Fraction of luminosity in top 1% |  | 58.3 | %
FINAL DOUBLET
IP
= 8 m
FFS length 500 m
Traditional scheme offers separated functions and straightforward cancellation of geometrical aberrations.
Chromaticity small and long causes high chromatic aberrations
FFS design is driven by correcting chromatic and geometric aberrations
Not locally corrected unavoidable lack of cancellation of high order chromatic aberration.

## Slide 5
1
LCWS14
ILC Final Focus System
Long option for ILC Final Focus
ILC FFS
slide 5/21
Long option for ILC Final Focus
ILC Baseline Design
Long option
Detector
Push-pull support
QD0
QF1
ground
Small using SC magnet
Less chromaticity generated at the IP
Large magnet vibration
Magnets outside of the detector on a stable ground
small magnet vibration
Same magnet for all detectors
Problem :
Luminosity and tuning of the FFS for the long option

## Slide 6
2
LCWS14
Design optimization and results
Traditional lattice optimization for 8 m
ILC FFS
slide 6/21
Traditional lattice design and optimization for = 8 m
CCX
CCY
Defocusing Quadrupoles
Focusing Quadrupoles
New sextupoles
- I
- I
- I
- I
CCX
CCY
Traditional design using extra sextupoles
Original traditional design

## Slide 7
2
LCWS14
Design optimization and results
Traditional lattice optimization for 8 m
ILC FFS
slide 7/21
Traditional lattice design and optimization for = 8 m
2 additional pairs of sextupoles located in each chromatic correction section CCX and CCY
high β-function and high dispersion region
-I transformation between pairs of sextupoles

## Slide 8
2
LCWS14
Design optimization and results
Traditional lattice optimization for 8 m
ILC FFS
slide 8/21
Nonlinear optimization (w/o SR)
Original lattice:
(10) = 825.35 nm
74% of deviation from ILC design
Extra sextupoles lattice:
(10) = 498.1 nm
5% of deviation from ILC design
Original lattice:
(10) = 7.96 nm
36% of deviation from ILC design
Extra sextupoles lattice:
(10) = 6.46 nm
10% of deviation from ILC design
Calculations made using MAPCLASS code

## Slide 9
2
LCWS14
Design optimization and results
Traditional lattice optimization for 8 m
ILC FFS
slide 9/21
Luminosity and momentum bandwidth (with SR)
Original lattice:
= 0.652
Influence of synchrotron radiation : 1.2%
Extra sextupoles lattice:
= 0.84
Influence of synchrotron radiation : 5%
Larger momentum bandwidth
Original lattice:
= 0.874
42% of luminosity loss from 1.5
Influence of synchrotron radiation : 1.8%
Extra sextupoles lattice:
= 1.36
10% of luminosity loss from 1.5
Influence of synchrotron radiation : 5.5%
Larger momentum bandwidth
Calculations made using PLACET and Guinea-Pig

## Slide 10
2
LCWS14
Design optimization and results
Traditional lattice optimization for 8 m
ILC FFS
slide 10/21
Comparison for shorter design
What is the impact of the on the traditional design performances?
(Optimization for = 6 m)

## Slide 11
2
LCWS14
Design optimization and results
Traditional lattice optimization for 8 m
ILC FFS
slide 11/21
Shorter design : nonlinear optimization (w/o SR)
lattice | [nm] | [nm]
Original design =8m | 825.35 | 7.96
New design L*=8m | 498.1 | 6.46
Original design L*=6m | 489.67 | 6.54
New design L*=6m | 492.48 | 6.08
lattice |  | 
 | 825.35 | 7.96
New design L*=8m | 498.1 | 6.46
Original design L*=6m | 489.67 | 6.54
New design L*=6m | 492.48 | 6.08
The original design for = 6 m provides better horizontal beam size than the extra sextupole design for = 8 m
The extra sextupoles design for = 6 m reduces only the vertical beam size
The shorter generates less chromatic aberrations at the FD

## Slide 12
2
LCWS14
Design optimization and results
Traditional lattice optimization for 8 m
ILC FFS
slide 12/21
Shorter design : momentum bandwidth (with SR)
Original design = 6 m : = 1.38
Extra sextupoles design = 6 m : = 1.42
Larger momentum acceptance for both design with = 6 m
Large impact of on the traditional scheme performance

## Slide 13
3
LCWS14
Tuning simulation using extra sextupoles ( = 8 m)
Tuning set up
ILC FFS
slide 13/21
Tuning simulation
The performance of a linear collider drops when we consider magnet misalignments
Under realistic conditions the luminosity is reduced and an alignment procedure is mandatory
Tuning process brings the system to its design performance using beam-based alignment techniques and beam parameters optimization algorithm
Tuning set up ( ILC errors parameters)
110 randomly misaligned machines (seeds)
Initial misalignment : 10 μm RMS in transverse plane ()
Elements misaligned : Quadrupoles, Sextupoles , BPMs
Dipole correctors : Corrector + Quad + BPM
BPM resolution : 10 nm
Tracking and luminosity measurement provided by PLACET and Guinea-Pig
Short Traditional lattice using extra sextupoles and = 8 m
Take into account nonlinearities and synchrotron radiation
Luminosity goal : = 1.5

## Slide 14
3
LCWS14
Tuning simulation using extra sextupoles ( = 8 m)
Alignment procedure
ILC FFS
slide 14/21
Alignment procedure (A. Latina algorithm)
Beam Based Alignment (orbit correction) : Sextupoles switched OFF
1-1 correction =
Minimize BPMs reading
DFS =
correct orbit and dispersion simultaneously
Multipole-shunting (1)
Sextupoles Powered individually
Beam Based Alignment
Sextupoles switched ON
Multipole-shunting (2)
Beam parameters optimization using orthogonal knobs
DFS =
Multipole Knobs 1
Beam parameters optimization using orthogonal knobs
Multipole Knobs 2
1
2
3
4
5
6
7

## Slide 15
3
LCWS14
Tuning simulation using extra sextupoles ( = 8 m)
Steps before tuning the FFS
ILC FFS
slide 15/21
Steps before tuning
y
x
16 sextupoles in the lattice
32 sextupole position in and for the beam corrections
The tuning simulation time increases with the number of knobs
Response matrices calculation :
Weigthing factors ,
Knobs computation
1 iteration using 10 knobs
1 iteration using 23 knobs
1 iteration using 32 knobs

## Slide 16
3
LCWS14
Tuning simulation using extra sextupoles ( = 8 m)
Tuning preliminary results
ILC FFS
slide 16/21
Tuning preliminary results : Number of knobs
32 knobs 25h 36min
70% machines reach 65% of
23 knobs 18h 24min (simulation time)
15% machines reach 60% of
10 knobs 8h
10% machines reach 30% of
= 1.5

## Slide 17
3
LCWS14
Tuning simulation using extra sextupoles ( = 8 m)
Tuning preliminary results
ILC FFS
slide 17/21
Tuning preliminary results : all knobs
BBA + Knobs iterations do not improve the luminosity
Need to optimize the weights ,
70% machines reach more than 70% of and 25% machines reach more than 80% of
= 1.5

## Slide 18
3
LCWS14
Tuning simulation using extra sextupoles ( = 8 m)
Tuning preliminary results
ILC FFS
slide 18/21
Tuning optimization steps
Luminosity evolution after each optimization step for 3 random machines
The BBA cancels the luminosity gain by the sextupole knobs tuning but the luminosity is recovered after the sextupole knobs
Need to optimize the tuning algortihm?

## Slide 19
3
LCWS14
Tuning simulation using extra sextupoles ( = 8 m)
Tuning preliminary results
ILC FFS
slide 19/21
Tuning optimization steps
1-1 correction
DFS1
Sextupole-shunting
Sextupole knobs 1
DFS2
Sextupole-shunting 2
Sextupole knobs 2
1-1 correction
DFS1
Sextupole-shunting
Sextupole knobs 1
DFS2
Sextupole-shunting 2
Sextupole knobs 2
1-1 correction
DFS1
Sextupole-shunting
Sextupole knobs 1
DFS2
Sextupole-shunting 2
Sextupole knobs 2
The full algorithm is still the best option for the BBA + Knobs tuning
Other simulations are progressing for different optimization steps
Need to optimize the weigths and

## Slide 20
3
LCWS14
Tuning simulation using extra sextupoles ( = 8 m)
Tuning preliminary results
ILC FFS
slide 20/21
Weights optimization : and
DFS1 =
DFS2 =
DFS equation must be weighted in order to have the same impact on the vector of observables on the left hand-side of the system
The weights and are used for the dispersion terms while for the SVD to limit the amplitude of the correctors θ
Weight optimization is underway by simulating several combinations of weights on 40 seeds and by using as initial parameter the theoretical value of ω
Theoretical value of ω:

## Slide 21
4
LCWS14
Summary and conclusions
ILC FFS
slide 21/21
Summary and conclusions
The new traditional design using extra sextupoles for = 8 m provides a good correction of high order aberrations with 10% of total luminosity loss (1.36)
The long last drift limits the FFS performance especially for the non-local chromaticity correction scheme = 6 m provides better performances
The tuning turns out to be long due to the number of sextupoles in the lattice
With optimistic set up and errors parameters, the tuning of the system seems feasible but must be improved ( 70% machines reach more than 70% of ILC design luminosity)
Several simulations are mandatory for the optimization of the weights and and the alignment procedure in order to conclude on the tunability of this design