A Design Study of ILC Positron Source by Electron Driven Scheme
(300 Hz linac Simulation)
M. Kuriki, Y. Seimiya, T. Takahashi (Hiroshima U.)
T. Okugi, M. Sato, J. Urakawa, T. Omori (KEK)
S. Kashiwagi (Tohoku U.)
LCWS2014, Belgrade, Serbia, 6-10 October 2014

---
Undulator Positron Source
Driven by >125 GeV beam.
Polarized positron (30-60%) which is powerful tool for physics.
There is no fundamental and technical difficulties.

---
Undulator Positron Source
Pros and Cons
- Positron can be polarized (30-60%).
- Relatively less heat load on target.
- Require >130GeV drive beam. Share the e- beam for collision.
- The pulse structure is fixed, 1ms.
- Need physical path length adjustment.
- Undulator section is up to 230m.
- System demonstration prior to the construction is difficult.
- A technical backup is desirable.

---
Positron Source
Staging approach to minimize possible risks and maximize physics potential.
1st stage : Unpolarized e-driven e+ source .
  (no polarizatino, but “conventional”)
2nd stage: Polarized undulator driven e+ source. (polarized, but totally new)

---
Positron Source
Staging approach to minimize possible risks and maximize physics potential.
1st stage : Unpolarized e-driven e+ source .
  (no polarizatino, but “conventional”)
2nd stage: Polarized undulator driven e+ source. (polarized, but totally new)

---
E-Driven ILC Positron Source
- 6 GeV electron with W-Re target.
- SC accelerator, 2700 bunches/1 ms with SC 5Hz → 300 m/s.
- Can we relax the condition?
Positron Capture
Electron Gun
Electron Lianc
Positron Booster
Rotating Target
high heat load

---
E-Driven ILC Positron Source
- 6 GeV electron with W-Re target.
- SC accelerator, 2700 bunches/1 ms with SC 5Hz → 300 m/s.
- Can we relax the condition?
Positron Capture
Electron Gun
Electron Lianc
Positron Booster
Rotating Target
high heat load

---
Electron Driven Scheme (1)
E-Driven ILC Positron Source
- 300Hz NC accelerator → 2700/64ms (132 bunches x 300Hz , 64 ms).
- The heat load on the target is manageable.
- Tangential speed is 5 m/s.
Positron Capture
Electron Gun
Electron Lianc
Positron Booster
Rotating Target
Less heat load

---
E-Driven ILC Positron Source
- 300Hz NC accelerator → 2700/64ms (132 bunches x 300Hz , 64 ms).
- The heat load on the target is manageable.
- Tangential speed is 5 m/s.
Positron Capture
Electron Gun
Electron Lianc
Positron Booster
Rotating Target
Less heat load

---
Positron Capture Simulation
- E+ distribution was made by GEANT4.
- Tracking simulation in the injector section ( <250MeV) by GPT; AMD positron capture (B0~5.0T) followed by solenoid focusing section (0.5T) with L-band Acceleration up to 250 MeV.
- Chicane to remove electrons and lower energy positrons.
- Hybrid Booster linac (L- and S-band) and EC (Energy Compressor) by SAD.
- Positron yield is examined with DR acceptance.
target
e- linac
e+ capture
e+ booster
ECS
DR

---
AMD (Adiabatic Matching Device)
8mm, 5T
- AMD is made by Flux Concentrator.
- Induce a strong solenoid-like B filed for transverse momentum suppression.
- It could be similar to that for S-KEKB.

---
Impact of Near Target Configuration
- Positron yield strongly depends on the near target configuration.
  - Target Position wrt AMD peak field,
  - Solenoid field quality,
  - Existence of bridge solenoid coil,
- E=6GeV, t=14mm, σ=4mm, RAMD=10mm、BAMD=5T

---
Caputure efficiency at the injector
- Positron yield is examined at the injector.
- AMD field by KEKB FC.
- Bz is smoothly connected.
- BC, dz, and solenoid fluctuation has strong impacts.
With BC
Fluctuated
No BC
Dz	No BC, constant	With BC, constant	With BC, fluctuated
0 mm	1.45	1.65	1.05
5 mm	-	1.41	0.89
10 mm	1.10	1.18	-

---
Caputure efficiency at the injector

---
Positron Injector
- 3 L-band tubes (20mm aperture, 25 MV/m) with solenoid focusing.
- Deceleration capuring.
  - The positron peak is on deceleration phase.
  - Positrons are sent to the acceleration phase by phase slipping.

---
Positron Booster
- Positron booster is hybrid :L-band (17mm aperture) and S-band (10 mm aperture) accelerators.
- 62 L-band and 56 S-band tubes give an enough efficiency.
required yield

---
Chicane and ECS
Before and after chicane
- Chicane removes electrons and low energy positrons.
- ECS (Energy Compressor Section) optimize the longitudinal phase space distribution for better DR acceptance.
After ECS
DR acceptance

---
Pulse Structure and Beam-loading
- Positrons are accelerated by triplet multi-bunch pulse.
- The triplet pulse is repeated in 300Hz.
- Transient beam-loading should be compensated, otherwise, the beam is not accepted by DR.
RF Voltage
44 bunches
6.15ns spacing
0.55A
44 bunches
6.15ns spacing
0.55A
44 bunches
6.15ns spacing
0.55A
100ns
100ns
0.55A
264ns

---
Beam-loading Compensation by AM
Beamloading term
Acceleration voltage by a flat RF (E0),
AM to compensate the beam loading
For transient component
For steady component
V(no beam)
loading
V(with beam)
V(beam loading)

---
Beam-loading Compensation by AM
Beamloading term
Acceleration voltage by a flat RF (E0),
AM to compensate the beam loading
For transient component
For steady component
V(no beam)
loading
V(with beam)
It will be tested in KEK.
V(beam loading)

---
Capture Efficiency and PEDD
- PEDD：Peak Energy Deposition Density. The practical limit by SLC is 35 J/g.
- PEDD and energy deposition on the target per bunch is estimated giving 3.0e+10 positron per bunch with 50% margin.
- 6GeV, 14mm target, 4mm spot is likely to be optimum.

---
Capture Efficiency and PEDD
- PEDD：Peak Energy Deposition Density. The practical limit by SLC is 35 J/g.
- PEDD and energy deposition on the target per bunch is estimated giving 3.0e+10 positron per bunch with 50% margin.
- 6GeV, 14mm target, 4mm spot is likely to be optimum. (e+ yield is 1.25 and e- bunch charge is 2.4e+10.)

---
Conclusion
- Electron driven ILC positron source is considered as a technical backup.
- According to the simulation, 3.0E+10 positron/bunch is obtained with a moderate parameter set.
- By manipulating the pulse structure, target load is much relaxed.
- Beam-loading compensation for the triplet pulse acceleration is likely to be promising (to be tested in KEK).
- This work is partly supported by Grant-in-Aid for Scientific Research (C 26400293) by MEXT Japan.

---
Path Length Condition
- DR Bucket for the generated positron should be vacant.
- Self-reproduction condition: Positron goes to a bucket where the collision partner (electron) was.
- Another condition is for collision.
- The path length adjustment has to be made by physical length adjustment (timing shift can not make it).
{size 20 color yellow { For collision : L_1 + L_2 = %DELTA_1 + %DELTA_2 + L_3,}} {size 20 color yellow { For self-reproduction : L_1 + L_4 = %DELTA_2 + nC_{DR},}} {size 24 color yellow { L_3 + L_4 + %DELTA_1 = L_2 + nC_{DR},}}

---
Beamloading Compensation by AM
- Beam-loading compensation by AM (Amplitude Modulation) is considered.
- By solving RF envelope giving a flat acceleration, it can be compensated perfectly.
Beamloading term
Beamloading term
Acceleration voltage by a flat RF (E0),
To compensate the transient beam-loading, AM is introduced as follows,
For steady beam
loading suppression
For transient beam
loading suppression

---
Beam loading Compensation by AM
Acceleration voltage by AM RF (E0 +E1+E2 ),
Solution for the flat acceleration
V(no beam)
loading
V(with beam)
V(beam loading)

---
DR acceptance
- DR acceptance is
  - gAx+gAy<0.07m
  - dE<1.5%, dz<0.07m (FW)
- By considering RF acceleration in S or L-band, wider dE is desirable even with less dz.
0.015

---
Phase-space Matching with EC
- Matching with EC is considered.
- Transfer matrix of EC (R means R56).
- r1(EC entrance) is written by r2 (EC exit).
- Effective DR acceptance is operable by EC(R).

---
Optimization
dE Acc.
with EC
dE by Capture
dE by RF
f shows the allowed dinj
R56=1m is likely to be OK.

---
300Hz Conventional Positron Source
Several GeV drive beam.
Several X0 conversion target.
AMD(Adiabativ Matching Device) for pt compenstaion; B0~7.0T.
S-band or L-band Standing wave linac for capture. 25MeV/m.
6GeV, 15mm (W) target, 4mm rms beam size as a working assumptions.

---
Multi-Pulse Acceleration
M. Satoh
- AM to compensate BL effect.
- AM should be applied to not only on the pulse head, but also the pulse interval.
- A flat acceleration is made.
AM RF pulse
Beam pulse
VRF (no AM)
VRF (AM)

---
d-z phase-space
- 1000 electrons impinge on the target.
- >8000 positrons are generated.
- 1100 positrons are survived and accepted by DR.
- The yield is 1.1 (e+/e-).
- 1.5 is the design criterion.
Injector Output
Booster End
EC End
DR acceptance

---
Beam loading Compensation at EC

---
ILC Luminosity
{ size 20 color blue {L = {f_{rep} n_b N^2} over {4 %pi %sigma_x %sigma_y}}}
Event rate
Luminosity
Beamstrahlung
Disruption
{size 24 color blue { N = %sigma times L}}
{ size 20 color blue {{%DELTA E} over E prop {N^2 E} over { (%sigma_x^2 + %sigma_y^2)%sigma_z}}}
sy « sx
Keep luminosity and surppress
Beamstrahlung and Disruption.
{ size 20 color blue {D_{x,y} = {2Nr_e} over %gamma %sigma_z over {%sigma_{x,y}(%sigma_x + %sigma_y)}}}
Parameter	Value
Luminosity	1.8x1034cm-2s-1
Horizontal size	640 nm
Vertical size	5.7 nm
Bunch length	300 mm
Vertical Disruption	19.4
RMS energy by BS	2.4%
Horizontal emi.	10 mm.mrad
Vertical emi.	0.04 mm.mrad