## Slide 1: Hybrid ECAL: optimization and related developments
Taikan Suehara
H. Hirai, H. Sumida, Y. Sudo, T. Yoshioka, K. Kawagoe
(Kyushu University, Japan)

## Slide 2: Topics
Why hybrid?
Optimization
Combined DAQ
Plans

## Slide 3: ILD & ECAL
ILD: Intl. “Large” Detector
rECAL = 1800 mm (SiD: 1200 mm)
Excellent PFA power
but expensive ECAL/Yoke
mean cost
for ECAL/HCAL
ILD cost in DBD: 391.8 MILCU in total

## Slide 4: ILD ECAL: Silicon and Scintillator
SiECAL
ScECAL
Tungsten absorber + Silicon
320 mm (maybe 500 mm)
5 x 5 mm2 pixels
256 pixels / chip
Expensive sensor
Tungsten + Scintillator strips
1 mm thick (10-20 photons)
5 x 45 mm2 crossing strips
Each strip should be wrapped
Price is about half of Silicon (dominated by PPD)

## Slide 5: A comparison
V. Balagura (LLR), ILD meeting in Oshu

## Slide 6: Cost-conscious options
Small detector: rECAL ~ 1400 mm with silicon only
+ Robustness in ECAL, Simple
+ Cheaper not only in ECAL but also in York
Performance degraded (both trackers and CALs) esp. 1 TeV upgrade should be a problem
Very similar to SiD: redundancy reduced
Hybrid ECAL (Silicon + Scintillator)
- A bit more complexity, careful calibration needed (with AHCAL complexity will be reduced) - Cheaper only in ECAL: competitive if stray field restriction can be revisited for yoke
+ Performance degradation is very small
+ Large detector  more possibility for 1 TeV
+ Variety remained to SiD, more redundancy
performance
 equivalent luminosity  operation cost

## Slide 7: Consideration for Calibration
MIP calibration
LED calibration (Scintillator only)
  No specific procedure for hybrid
  Fluctuation can be seen by Si/Sc ratio
Electron calibration
  Compare with momentum in trackers
    Bhabha monochromatic (125 GeV?) many stats.
    Bhabha radiative return, WW/ZZ, continuous
  Si/Sc ratio can be confirmed with various Es
  Will be studied by MC
Pion calibration – using tau (continuous only)

## Slide 8: Optimization

## Slide 9: What to optimize
Thickness(es) of absorber (number of layers)
Granularity (pixel size)
How to combine Si/Sc
  Fraction of Si/Sc
  Alternate or grouped

## Slide 10: N layers & Granularity
Jet energy resolution is dominated by
  Intrinsic resolution @ low E (Mainly HCAL)
  Confusion @ high E
Other physics
  p0 reconstruction in tau (Higgs CP etc.)  relatively high energy photons
  Hgg (higher energy)
  Photon pointing (BSM study)

## Slide 11: A study of # layers
Preliminary

## Slide 12: Hybrid: alternate or grouped?
Essentially the same performance in DBD detector  grouped setup is favored for simplicity
More check (tau etc.) needed

## Slide 13: Optimization - ToDo
Optimization still in early stage  One proposal should be shown in a year
Plans
  Hadron energy resolution study
  Confusion study with different granularity and combination of Si/Sc
  Tau/p0 separation study
  Test of calibration procedure in MC
  Goal: cheaper (similar to 1400 mm) detector without significant degradation of performance

## Slide 14: DAQ

## Slide 15: Combined DAQ - motivation
“CALICE DAQ” was aimed to unify all efforts involving DAQ of calorimeters to save resource.
  “ROC” chips  successful
  DIF/LDA board  spilt some years ago
  Software  completely independent
At some point, we should unify (again)
 Hybrid ECAL is a good start point

## Slide 16: EUDAQ: a high level structure
Calice Producer
calicoes / others
TCP connection

## Slide 17: Planned test of combined DAQ
2nd TB period at CERN in this Autumn - 26th November to 8th December
  Mainly AHCAL testbeam with 3 ScECAL layers
We will put a Si layer in front of Sc layers
Minimum-combined DAQ will be tested
  Developing now
  based on EUDAQ

## Slide 18: Current status
Succeeded to run EUDAQ with CaliceProducer producing dummy data encoded to LCIO object and save to LCIO file using DataCollector Ready to attach to calicoes/others

## Slide 19: Combined DAQ - ToDo
General discussion has started at last CALICE technical board
Agreement at all-CALICE is needed about the framework to be used (at least)
Gradual approach is the only possibility now - if we don’t have a strong group doing everything
I hope it well proceed in several years to one “ILC DAQ”

## Slide 20: Summary
We think Hybrid ECAL is a strong option for cost-effective ILD
We plan to finish a “optimized hybrid” setup in a year
Combined DAQ is another issue we will try to combine Si/Sc DAQs as a first step to more generic DAQ