Posipol 2014 Summary
M. Kuriki and W. Gai
Posipol2014, Ichinoseki, Iwate, 2014/8/27-29

---
Posipol 2014
Electron/FEL/other : 3
Undulator : 7
Laser Compton/X-ray: 7
Conventional/KEKB : 12

---
Recommendation
Ferrofluid sealed and water cooled
Recommendation with the highest priority.
1. Resume the water-cooled ferro-fluid sealed target test with modifications. (1M USD, 2014-2015)
2. If (a) is successful, we construct the target equivalent to the real machine. (3 M USD, 2015-2017)
3. Endurance test of the target (2017)

---
Non-water cooled
1. Investigate several critical aspects to establish the conceptual design of the non-water cooled target. (2014-2015)
2. Some basic tests, e.g. friction with lubricant, material dilution, out gas rate, etc. if it is possible with a limited amount of money. (2014-2015)
3. If (a) and (b) are succesfull, a mock-up is constructed (3.1 M Euro + 5.5 Man.year) which is compatible to examine radiation cooling and contact cooling. (2 years)

---
300kHz electron driven
1. It is desirable to have a technical backup from a project point of view.
2. Finish the target prototyping and endurance test. (2014-2016)
3. Complete TDR level design (2015).
  1. Fix the lattice, components with cost estimation. TDR cost estimation can be reused.
4. Establish engineering design (2016-2017)