## Slide 1
On behalf of the LCTPC collaboration
Study of a Large Prototype TPC using
Micro-Pattern Gas Detectors
David Attié 
CEA Saclay/Irfu
www.lctpc.org
Notes: I’m here to present a TPC review

## Slide 2: Overview
Introduction: Physics case at International Linear Collider (ILC)
R&D of a Large Prototype Time Projection Chamber for ILC
TPC Readout using Micro-Pattern Gaseous Detectors:
  GEM modules with ALTRO electronics
  Integrated AFTER-based electronics and resistive Micromegas detector module
  Pixel readout
Studies
  Transverses resolution
  Multi-module effect & field distorsions
  Ion feedback
  2-Phase CO2 cooling
Conclusion

## Slide 3: Introduction: Physics Case at ILC
B=3.5 T
e+eHZ,Zµµ
Identify the particle of cosmic dark matter
Find the origin of the masses of elementary particles
  precision of Higgs coupling to each particle mass
  sensitivity of the ILC experiments to Higgs boson couplings in a model-independent analysis
Higgs-strahlung recoil mass: e+e- → ZH (Z→μ+μ-/e+e-) + X
Next collider: linear e+e– collider, length: ~ 31km
Tunable center of mass energy of 200-500 GeV
Two detectors with push-pull concept
Particle Flow* concept necessary [*] Particle flow: the aim to reconstruct every particle in the best suited sub-detector

## Slide 4: Time Projection Chamber for ILD
TPC is the central tracker for International Linear Detector
– Large number of 3D points  continuous tracking
– Good track separation and pattern recognition
• Low material budget inside the calorimeters important for PFA
– Barrel: inner <1% X0 ; outer <5% X0 – Endplates: ~25% X0 (<10 cm)
• Two options for endplate readout (MPGD):
    – GEM
    – Resistive Micromegas
• Alternative: pixel readout
ILD
TPC Requirements :
Momentum resolution:
(1/pT) < 9×10-5 GeV-1
Spatial resolution at 3.5T:
(r) < 100 m
(z) < 500 m
Field uniformity:
E/E~2×10-4
Tracking eff. for pT>1 GeV: 97%
dE/dx resolution ~5%
4.7m
3.62m
Cathode membrane
Endplate
MPGD
Large Prototype
TPC

## Slide 5: Large Prototype TPC for ILC
Built by the LCTPC collaboration in 2008
Financed by EUDET
Magnet upgraded in 2012 within AIDA
Located at DESY: 6 GeV e- beam
Sharing out :
- magnet: KEK, Japan
- field cage, stage: DESY, Germany
- cosmic trigger: Irfu, France
- beam trigger: Nikhef, Netherlands
- endplate: Cornell, USA
- Resistive Micromegas: Irfu, France, Carleton/Montreal, Canada
- Double GEMs with 100m laser-etched crystal polymer: Saga, Japan
- Triple 50m GEMs: DESY, Cern
- TimePix pixel: F, G, NL<
1T PCMagnet on lifting stage
Large Prototype TPC
Endplate + 7 Micromegas modules

## Slide 6: Micro-Pattern Gaseous Detectors: Micromegas & GEM
50-100 µm
40 kV/cm
~1000 µm
1 kV/cm
GEM
~100 µm
80 kV/cm
Micromegas
Technology choice for TPC readout: Micro Pattern Gaseous Detector
more robust than wires
no E×B effect
better ageing properties
easier to manufacture
Avalanche
fast signal & high gain
low ion backdrift
Gas Electron Multiplier (F. Sauli, 1997)
2 copper foils separated by kapton
multiplication takes place in holes
use of 2 or 3 stages
MICROMEsh GAseous Structure (Y. Giomataris et al., 1996)
metallic micromesh (typical pitch 50-100 µm)
supported by pillars, multiplication between anode and mesh, high gain
Gas Electron Multiplier (F. Sauli, 1997)
2 copper foils separated by kapton
multiplication takes place in holes (50-100 µm)
2-3 layers needed, high gain

## Slide 7: Asian GEMs
Double GEM module using Laser-etched Liquid Crystal Polymer of 100 µm
Made in Japan (SciEnergy)
Pad size: 1.21×5.4 mm2
28 staggered rows of 176-192 pads 4829 channels
3 modules equipped (10 000 channels) read out by ALTRO electronics
Next step: SALTRO with better integration

## Slide 8: European GEMs
Triple GEM module with thin ceramic frame (1mm)
Manufactured at Cern (50 µm)
Pad size: 1.26×5.85 mm2
28 rows (4829 channels)
3 modules equipped (10 000 channels)
read out by ALTRO electronics

## Slide 9: Resistive Micromegas
Pads PCB
+
Micromegas
Cooling system
Front-End Mezzanine
Front-End Card (FEC)
Fully integrated Module
Resistive Micromegas Detector
FEC
FEM
Micromegas with resistive coating
Various resistive coatings have been tried:
  Carbon-loaded Kapton (CLK): 3 and 5 /,
  resistive ink
Pad size: 3×6.8 mm2
24 pad rows (1726 channels)
7 modules equipped (12 000 channels) read out by fully integrated electronics based on AFTER chips (T2K TPC)
Resistive foil
Isolated layer
Pads
PCB
Micromegas mesh
d/X00.24
See Dixit et.al., NIM A518 (2004) 721

## Slide 10: Pixel Readout R&D
GEM
InGrid
Bonn
Bonn, Nikhef
Irfu, Nikhef
TimePix chip: 256 × 256 pixels of 55 × 55 µm² size
Each pixel can be set to:
  Hit counting
  Charge measurement
  Time measurement

## Slide 11: LCTPC Software Framework
Reconstruction, simulation, analysis based on common ILC software tools:
  LCIO (Linear Collider I/O): event data model
  Marlin (Modular Analysis & Reconsctruction for the LINear Collider)
  LCCD: (Linear Collider Conditions Data toolkit)
  Gear: (Geometry Api for Reconstruction)
Specific software package of LCTPC:
MarlinTPC: https://znwiki3.ifh.de/MarlinTPC/MarlinTPC
  Reconstruction processors
  Conditions handling
  Simulation (coarse to detailed)
  Common analysis for standard plots
Data
  Testbeam data stored on Grid storage
  → accessible by whole collaboration
  Common conditions database server

## Slide 12: Transverse resolution [Resistive Micromegas]
Gas: Ar/CF4/Iso 95/3/2
B = 0 & 1T
B=0 T
Cd = 315.1 µm/√cm (Magboltz)
B=1 T
Cd = 94.2 µm/√cm (Magboltz)
0: resolution at z=0
Neff: effective number of electrons
Cd : the diffusion constant

## Slide 13: Transverse resolution [GEMs]
Gas: Ar/CF4/Iso 95/3/2
B= 1T
Asian GEM
European GEM
0: resolution at z=0
Neff: effective number of electrons
Cd : the diffusion constant

## Slide 14: Field distorsions at B=0T
B=0T, distortions due to E only
  In r: 150 to 200 µm corrected down to 20 µm
  In Z: few 100 µm (50 µm)
Before corrections
After corrections
14
In r
In Z

## Slide 15: Field distorsions at B=1T
B=1T for GEM and Micromegas
  In r: 150 to 200 µm corrected down to 20 µm
  In Z: few 100 µm (50 µm)
GEM
Micromegas
After correction
In r
In Z

## Slide 16: Ion Back Flow Issue
Primary ions create distortions in the Electric field which result to O(<1µm) track distortions. 1 to 2 orders of magnitude safety margin with estimated background
After each bunch train, a
disk of positively charged
ions from the amplification
stage drifts back into the
TPC volume

## Slide 17: Data taking in 2014
Cosmic
Laser
Beam 4 GeV
Edrift (V/cm) | Drift Velocity (cm/s) | 
 | Measured | Simulated
230 | 7.44±0.01 | 7,55±0.1
140 | 5.84±0.01 | 5,79±0.1
T2K gas: Ar/CF4/Iso 95/3/2
Gas impurity:
  60 ppm O2,
  150 ppm H2O
Electron momentum measurement

## Slide 18: Test of CO2 Cooling System
2-phase CO2 cooling system was designed for the LP setup of the Micromegas modules with integrated electronics (26W/module)
CO2 has lower viscosity & higher latent heat than all usual refrigerants
  Very small pipes (high pressure with low material budget)
  CO2 liquid & gas can be used at room temperature
Operation and test conditions :
  2PCO2 at 45 bars 10°C
  Temperature control during different regimes
    5V LV supply on, nocooling
    LV supply off, with cooling
    LV supply on, with cooling
    2 series of measurement
About 30°C stable temperature was achieved during operation of 7 Micromegas modules at DESY
7 FEMs
6 FECs per FEM

## Slide 19: Pulse Shape Fit Procedure
Fit each individual (main) pulse with f(t)
  normalize amplitude to Amax pulse-by-pulse
  force pulse maximum at zero
  3 time bins before and 2 time bins after
Significatively improved compared to parabolic or box fit
The following analysis function f(t) is proposed for
determination of the charge using pulse shape:

## Slide 20: Pulse Shape Fit Procedure
Z resolution study with the Kalman filter is then performed in MarlinTPC
  improvement of about 25% all over drift distance
  this method shows homogeneous resolution across a module

## Slide 21: Summary
The LCTPC collaboration have been working since many years on a Large Prototype of a TPC
The performance of two MPGD technology reached the requirements of the ILD detector
The readout technology has to be chosen (GEM or Micromegas)
Studies are going on: ion back drift, electronics, mechanical integration, software processors ...
The presented infrastructure has received funding from the European Commission under
the FP7 Research Infrastructures project AIDA, grant agreement no. 262025.

## Slide 22: Thank you

## Slide 23: Backup slides