## Slide 1: Development of a Low-latency, High-precision, Intra-train Beam Feedback System Based on Cavity Beam Position Monitors
N. Blaskovic Kraljevic, D. R. Bett, P. N. Burrows, G. B. Christian, M. R. Davis, Y. I. Kim, C. Perry
John Adams Institute, University of Oxford, UK

## Slide 2
Outline
Neven Blaskovic Kraljevic 2
Introduction
  Feedback at a linear collider
  International Linear Collider
  Feedback on Nanosecond Timescales
Experimental setup at Accelerator Test Facility
Cavity beam position monitor signals
Modes of feedback operation
Results

## Slide 3
Introduction
Feedback at a Linear Collider
Neven Blaskovic Kraljevic 3
Successful collision of bunches at a linear collider is critical
A fast position feedback system is required
Misaligned beams at interaction point (IP) cause beam-beam deflection

## Slide 4
Neven Blaskovic Kraljevic 4
Successful collision of bunches at a linear collider is critical
A fast position feedback system is required
Introduction
Feedback at a Linear Collider
Misaligned beams at interaction point (IP) cause beam-beam deflection
Measure deflection on one of outgoing beams
(beam position monitor)

## Slide 5
Neven Blaskovic Kraljevic 5
Successful collision of bunches at a linear collider is critical
A fast position feedback system is required
Misaligned beams at interaction point (IP) cause beam-beam deflection
Measure deflection on one of outgoing beams
Correct orbit of next bunch (correlated to previous bunch due to short bunch spacing)
(beam position monitor)
Introduction
Feedback at a Linear Collider

## Slide 6
Introduction
International Linear Collider (ILC)
Neven Blaskovic Kraljevic 6
Proposed linear electron-positron collider
Centre-of-mass energy: 250-1000 GeV
Vertical beamsize: 5.9 nm
Bunch separation: 554 ns
(ILC Technical Design Report)

## Slide 7
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic Kraljevic 7
Test bed for the International Linear Collider
Facility located at KEK in Tsukuba, Japan
Goals:
  37 nm vertical spot size at final focus
  Nanometre level vertical beam stability

## Slide 8
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic Kraljevic 8
Electron source
90 meters

## Slide 9
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic Kraljevic 9
1.28 GeV linear accelerator
Electron source
90 meters

## Slide 10
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic Kraljevic 10
Damping ring
Electron source
1.28 GeV linear accelerator
90 meters

## Slide 11
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic Kraljevic 11
Damping ring
Electron source
Extraction line
Final focus
Model interaction point (IP) of a collider
1.28 GeV linear accelerator
90 meters

## Slide 12
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic Kraljevic 12
Damping ring
Electron source
Extraction line
Final focus
Model interaction point (IP) of a collider
Feedback system
1.28 GeV linear accelerator
90 meters

## Slide 13
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic Kraljevic 13
ATF can be operated with 2-bunch trains in the extraction line and final focus
The separation of the bunches is ILC-like (tuneable up to ~300 ns)
Our prototype feedback system:
  Measures the position of the first bunch
  Then corrects the path of the second bunch
Train extraction frequency: ~3 Hz

## Slide 14
Introduction
Feedback on Nanosecond Timescales (FONT)
Neven Blaskovic Kraljevic 14
Low-latency, high-precision feedback system
We have previously demonstrated a system meeting ILC latency, BPM resolution and beam kick requirements
We have extended the system for use at ATF
We aim for nanometre level beam stabilisation

## Slide 15
Neven Blaskovic Kraljevic 15
P3
P2
P
Stripline BPM
12 cm long strips
12 mm radius
On x and y mover system
Experimental Setup
beam

## Slide 16
Neven Blaskovic Kraljevic 16
P3
P2
for stripline BPM
Analogue: latency 13 ns
Resolution of 330 nm
Details in poster TUPME009
Σ
Δ
BPM top
BPM bottom
Processor
Processor
Processor
Experimental Setup
beam

## Slide 17
Neven Blaskovic Kraljevic 17
P3
P2
Processor
Processor
IPB
IPB
Cavity BPM at beam waist
C-band: 6.4 GHz in y
Low Q: decay time < 30 ns
Resolve 2-bunch trains
Experimental Setup

## Slide 18
Neven Blaskovic Kraljevic 18
P3
P2
for cavity BPM
Analogue, 2-stage downmixer
Resolution of < 100 nm
Developed by Honda et al.
Processor
Processor
Processor
IPB
Processor
Experimental Setup

## Slide 19
Neven Blaskovic Kraljevic 19
P3
Processor
P2
Processor
IPB
Processor
Board
Board
Board
9 ADC channels at 357 MHz
2 DAC channels at 179 MHz
Xilinx Virtex 5 FPGA
Experimental Setup

## Slide 20
Neven Blaskovic Kraljevic 20
P3
Processor
P2
Processor
Amplifier
Amplifier
Amplifier
IPB
Processor
Board
Board
Made by TMD Technologies
± 30 A drive current
35 ns rise time (90 % of peak)
Amplifier
Experimental Setup

## Slide 21
Neven Blaskovic Kraljevic 21
P3
Processor
P2
Processor
K2
Amplifier
IPK
Amplifier
K1
Amplifier
IPB
Processor
Board
Board
Vertical stripline kicker
30 cm long strips for K1 & K2
12.5 cm long strips for IPK
K
Kicker
Experimental Setup
Local upstream feedback results presented in poster TUPME009

## Slide 22
Cavity BPM Signal Processing
Neven Blaskovic Kraljevic 22
Reference cavity
Monopole mode frequency (in y)
~6426 MHz
IPB cavity
Dipole mode frequency (in y)
~6426 MHz

## Slide 23
Neven Blaskovic Kraljevic 23
Cavity BPM Signal Processing
The IPB and reference cavity signals are downmixed using a common, external 5712 MHz local oscillator (LO)
simplified schematic

## Slide 24
Neven Blaskovic Kraljevic 24
Cavity BPM Signal Processing
The IPB signal is downmixed using the reference cavity signal as LO
The I and Q output signals at baseband are used to obtain the beam position
simplified schematic

## Slide 25
K2
K1
IPB
Neven Blaskovic Kraljevic 25
P3
Processor
P2
Processor
Amplifier
Amplifier
Amplifier
Processor
Board
Board
IPK
Feedforward
Use position at P2 & P3 to correct position at IPB
Correction calculated locally, then sent along 60 meters of cable
Latency: 202 ns
Effect measured at IPB

## Slide 26
Neven Blaskovic Kraljevic 26
FF Off Jitter: 160 ± 10 nm
FF On Jitter: 106 ± 10 nm
FF Off Correlation: 73 %
Feedforward

## Slide 27
Neven Blaskovic Kraljevic 27
FF Off Jitter: 160 ± 10 nm
FF On Jitter: 106 ± 10 nm
FF Off Correlation: 73 %
FF On Correlation: 23 %
Feedforward

## Slide 28
Neven Blaskovic Kraljevic 28
Feedforward
6 μm incoming beam position scan
first bunch uncorrected
second bunch corrected

## Slide 29
P3
P2
K2
K1
Neven Blaskovic Kraljevic 29
Processor
Processor
Amplifier
Amplifier
Amplifier
Processor
Board
Board
IPK
IPB
Interaction Point Feedback
IPB position is used to drive the local kicker IPK
Latency: 212 ns
Effect measured at IPB

## Slide 30
Neven Blaskovic Kraljevic 30
FB Off Jitter: 168 ± 7 nm
FB On Jitter: 98 ± 5 nm
FB Off Correlation: 81 %
Interaction Point Feedback

## Slide 31
Neven Blaskovic Kraljevic 31
FB Off Jitter: 168 ± 7 nm
FB On Jitter: 98 ± 5 nm
FB Off Correlation: 81 %
FB On Correlation: -16 %
Interaction Point Feedback

## Slide 32
Neven Blaskovic Kraljevic 32
Interaction Point Feedback
10 μm incoming beam position scan
first bunch uncorrected
second bunch corrected

## Slide 33
Conclusion
Neven Blaskovic Kraljevic 33
Demonstrated low-latency, high-precision, intra-train feedback systems
Cavity BPM feedback latency: 212 ns
Achieved beam stabilisation at the ATF IP in 2 modes:
  Feedforward: ~100 nm
  IP feedback: ~100 nm

## Slide 34: Thank you for your attention!
Neven Blaskovic Kraljevic 34
We thank the ATF collaboration and the ATF operations team for their support

## Slide 35
Ground Motion vs. Frequency
Neven Blaskovic Kraljevic 35
Vertical ground motion power spectral density integrated up from a range of cut-off frequencies to give the RMS ground motion as a function of frequency
R. Amirikas et al.

## Slide 36
Monopole and Dipole Cavity Modes
Neven Blaskovic Kraljevic 36
Y. Inoue et al.
Monopole mode
TMrφz = TM010
Dipole mode
TMrφz = TM110
Electric field position independent
Electric field proportional to position

## Slide 37
IPK
IPB
Neven Blaskovic Kraljevic 37
P3
Processor
P2
Processor
K2
Amplifier
Amplifier
K1
Amplifier
Processor
Board
Board
Coupled-loop feedback system allows correction of both position & angle
Latency: 134 ns
Effect measured at IPB, located 60 meters downstream from P3
Upstream Feedback

## Slide 38
Neven Blaskovic Kraljevic 38
FB Off Jitter: 0.35 ± 0.02 μm
FB On Jitter: 0.30 ± 0.01 μm
FB Off Correlation: 79 %
Upstream Feedback

## Slide 39
Neven Blaskovic Kraljevic 39
FB Off Jitter: 0.35 ± 0.02 μm
FB On Jitter: 0.30 ± 0.01 μm
FB Off Correlation: 79 %
FB On Correlation: 14 %
Upstream Feedback

## Slide 40
Neven Blaskovic Kraljevic 40
Interaction Point Feedback
first bunch uncorrected
second bunch corrected
Beam waist scan