## Slide 1: Effect of IPK at IPB
N. Blaskovic

## Slide 2: Contents
Effect of IPK at IPB in June 2012 (operating IPK from S-band hut)
Effect of IPK at IPB in January 2013 (operating IPK via the feedforward cable)
Effect of IPK at IPB in June 2014 (operating IPK with a local board at the IP) with effective bunch spacing of:
  116 buckets
  77 buckets
N. Blaskovic

## Slide 3
N. Blaskovic
Our first tests using the IPK kicker in June 2012 showed that we could obtain a kick of ± 7 um at IPB
12 June 2012 FONT Twiki

## Slide 4
N. Blaskovic
Our next tests using the IPK kicker in June 2012 showed that we could obtain a kick in excess of ± 10 um at IPB
15 June 2012 ATF Operation Meeting report, by Doug

## Slide 5
N. Blaskovic
In January 2013, we used to get -0.007 um/DAC kick and a linear range from -1000 to 1000 DAC counts

## Slide 6
N. Blaskovic
Now in June 2014 with a bunch 1 strobe 116 samples before the bunch, we have a linear range much smaller than -1000 to 1000 DAC

## Slide 7
N. Blaskovic
Now in June 2014 with a bunch 1 strobe 116 samples before the bunch, we have a linear range much smaller than -1000 to 1000 DAC but a larger effect with -0.012 um/DAC in the linear range

## Slide 8
N. Blaskovic
Now in June 2014 with 77 bucket bunch spacing, the linear range is still smaller than -1000 to 1000 DAC counts and the kicker’s effect is reduced to -0.008 um/DAC in the linear range
IPKcal1 on 190614, from Doug

## Slide 9: Conclusions
Shorter bunch spacing may yield weaker um/DAC kick (slides 7 & 8)
Kicker saturation appears at lower DAC settings when IPK driven by local board compared to when driven from S-band hut or via feedforward cable (slides 3, 5 & 6)
The maximum kick of IPK at IPB was in excess of ± 10 um in June 2012, but only ± 7 um in June 2014 (slides 4 & 6)
N. Blaskovic