## Slide 1: Feed forward orbit corrections for the CLIC RTML
R. Apsimon, A. Latina

## Slide 2: Motivation
Emittance growth from betatron collimation
  Strongly dependent on orbit jitter in collimators
Damping ring extraction stability
  Kicker and septa stability extremely stringent
  FF systems relax requirements

## Slide 3: RTML FF systems
EC1: first energy collimator system
EC2: second energy collimator system
BC: betatron collimation system
eFF1: first feed forward system in electron RTML
eFF2: second feed forward system in electron RTML
pFF1: first feed forward system in positron RTML
pFF2: second feed forward system in positron RTML

## Slide 4: Design considerations
Hardware:
  BPM design, resolution and signal processing
  Transmission cable speed and latency budget
  Kicker design and stability
  Digital feed forward electronics
  Machine protection
Optics
  Optics designs of BPM and kicker regions

## Slide 5: BPM design
Use stripline BPMs for high bandwidth and
reasonably low resolution.
Position
where and are the difference and sum
of opposing stripline signals.
Resolution
Where is the gain ratio between difference and sum channels on the digital electronics, is the electrical noise on the BPM system and R is the BPM resolution.
FONT BPMs consistently achieve resolutions ~1.6 times thermal limit of noise.
CLIC RTML BPMs aim for ~1.3 times thermal limit by digitising BPM signals immediately after analogue processing. RTML BPM radius is 6 cm, so expect resolutions ~ 1.4μm

## Slide 6: Transmission speed
A minimum timing latency, to allow for calculation of FF corrections
pFF2 and eFF2 layouts very similar, very small horizontal offset of beam after turnaround.
Beam travels ~1600 m, signals travel ~50 m.
Required cable speed: ~0.03c Extremely easy to achieve with any transmission cable
eFF1:
Horizontal offset after turnaround ~ 610 m
Minimum cable speed:
Where ρ is the radius of curvature of the central arc
Use high speed (~0.88c), low attenuation (~6dB over 600 m) cables to maximise latency:
e.g. LDF4.5-20
pFF1:S-shaped chicane
Minimum cable speed:
Use free space optical communication: send IR signals between BPM and kicker regions

## Slide 7: Kicker design
Feed forward systems should be capable of orbit corrections of
Use electrostatic kickers:
Fast rise and fall times (~5 ns)
Relatively weak so good for small and precise corrections
Stripline voltage:
Where d is the stripline separation (12 cm), pc is the beam momentum (9 GeV) and L is the kicker length (~1 m)
Kicker voltage = ±220V horizontally and ±70V vertically.
A kicker stability of ~1% will result in ~0.01% increase in jitter compared to expected BPM resolution.
Systematic effects (e.g. field homogeneity) can be calibrated out
Very relaxed kicker stability requirements

## Slide 8: Digital feed forward electronics
Latency of digital electronics expected to be similar to that of the FONT digital electronics, ~50 ns.
Total latency budget is ≥ 150 ns
Use remaining budget for additional features:
FF systems can only correct orbit jitter ≤0.5 σ, so use BPM measurements to determine when beam is dangerously off-orbit and fire a downstream dump kicker.
Systematic correction of oscillations on bunch train with tuneable analogue ripple on kicker pulses.

## Slide 9: Machine protection
A safe beam determination algorithm can be run in parallel to the normal feed forward correction algorithm.
The safe beam determination can be performed in ~ 5 – 10 ns and a beam dump trigger sent to the dump kicker.
As the dump kicker will be more powerful than the feed forward kickers it will require a longer rise time, thus a dump signal should be sent a quickly as possible.
Given the beam optics described in the next slides, the beam positions in the two feed forward BPMs can be used to determine a safe beam condition by :

## Slide 10: Optics considerations
In normalised coordinates, the sensitivity of a phase space measurement can be expressed in terms of the optics and BPM resolution:
The second term vanishes when or an odd multiple. The first term is minimised when according to the arithmetic to geometric mean inequality theorem.
Converting back into normal phase space it can be shown that
In conclusion: need a periodic lattice between BPMs
Use 90o FODO cells for the BPM and kicker regions.

## Slide 11: Tracking simulations
3 studies undertaken:
Ideal system
  Comparison of beam stability through RTML with and without feed forward corrections
    Perfect BPM resolution and alignment
    Initial beam offset at start of RTML varied to simulate DR extraction errors
Precision study
  Impact of BPM resolution of feed forward performance
    Perfect BPM alignment
    Initial beam offset at start of RTML varied to simulate DR extraction errors
Accuracy study
  Impact of BPM alignment errors on feed forward performance
    Perfect BPM resolution
    Perfectly extracted beam at start of RTML

## Slide 12: Tracking results: Ideal system

## Slide 13: Tracking results: Precision study

## Slide 14: Tracking results: Accuracy study

## Slide 15: Tracking results: Ideal system

## Slide 16: Tracking results: Precision study

## Slide 17: Tracking results: Ideal system

## Slide 18: Tracking results: Precision study

## Slide 19: Tracking results: Accuracy study

## Slide 20: Tracking results: Ideal system

## Slide 21: Tracking results: Precision study

## Slide 22: Summary of tracking results
Horizontal emittance growth:
Factor 0f ~4 reduction in emittance growth
1-2 μm resolution has a negligible effect on FF performance compared to perfect BPMs
~ ±10 μm alignment tolerance required
Horizontal jitter amplification:
Factor of ~7.5 reduction in jitter amplification
1-2 μm resolution has a negligible effect on FF performance compared to perfect BPMs
Vertical emittance growth:
Factor of ~1.5 reduction in emittance growth
1-2 μm resolution has a tolerable effect on FF performance compared to perfect BPMs
~ ±2-5 μm alignment tolerance required
Vertical jitter amplification:
Factor of ~6 reduction in jitter amplification
1-2 μm resolution has a negligible effect on FF performance compared to perfect BPMs

## Slide 23: Conclusions
The design of the feed forward hardware has been based on existing technology and the required performance has been experimentally demonstrated (FONT feedback system at ATF2); thus confirming the feasibility of the system.
The optics of the BPM and kicker regions have been studied analytically to ensure a global optimisation.
Tracking simulations have shown a good performance of the feed forward systems, including resolution and misalignment errors.