## Slide 1: CTF3 Latency

## Slide 2: Signals – without driving amps

## Slide 3: Original latency estimates
By putting out constant signal (2000 cnts) on DACs coinciding with the duration of the beam pulse, measured the offset between the correction signal on the monitors and the beam-induced pick-up.
Kicker480 (u/s): -8.4 ns (-3 cycles) ~1.7 m
Kicker780 (d/s): +30.8 ns (+11 cycles) ~6.2 m
Time difference between kicker pickup = 36.4 ns = 10.9m between the kickers (agrees with model)

## Slide 4: Latency breakdown
Based on most recent measurements/estimates:
  TOF PhM -> TL2 : 380 ns
  Kicker cables : 210 ns (TDR)
  Phase monitor electronics + cables : 50 ns (?)
  Leaves ~ 120 ns for FPGA + amplifiers
  Estimate: FPGA (20 clock cycles : ~67 ns), Amplifier (27 – 35 ns), ~20 ns slack

## Slide 5: Detailed Latency (1)
Driving amps with 200 cnts
  (8% full kick)
  Arbitrary timing
Rise of signal (312-318) 316
  16.8 ns RT
Beam induced pickup: 508 -516 (peak @ 511)
  8.4 ns RT
195 samples = 546 – 380 = 166 ns
Roughly consistent with 210 – 50 =160 ns

## Slide 6: Detailed Latency (2)
Drive output timing : 201 – 216 (206)
Constant drive output at T(10) cf 316 (PhM rise)
Sample 206+306= 512
Therefore output would have risen to 80% at T(512), cf beam pickup at T(511)
Present timing very marginal.

## Slide 7: Firmware Latency
Full simulation of (pseudo)-top level and below for timing verification

## Slide 13: Firmware Latency
Simulated latency:
  22.5 cycles : ~63 ns @ 2.8 ns
    FPGA logic: up to 18 cycles
      input/output buffer x2
      input/output filtering (latency 3) x2
      BRAM lookup (latency 2)
      Mults (latency 2) x2
      Shift register (latency 2)
      Pipelining x2
    ADCs : 3.5 cycles + DAC timing (~ 1 cycle) + up to 1 cycle for synchronising
Measured latency
  63.6 ns (@2.8ns) includes 2 times 0.5m RG58
  60.4 ns without extra cables (! ? !)
Final timings will need tuning; aim to use minimum pipeling necessary to run as fast as possible (up to 400 MHz) providing there is enough slack.
  Lump all slack into the shift registers!!