## Slide 1: Kicker Cable Length Measurements
Jack Roberts,
Alex Rollings, Joe Taylor,

## Slide 2: Overview
Observed around a 8 ns latency deficit for the first kicker, 31 ns slack for first kicker (beam time of flight difference).
Cables for first kicker have been shortened (and rerouted) by around 30 ns or 6 m to bring latency in budget.
Joe and Alex took cable length measurements before and after the cables were cut.

## Slide 3: Short Version:
 | Cable Label | End | Side | Old Length (ns) | New Length (ns)
Upstream/ 1st Kicker (480) | 2907700 | Upstream | Left | 206.0 ± 0.3 | 170.9 ± 0.3
 | 2907701 | Upstream | Right | 206.0 ± 0.4 | 171.3 ± 0.3
 | 2907702 | Downstream | Left | 205.8 ± 0.4 | 171.2 ± 0.3
 | 2907703 | Downstream | Right | 205.4 ± 0.4 | 171.6 ± 0.3
Downstream/ 2nd Kicker (780) | 2907838 | Upstream | Left | 211.2 ± 0.4 | 204.3 ± 0.3
 | 2907839 | Upstream | Right | 210.5 ± 0.3 | 205.2 ± 0.3
 | 2907840 | Downstream | Left | 211.3 ± 0.4 | 205.4 ± 0.3
 | 2907841 | Downstream | Right | 209.8 ± 0.4 | 204.3 ± 0.3
Different data analysis technique used.
Using old approach with new data:
  Lengths for 2nd kicker agree to 0.8 ± 0.2 ns between data sets.
  Cables for first kicker shortened by 28.9 ± 0.3 ns.
How well matched do the lengths need to be (1 ns ~= 20 cm)?

## Slide 4: Equipment Setup
SCOPE
PULSE
GENERATOR
10 ns
10 ns
10 ns
KICKER CABLE
SPLITTER
L
Δt
TIME
SIGNAL
Δt
TIME
SIGNAL
Signal as seen on scope:
Two signal components:

## Slide 5: Data Before Cable Cutting
Noise level
4σ above noise
Noise level
4σ above noise
1 point every 0.4 ns.
Strange oscillations in signal.
Width 1st slope ~40 ns, width 2nd slope ~30 ns
Δt

## Slide 6: 1st Kicker, Before Cable Cutting

## Slide 7: 2nd Kicker, Before Cable Cutting

## Slide 8: New Edge Detection Method
If each slope is well defined by the Gauss error function, the differential of the slope is a Gaussian with peak at the mid-point of the slope.

## Slide 9: Data Before Cable Cutting
Peaks not visible outside the noise of the difference.

## Slide 10: Data After Cable Cutting: 1st Kicker
LeCroy (FONT owned) scope: 2 ns between points.
Peaks visible in the difference, Gaussian fits shown.
Width 1st slope ~40 ns, width 2nd slope ~30 ns.
Δt
Δt

## Slide 11: Data After Cable Cutting: 2nd Kicker
LeCroy (FONT owned) scope: 2 ns between points.
Peaks visible in the difference, Gaussian fits shown.
Width 1st slope ~40 ns, width 2nd slope ~30 ns.
Δt
Δt

## Slide 12: Example Fits

## Slide 13: 1st Kicker, After Cable Cutting

## Slide 14: 2nd Kicker, After Cable Cutting

## Slide 15: Lengths:
 | Cable Label | End | Side | Old Length (ns) | New Length (ns)
Upstream/ 1st Kicker (480) | 2907700 | Upstream | Left | 206.0 ± 0.3 | 170.9 ± 0.3
 | 2907701 | Upstream | Right | 206.0 ± 0.4 | 171.3 ± 0.3
 | 2907702 | Downstream | Left | 205.8 ± 0.4 | 171.2 ± 0.3
 | 2907703 | Downstream | Right | 205.4 ± 0.4 | 171.6 ± 0.3
Downstream/ 2nd Kicker (780) | 2907838 | Upstream | Left | 211.2 ± 0.4 | 204.3 ± 0.3
 | 2907839 | Upstream | Right | 210.5 ± 0.3 | 205.2 ± 0.3
 | 2907840 | Downstream | Left | 211.3 ± 0.4 | 205.4 ± 0.3
 | 2907841 | Downstream | Right | 209.8 ± 0.4 | 204.3 ± 0.3
Different data analysis technique used.
Using old approach with new data:
  Lengths for 2nd kicker agree to 0.8 ± 0.2 ns between data sets.
  Cables for first kicker shortened by 28.9 ± 0.3 ns.
How well matched do the lengths need to be (1 ns ~= 20 cm)?