## Slide 1: Plans for Data Acquisition from the FONT5 Board at CTF3
Jack Roberts

## Slide 2: Setup used so far
FONT5 Board
LabVIEW
DAQ
PC in Klystron Gallery
RS232
RS232
Data
FESA
CERN Control System
MatLab
Data
PC in Control Room
FEC
(Front End Computer)
CTF3 Device

## Slide 3: Setup used so far
No communication between FONT5 board and CERN control system. Data saved separately and combined later in analysis.
CTF3 Devices we need to control/acquire from:
  Phase shifters
  BPMs
  Magnet/corrector currents
  PETS phase / other phase monitors
Difficult to quickly get information on performance of phase feedforward system.
Possible to be saving data in one place and not the other.

## Slide 4
CERN Control System
MatLab
Data
PC in Control Room
FONT5 Board
LabVIEW
DAQ
PC in Klystron Gallery
RS232
RS232
Data
Shared variables
FESA
IEPLC
Ethernet
Ethernet
FEC
(Front End Computer)
FESA
FEC
(Front End Computer)
CTF3 Device
Proposed Setup

## Slide 5: Proposed Setup
Communication between the FONT5 board and the CERN control system via IEPLC:
  Provides tools and infrastructure to interface between LabVIEW and FESA via LabVIEW shared variables.
FONT5 data can then be acquired (and parameters can be set) from the CERN control system via MatLab in the normal way.

## Slide 6: Work Required: CERN Infrastructure
IEPLC Class: Definition of variables to be shared. Made via graphical tool.
IEPLC Mapping Document: Information about FEC the IEPLC class will be deployed on. Also made via graphical tool.
FESA Class: Communication between IEPLC and the control system. Barebones class generated by IEPLC but may need to add details to it.
Front End Computer (FEC): All the above needs to run on a FEC (Linux PC).
I’ve started to look in to this – aiming to transmit data to the control system from a basic LabVIEW VI (random number generator).

## Slide 7: Work Required: FONT5 Infrastructure
Identify which parameters/variables in the DAQ need to be shared:
  Simplest first iteration: ADCs, DACs, feedforward on/off.
  What’s shared with EPICS at ATF?
Add shared variables to DAQ and set them up in the required way to interface with IEPLC:
  Tool available to create the variables from the IEPLC class.
Add a BPM/some other CTF device in to the FONT5 DAQ to make synchronisation between FONT data and CTF data easier (RADE).
Will need a FONT5 board for testing at CERN after I’ve managed to get IEPLC working with the simple test system.

## Slide 8: Links
IEPLC (acquire/set LabVIEW variables via control system): http://wwwpsco/private/ieplc/www/home/
RADE (acquire/set CERN devices in LabVIEW): https://j2eeps.cern.ch/wikis/display/EN/RADE
FESA (normal interface between devices and control system): https://wikis.cern.ch/display/FESA3/Project