## Slide 1: Chip Developments of the Bonn Group
Hans Krüger, Bonn University

## Slide 2: ASIC Design Projects
ATLAS Pixel Detector
  Hybrid pixel sensors
    FE-I3 (250nm, current pixel detector)
    FE-I4 (130nm, Insertable B-layer, current upgrade)  done
    FE-x (65nm, future HL upgrade, RD53 collaboration)  work just started
  Fully depleted Active CMOS Sensors (DMAPS)
    Commercial CMOS technology for the sensing layer, monolithic or hybrid  HL upgrade option
Belle II Pixel Vertex Detector (SuperKEKB e+ / e- collider)
  Digital signal processing on pixel module (65nm, DHP chip)  (alomost) done
    1.6GHz PLL
    High speed serial links
    High density digital signal processing
    Low power, high density 10 Msps 8-bit ADC
X-ray imaging (low energy, synchrotron light sources, X-FEL)
  AGIPD (130nm hybrid pixel detector, XFEL@DESY)
  New developments: monolithic or hybrid with active CMOS sensors

## Slide 3: 65nm CMOS Design Activities – Belle II
Projects
DEPFET Pixel Vertex Detector for BELLE II (2015) Data handling processor (DHP), mainly digital design, including full custom blocks:
  PLL (1.6 GHz)
  High speed serial link (1.6 Gbps)
  LVDS IO
„Generic“ (future pixel chips)
  Low power analog front-end (CSA + discr.)
  Low power, small area ADC
  SEU test structures
Chip submissions
DHPT 0.1, four chiplets, Oct. 2011
DHPT 0.2, four chiplets, June 2012
DHPT 1.0
  14 mm2 MPW
  C4 bumps

## Slide 4: Chip Design Activites – RD53
Focused on 65nm CMOS technology for HL pixel detector upgrades
Joint CMS/ATLAS (+CLIC) development
RD53 collaboration recommended by LHCC June 2013
  Institutes: 17 (+ 3 new applicants)
    ATLAS: CERN, Bonn, CPPM, LBNL, LPNHE Paris, NIKHEF, New Mexico, RAL, UC Santa Cruz.
    CMS: Bari, Bergamo-Pavia, CERN, Fermilab, Padova, Perugia, Pisa, PSI, RAL, Torino.
  Collaborators: ~100, ~50% chip designers
  Initial work program covers ~3 years to make foundation for final pixel chips
  Co-spokes persons: ATLAS: M. Garcia-Sciveres, LBNL. CMS: J. Christiansen, CERN
RD53 web: www.cern.ch/RD53/

## Slide 5: RD53 Working Groups

## Slide 6
Backup

## Slide 7: PLL & High Speed Link Driver
PLL
  80 MHz reference clock
  1.6 GHz, 800MHz & 320 MHz outputs
Pseudo random bit sequence generator (8 bit LFSR)
Current mode logic (CML) driver
  Programmable pre-emphasis (first order FIR filter)
  Two differential pairs with adj. bias currents (tap weights a, b)
  Programmable delay dt
PLL_CML Test Chip,
T. Kishishita
I0
1.6 GHz
TX1_P
50 
50 
TX1_N
pre drv.
I1
del
PLL
LFSR
80 MHz
2
dt
a
b
CML driver
800 MHz
320 MHz
320 MHz
TXO_P
TXO_N
CML driver

## Slide 8
LPF
CP
PFD
VCO
DIV
140um
55um
Layouts
T. Kishishita
75 µm
105 µm
Decoupl. C
Predriver circuit
poly-res. with dummy structures
PLL
CML driver

## Slide 9: Gbit Link Test Setup
TWP cable, 10 (20) m
Flex cable, 38cm
DHPT 0.1
Signal Integrity Analysis

## Slide 10: Signal Integrity Analysis
1.6 Gbps, 8bit LFSR sequence
10m Infiniband cable (LEONI, AWG 26)
Preemphasis off
Preemphasis on (600ps, max. Iboost)
400 mV
600 mV

## Slide 11: Low Power ADC
8bit ADC
  10 Msps
  Charge redistribution
Asynchronous operation  low power
  No clock distribution needed
  Sample signal triggers digitization sequence
Serial LVDS data out
T. Hemperek, T. Kisisita
Function Diagram
Asynchronous ADC timing

## Slide 12: ADC Layout
Folded DAC
40 um
70um
DAC
Straight DAC
30 um
120 um
DAC
ADC area dominated by DAC
Switched capacitor DAC layout critical for DNL performance
8 bit  7 bit: half size

## Slide 13: Asynchronous ADC Measurements
Measured at 10 MHz sample rate
Power consumption: ~40uW
Works up to 12.5 Msps
Single Ended Mode
Differential Mode