## Slide 1: Progress on effort towards integrating FONT5 board with CERN control system.
Jack Roberts

## Slide 2: Summary
Progress has been slow but there has been progress.
Involves work on three different systems (LabVIEW, IEPLC and FESA), all of which have different support groups at CERN based at Prevessin, and none of which I have much experience in.
I’m maybe two thirds through getting my test setup finished and working.

## Slide 3: Test Setup Progress
Make LabVIEW test setup
  Simple looped random number generator.
Make IEPLC class document
  Defines names and access mode of parameters to be shared.
Make IEPLC mapping document
  Defines setup of the PC that LabVIEW is running on.
Import shared variables in to LabVIEW.
  IEPLC tool to do this. Shared variables only work in Windows!
Integrate shared variables in to pre-existing VIs.
  May require a lot of thought/effort for FONT DAQ.
Test connection to shared variables using IEPLC diagnostic tool.
  Had some firewall and variable initialisation issues but now working.
GREEN = done
RED = still to do

## Slide 4: Test Setup Progress
Generate FESA source files from IEPLC tool.
  FESA is the architecture for communicating between hardware and the control system.
Create FESA class in Eclipse environment using generated files from IEPLC.
  Some changes have to be made by hand from barebones class generated by IEPLC. Finally got it to compile yesterday.
Create FESA device instance.
  Definition of FEC, devices that will be deployed.
Create FESA deploy unit.
  Executable to be run on FEC.
Deploy FESA class on FEC.
Test connection to FEC/LabVIEW shared variables using FESA diagnostic tool.

## Slide 5: Test Setup Progress
Register FESA class in database?
  I think this is necessary for the Java/MatLab tools to be able to communicate with the FESA class.
Test acquisition/settings of LabVIEW shared variables through control system using normal MatLab tools.

## Slide 6: Implementation in FONT Board
I talked to LabVIEW support at CERN yesterday.
Their suggestion was to completely remake the DAQ in a more modular way (!).
Would like to avoid that in the short term but even the minimal effort option will require quite a lot of thought to work out how to integrate everything.