## Slide 1: Digital Hadron Calorimetry using Gas Electron Multipliers
Andy White
University of Texas at Arlington

## Slide 2
Overview
GEM/DHCAL basics
Review of GEM/DHCAL developments
Results to date
Plans
ThickGEM/DHCAL
THGEM structures
Recent results/CERN test beam
Digital Hadron Calorimetry using Gas Electron Multipliers

## Slide 3
GEM-based Digital Calorimeter Concept
Use Double GEM layers to minimize gap size
{
~6.5mm
-2100V
∆V ~400V
∆V ~400V
0V
NmaxE0

## Slide 4: 30x30 prototype GEM chamber and Readout Electronics
Readout systems
Chamber
GEM Foils(3M)
310x310 mm2
Active area : 280x280 mm2
Active gas volume
350x350x6 mm3
 For 3/1/1 gaps
KPiX readout system/SLAC
  13 bit resolution(ADC)
  Handles 1024 channels/chip,
  3 gain ranges
  Normal gain
Readout channels: KPIX(64), DCAL(256)
64-readout pads(KPIX)
Pad board
FE board
DCAL readout system/ANL
  1 bit resolution(ADC)
  64 channels/chip
  2 gain ranges
  High gain for GEMs (10 fC~200 fC signals)
  Low gain for RPCs (100 fC~10 pC signals)

## Slide 5
KPiX FPGA board
KPiX Interface board
UTA GEM-DHCAL Cosmic Test Stand
KPIX chamber
DCAL chamber 2
DCAL chamber 1
Trg counter1
Trg Counter2

## Slide 6: GEM+KPiX7 Fe55 and Ru106 Spectra
Fe55
Ru106
Good conformation to characteristic Minimum Ionizing Landau fit

## Slide 7: HV=1950V, Fe55, ST=1.8V=14 fC
7
2009_11_18_10_20_49

## Slide 8
Pressure Dependence of Gain

## Slide 9
Red: 2012, blue: 2013, green:2014
Study the seasonal change of GEM detector gain.
Days
Mean signal (fC)
Yvonne Ng – UTA Student

## Slide 10
T-1010 Experiment Setup

## Slide 11
Particle: Muon
High Voltage: 1950V
Energy: 32 GeV
Trigger: 10x10cm2
Particle: Proton
High Voltage: 1950V
Energy: 120 GeV
Trigger: 2x2cm2
Particle: Pion
High Voltage: 1950V
Energy: 32 GeV
Trigger: 2x2cm2
GEM Response with KPiX
Results pressure corrected

## Slide 12: Hit Map for Pions vs Pion Showers (KPiX)
Hits above 5fC were counted and normalized to 1000
Demonstrates the KPIX capability to take many hits simultaneously

## Slide 13
Efficiencies and Hit multiplicities (KPiX)
Results pressure corrected

## Slide 14: Toward 100cmx100cm GEM Planes
GEM DHCAL A.White
Each of the GEM 100cmx100cm planes will consist of three 33cmx100cm unit chambers

## Slide 15: Toward 100cmx100cm GEM Planes!!
GEM DHCAL A.White
Two 33cmx100cm chamber parts delivered
Class 10,000 clean room (12’x8’) construction completed
Jig for 33cmx100cm chamber being procured
Assembly jig
Anode
Spacer
GEM Foil
Positioners
Positioners

## Slide 16: Preparation for LGEM Assembly
Current situation:
Waiting resumption of detector R&D support
Characteristics of GEM chambers (Eff. vs. mult, long term stability) show suitability fro DHCAL application.
Next:
Complete one 33cm x 100cm chamber
Test chamber in lab
Build two more chambers
Beam test with KPiX/synchronous beam at SLAC ESTB

## Slide 17
DHCAL – Thick GEM
2012 JINST 7 C05011
RPWELL
ThickGEM technology developed at Weizmann Institute of Science, Israel
Tested in collaboration with Portugal (Aveiro, Coimbra), US(SLAC,UTA)
Slides courtesy Dr. Shikma Bressler (WIS)
From very recent CERN test beam

## Slide 19
RPWELL
THGEM “preamp” to mimic HIPs

## Slide 20
Laboratory studies with X-Rays
103
104

## Slide 21
Laboratory studies with X-Rays

## Slide 22
Before CERN shutdown

## Slide 23
μ
π

## Slide 28
DHCAL – Thick GEM

## Slide 29
DHCAL – Thick GEM technology
ThickGEM
Single; 5.9 mm
Single; 5.8 mm
Double; 6.3 mm
Double; 5.3 mm
Double; 4.8 mm
The DHCAL requirements were met
Build meter-scale single-stage detector
One prototype in collaboration with Israeli industry
Prototype(s) to test within CALICE’s DHCAL module
Study extensively THGEM concepts with broader dynamic range
RPWELL
Using newly developed techniques
Test in beam of 100 x 100 mm2 prototype
Rubin 2013 JINST 8 P11004
Bressler 2014 JINST 9 P03005
(Near) future plans

## Slide 30
EXTRA

## Slide 31
HV power
Analog signal
Gas outlet
LV power
Data cable
Top side
Fe55 Source Signal
1 cm2 anode pads

## Slide 32: KPiX Readout scheme (SLAC)
Amplifier
Calibration circuit
Shaper
Trigger logic
Storage buffers
ADC
ADC/fC
DHCAL anode pad
4-deep
“pipeline”
Notes: 32

## Slide 33: T-1010 Experiment Setup
GEM6: Read out by 13bit KPiX designed for the ILC time line
GEM7, GEM5, GEM4: Read out by 1bit DCAL chip by ANL and FNAL
GIA: Medical image intensifier prototype with 12 bit ADC in-house readout
Triggers formed off the motion table:
10x10 coincidences for guaranteed beam penetration through the detector array
2x3 coincidences arranged perpendicular to each other for 2x2 coverage in the center of the detector array
Coincidence of 1*2: Guaranteed beam penetration with center 2x2 coverage (efficiency ~95%)
GEM7
GEM6
GEM5
GEM4
10x10
2x3 V
10x10
2x3 H
GIA
GEM7
GEM6
GEM5
GEM4
10x10
2x3 V
10x10
2x3 H
GIA

## Slide 34
Base steel plate, t=2 mm
Readout Board
320x500 mm2
320 mm
1000 mm
33cmx100cm DHCAL Unit Chamber Construction
1mm pad board
2mm FE board
1mm assister strong back
2mm steel strong-back + thin cathode layer
3mm
1mm
1mm
G10 spacers will be used without aligned dead areas.
Readout boards will be glued in the seam
Readout boards are part of the gas volume!!
GEM foils with 31 HV strips delivered

## Slide 36
RPWELL with thinner Semitron layer has improved rate performance