## Slide 1: Progress towards nanometre-level beam stabilisation at ATF2
N. Blaskovic, D. R. Bett, P. N. Burrows, G. B. Christian, C. Perry
John Adams Institute, University of Oxford

## Slide 2
Outline
Neven Blaskovic 2
Introduction
  Feedback at a linear collider
  International Linear Collider
  Feedback on Nanosecond Timescales
Experimental setup at Accelerator Test Facility
Position jitter on waist
Interaction point feedback results

## Slide 3
Introduction
Feedback at a Linear Collider
Neven Blaskovic 3
Successful collision of bunches at a linear collider is critical
A fast position feedback system is required
Misaligned beams at interaction point (IP) cause beam-beam deflection

## Slide 4
Neven Blaskovic 4
Successful collision of bunches at a linear collider is critical
A fast position feedback system is required
Introduction
Feedback at a Linear Collider
Misaligned beams at interaction point (IP) cause beam-beam deflection
Measure deflection on one of outgoing beams
(beam position monitor)

## Slide 5
Neven Blaskovic 5
Successful collision of bunches at a linear collider is critical
A fast position feedback system is required
Misaligned beams at interaction point (IP) cause beam-beam deflection
Measure deflection on one of outgoing beams
Correct orbit of next bunch (correlated to previous bunch due to short bunch spacing)
(beam position monitor)
Introduction
Feedback at a Linear Collider

## Slide 6
Introduction
International Linear Collider (ILC)
Neven Blaskovic 6
Proposed linear electron-positron collider
Centre-of-mass energy: 250-1000 GeV
Vertical beamsize: 5.9 nm
Bunch separation: 554 ns
(ILC Technical Design Report)

## Slide 7
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic 7
Test bed for the International Linear Collider
Facility located at KEK in Tsukuba, Japan
Goals of the present accelerator (ATF2):
  37 nm vertical spot size at final focus
  Nanometre level vertical beam stability

## Slide 8
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic 8
Electron source
90 meters

## Slide 9
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic 9
1.28 GeV linear accelerator
Electron source
90 meters

## Slide 10
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic 10
Damping ring
Electron source
1.28 GeV linear accelerator
90 meters

## Slide 11
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic 11
Damping ring
Electron source
Extraction line
Final focus
Model interaction point (IP) of a collider (location of feedback system)
1.28 GeV linear accelerator
90 meters

## Slide 12
Introduction
Accelerator Test Facility (ATF) at KEK
Neven Blaskovic 12
ATF can be operated with 2-bunch trains in the extraction line and final focus
The separation of the bunches is ILC-like (tuneable up to ~300 ns)
Our prototype feedback system:
  Measures the position of the first bunch
  Then corrects the path of the second bunch
Train extraction frequency: ~3 Hz

## Slide 13
Introduction
Feedback on Nanosecond Timescales (FONT)
Neven Blaskovic 13
Low-latency, high-precision feedback system
We have previously demonstrated a system meeting ILC latency, BPM resolution and beam kick requirements
We have extended the system for use at ATF
We aim for nanometre level beam stabilisation at the ATF IP

## Slide 14
Neven Blaskovic 14
IPB
Cavity BPM at beam waist
C-band: 6.4 GHz in y
Low Q: decay time < 30 ns
Resolve 2-bunch trains
Experimental Setup
IPB
beam

## Slide 15
Neven Blaskovic 15
for cavity BPM
Analogue, 2-stage downmixer
Resolution of < 80 nm
Developed by Honda et al.
Processor
Experimental Setup
IPB
Processor
beam

## Slide 16
Neven Blaskovic 16
Board
9 ADC channels at 357 MHz
2 DAC channels at 179 MHz
Xilinx Virtex 5 FPGA
Experimental Setup
IPB
Processor
Board
beam

## Slide 17
Neven Blaskovic 17
Made by TMD Technologies
± 30 A drive current
35 ns rise time (90 % of peak)
Amplifier
Experimental Setup
Amplifier
IPB
Processor
Board
beam

## Slide 18
Neven Blaskovic 18
IPK
Amplifier
IPB
Processor
Board
Vertical stripline kicker
12.5 cm long strips for IPK
Just before IP chamber
IPK
Kicker
Experimental Setup
beam

## Slide 19
Neven Blaskovic 19
Position Jitter
Measured position jitter on waist ~ 75 nm

## Slide 20
Neven Blaskovic 20
Position Jitter
A few hours later, measured position jitter > 200 nm

## Slide 21
Neven Blaskovic 21
Position Jitter
Using a downstream BPM, the waist position was found to have drifted
Correcting for waist drift off-line recovers waist beam jitter ~ 75 nm

## Slide 22
Resolution
Neven Blaskovic 22
The ~75 nm measured jitter is an upper limit to the resolution of the BPM, for the single-point sampling used in the feedback firmware

## Slide 23
Off-line analysis shows that multi-sample averaging improves the resolution to under 40 nm
Resolution
Neven Blaskovic 23
The ~75 nm measured jitter is an upper limit to the resolution of the BPM, for the single-point sampling used in the feedback firmware

## Slide 24
Neven Blaskovic 24
Interaction Point Feedback
IPB position is used to drive the local kicker IPK
Latency: 212 ns
Effect measured at IPB
IPK
Amplifier
IPB
Processor
Board
beam

## Slide 25
Neven Blaskovic 25
Interaction Point Feedback

## Slide 26
Neven Blaskovic 26
Interaction Point Feedback

## Slide 27
Conclusions
Neven Blaskovic 27
Demonstrated low-latency, high-precision, intra-train feedback systems
Cavity BPM feedback latency: 212 ns
Cavity BPM resolution
  Single-point sampling: < 80 nm
  Multi-sample averaging: < 40 nm
Achieved beam stabilisation at the ATF IP, reducing the jitter to < 90 nm

## Slide 28: Thank you for your attention!
Neven Blaskovic 28

## Slide 29
Cavity BPM Signal Processing
Neven Blaskovic 29
Reference cavity
Monopole mode frequency (in y)
~6426 MHz
IPB cavity
Dipole mode frequency (in y)
~6426 MHz

## Slide 30
Neven Blaskovic 30
Cavity BPM Signal Processing
The IPB and reference cavity signals are downmixed using a common, external 5712 MHz local oscillator (LO)
simplified schematic

## Slide 31
Neven Blaskovic 31
Cavity BPM Signal Processing
The IPB signal is downmixed using the reference cavity signal as LO
The I and Q output signals at baseband are used to obtain the beam position
simplified schematic

## Slide 32
Neven Blaskovic 32
Methods to Improve Resolution
Using multi-sample averaging takes the measured jitter from ~75 nm to ~40 nm

## Slide 33
Neven Blaskovic 33
Methods to Improve Resolution
Removing correlation with bunch phase, charge and off-waist BPM takes the measured jitter from ~75 nm to ~50 nm and <40 nm with averaging

## Slide 34
Neven Blaskovic 34
Methods to Improve Resolution
Jitter (nm) | Remove correlation with | 
 | off-waist BPM | bunch phase, charge & off-waist BPM
Single-sample | 76 | 49
Multi-sample | 42 | 39
On-waist jitter measurement gives upper limit on BPM resolution
In green, the level of resolution used in feedback so far

## Slide 35
Ground Motion vs. Frequency
Neven Blaskovic 35
Vertical ground motion power spectral density integrated up from a range of cut-off frequencies to give the RMS ground motion as a function of frequency
R. Amirikas et al.

## Slide 36
Monopole and Dipole Cavity Modes
Neven Blaskovic 36
Y. Inoue et al.
Monopole mode
TMrφz = TM010
Dipole mode
TMrφz = TM110
Electric field position independent
Electric field proportional to position

## Slide 37
Neven Blaskovic 37
Interaction Point Feedback
first bunch uncorrected
second bunch corrected
Beam waist scan