Ecal activities at LAL
Roman Pöschl
CALICE Collaboration Meeting KEK/Japan – April 2015

---
Comments on Assembly
- In the following the assembly of (short) Ecal layers is documented
- These steps have been devlopped by the LAL team
    Julien Bonis, Patrick Cornebise, Alice Thiebault, Marco Fernandez
    (Consultation by Christian Bourgeois and Alexandre Gonnin)
   All steps allow assembly in a fully controled manner with very little human 'contact'
  with detector devices
- For the tests, training an ASU with false SiWafers was used
- Last test before assembly of 'real' ASUs

---
Assembly of SiW Ecal layers
Assembly bench in LAL Workshop

---
Assembly bench from a different angle

---
Steps of assembly
2. Picking PCB from delivery plate

---
Steps of assembly
3. Preparing the HV Kapton
Placing glue dots for connection SiWafer – HV Kapton
Proper grid of glue dots
Well controled paramters at well defined
spots

---
Steps of assembly
4. Placing and fixing

---
Steps of assembly
5. Adapter card alignment (applies also for further ASUs)

---
Steps of assembly
6.1 Interconnection – Placing the frame

---
Steps of assembly
6.2 Interconnection – Do the job
Interconnection in/on assembly bench
... following carefully studied specifications
Human being to be “replaced” by robotic procedure
(AIDA-2020)
- This part of the assembly has to be very carefully integrated into planning of detector design!!!

---
Steps of assembly
7. Polymerisation (Gluing PCB – HV Kapton)
Polymerisation for about 1/2 day at 40o C
(Check time with experts)
Layer remains in cradle during polymerisation

---
Steps of assembly
8. Finishing
Interconnection pair Adpater card/ASU
Connection of HV straps
Not shown: Placing of thermal copper drain and closing with Aluminum cover
Ready for use: a) Leakage current b) Tests with data

---
Comments
- All steps of assembly procedure have been exercised with an experimental model
- New w.r.t. FEV8 (2012)
  Four wafers, interconnection in mechanical structure
- Ready to receive and assemble 'real' layers
  Important step to stabilise effort at LAL (We are sitting at the end of the chain)
- Assembly of short layers takes about 1 day
   * including polymerisation => parallelisation
   * do not expect much longer for long layer (provided enough automatisation)
- AIDA-2020 will help to scrutinise procedure further
  - Further reduction of human intervention
  - Interconnection is maybe most delicate step that needs automatisation and
   monitoring (in particular in view of long slabs)

---
FEV8_COB
Produced by EOS Company South-Korea under supervision of SKKU/OMEGA/LAL
Metrology
Thickness ~1.1mm
Planarity not overwhelming 1,0mm et 1,4mm of bending
Still within industrial limits
Will be subject of discussion with EOS company next week

---
FEV8_COB – Chip bonding
Realised in CERN bonding lab
... but “Black Pad” problem observed
Successful bonding
Would influence long term reliability
  (to be discussed with EOS)

---
FEV8_COB – On test bench
High tech piece of paper
Integrated smoothly with existing hardware and current version of calicoes/pyrame software

---
Some impression of FEV8_COB tests
Signal r/o from ASICs
...
- Quick test series (More profound tests slowed down by funding “accident”)
- ASICs on PCBs react correctly to slow control commands
- Acquisition and readout works properly (Noise from channels)
- Problems with starting PreAmp for injected charge pulses (has been also observed for
   earlier production by Protechno and Exception)
   -> requires access to probes of SKIROC2 <- requires configuration through DAQ2 s/w

---
Summary and outlook
- LAL team is preparing for assembly of short layers
- Succesful exercise with experimental model of a layer
  Many different steps that have to be mastered!!!
  Experience will be input to further automatisation
  Assembly has to become integral part of detector design!
  LAL team is fragile but motivated and skillful!
- Continuing R&D on Chip on Board solution
  10 boards have been produced
  2 boards have been equipped with SKIROC2 ASICs by CERN
  Black Pad effect observed during bonding
  First tests on test bench are encouraging
  Observed issues need more profound debugging
  Will talk to PCB producer next week
  Will search for “All-Korean” solution
  (for on-Board and packed versions)

---
Backup