## Slide 1: The undulator based ILC positron source activities at ANL
Wei Gai
ANL/Tsinghua University
AWLC 15, KEK

## Slide 2: Beamline Lattice
New lattice design has been done to comply with the new layouts as follow.

## Slide 3: Existing (unsolved) Issues for Undulator based source
Beam dynamics, (OK)
Undulator (OK? Or @95%)
Target (heating and shocks)
  Good? No issues? No critical problems (97%), there is rooms for further improvements.
Target support vacuum chamber, test at LLNL.
  Life time of the vacuum seal (short time survival, but long term > a few weeks with vacuum spikes, no clear path forward at this point), no radiation damaging testing yet. , and
  Cooling water impact on wheel dynamics (simulation should be done).
  Rotating Seal leak tests at KEK planned.
  New ideas: Non-contact (differenetial pumping), support, radiation cooling. Many others (later in the talk).
OMD, (OK)
Accelerator (NC)
  SLAC test showed 14 MV/m.
Interfacing with damping ring (OK)

## Slide 4: Positron Source Spinning Wheel Target
Prototype has been built and tested for eddy current issue.
Vacuum seal test of supporting shaft was not very successful. The current prototype is not robust enough for production system.
Still need to demonstrate full wheel with cooling channel.
Not funded for further test and demonstration.

## Slide 5: Major Concerns on positron sources
Issues on moving forward on the current LLNL test.
  Approaches are still viable?
  Funding
  Technical support
Alternative target design for undulator sources
  Other type of targets
    Radiative cooling,
    Sliding cooling
    ….

## Slide 6: Remedies and benefits
Eliminate the need of rotating vacuum seal by putting the whole target system in vacuum chamber.
Eliminate the need of rotating water union and the complicated cooling channels in target wheel by using conduction cooling from spring loaded cooling pads
The eliminating of rotating vacuum seal problem will enable us to support the shaft on both ends without concerning the vacuum.
The eliminating of cooling channels in target wheel will simplify the target wheel design process and allows more freedom on optimization.

## Slide 7: Looking from outside, -A vacuum chamber without external drive except electrical and cooling water feed-throughs

## Slide 8: Inside the chamber
Target wheel, geometry may be optimized for cooling efficiency and wheel balance
Cooling pads and supporting structures
Magnetic bearing on both sides
Your text here
Cooling water manifolds are not showing.
Flux concentrator and accessories are not included in this conceptual illustration.

## Slide 9: Cross section view
Target wheel, geometry may be optimized for cooling efficiency and wheel balance
Cooling water manifolds are not showing.
Flux concentrator and accessories are not included in this conceptual illustration.
Magnetic bearing on both side
Vacuum compatible motor

## Slide 10: Vacuum compatible electrical motor
One needs to remember that magnetic motor does not require lubrication itself as long as bearings are lubricated correctly. We consider a motor drive that is oil free and maintenance free.
Through the web search, we found the MiTi®’s 32 kW, 60,000 rpm Oil-Free, High-Speed Motor.

## Slide 11: Magnetic bearing
The principle of magnetic bearing is simple, it has been used extensively in aerospace industry.
Active bearing basics. Electromagnetic fields support moving parts without contact; servo control system stabilizes suspended element by increasing supporting force in direction opposite that of any displacement, to restore correct position.

## Slide 12: Conduction cooling using spring loaded cooling pads - the game changer
By using the spring loaded cooling pads in close contact with the target rim, we can easily remove the power deposited in target.
As we removed the need of cooling water channel inside the target wheel, we eliminated the need of feeding cooling water in the shaft and thus eliminated the need of rotating vacuum seal altogether and make it possible to have the target system enclosed completely inside a vacuum chamber with only electrical connections and stationary cooling water feed through.

## Slide 13: Summary of the scheme: The friction between target wheel and cooling pad
The friction between target wheel and cooling pad would be a problem if there is not a vacuum compatible lubricant as the target wheel is in constant contact with the cooling pads.
The friction problem will be solved by coating the wheel and cooling pads with a solid film of Tungsten Disulfide (WS2).
WS2 is a magic material, which has following properties: Tungsten Disulfide (WS2) or Tungsten Disulphide is an extremely slick, dry film lubricant coating. WS2 has an extremely low coefficient of friction of 0.03 -- lower than that of Teflon, Graphite, or Molybdenum Disulfide (MoS2). The film is remarkably durable compared to many other lubricant materials and can withstand tremendously high loads of over 300,000 psi! WS2 has unsurpassed performance properties for lubricity, non-stick, low drag, wear life, and load rating.
WS2 has an electrical conductivity in the order of 10-3 (ohm.cm)-1 [1]. With a half micron coating, the electrical/thermal resistance introduced by the coating will be negligible
[1]. P. A. Chate, D. J. Sathe and P. P. Hankare, Electrical, optical and morphological properties of chemically deposited nanostructured tungsten disulﬁde thin ﬁlms. Appl Nanosci (2013) 3:19–23, DOI 10.1007/s13204-012-0073-0

## Slide 14: Proposed Parameters
The ILC target rim has area of > 1000 cm^2 and will be coated with WS2.
The cooling pad will be spring loaded and also coated with WS2.
The contacting area is assumed to be 300cm2 with a contact pressure of 1N/cm2 (1.45psi). The heat generated by the friction is estimated to be 3kW.
If Tungsten(173 W/m/K) is used for the cooling pads, then the temperature at the surface of target will be estimated at about 38 K above ambient for 20kW power removal.
The cooling pad will have cooling channel inside and connected with cooling water manifolds. As the cooling pad is stationary, a vacuum compatible cooling water manifold should be easily implemented.

## Slide 15: R&D issues and Risks
R&D issues:
  Design a vacuum chamber that can house 1 meter wheel with cooling system implemented on the outer wall and pads.
  Purchase a vacuum compatible motor capable of 10 kW, and 4000 rpm.
  A set of magnetic bearing to support the shaft with TI wheel. Or use the WS2 coating if ball bearings are used.
  Gain experience on WS2 coating.
Risks: Based the data we find, we could not identify any major risk associate with the design. However, we would like to prototype the system on the full scale to gain the experiences on
  Lifetime of the WS2 coating;
  Vacuum compatible motor selections;
  Heat removal from a high vacuum chamber;
  Stabilization of wheel with magnetic bearing/WS2 coated bearing;
  Eliminate any unwarranted concerns on the undulator based source

## Slide 16: Report on initial sliding cooling test at Institute of Modern Physics, China 摩擦冷却实验报告
By XM Zhang, ZM Zhang and Wei Gai

## Slide 18: （1）理论计算（多层平壁的稳态热传导） Heat transfer modeling of multi-layered system
在稳定状态下，通过各层的热流量均等于Q，

## Slide 20: 理论的计算（mathmatica 300degree）

## Slide 22: （2）Experiment Set-up

## Slide 23: Initial Analysis:
（1）上面的图形表示：转靶不同频率下通水与不通水之间靶的温度、石墨的温度、铜块的温度的对比图。比较而言，通水的确可以带走热量。
（2）根据材料的属性，大概有37%摩擦产生的热作用于转靶。63%作用于石墨，根据具体情况，
17HZ(10min)下，摩擦力产热14kJ,摩擦力的功率22w
34HZ(10min)下，摩擦力产热22KJ，摩擦力的功率36w
摩擦力做功，相对比较小。

## Slide 24: （3）Next Step, fully instrumented/quantitative tests
1）External heat
2）Apply MoS2
3）Instrument temperature sensors everywhere.

## Slide 25: Future Plan (or recommendations)
At IMP
  More quantitative tests of components, investigate critical engineering issues.
  External heat sources (10 kW) and a full wheel (1 meter ) at 2000 rpm.
  Investigate mechanics of the sliding contacts,
At ANL (working with Tribology Group)
  Support the IMP tests,
  An optimized design for ILC parameters, including advanced surface coating techniques,
  Design and test vacuum compatible components,
  Construct a realistic target that can operate continuously for years.
Working with good engineering team, I am optimistic and confident.
One more thing……

## Slide 26
4 meter Helical undulators
Either in booster or
Main ring
Target, capturing for positron and acceleration 6 GeV for both electron and positron
Stacking as in CLIC design and with some damping damping
Injection into booster ring at 6 GeV, (Tang made direction right)
Undulator based positron source can be adapted for FCC and CEPC
~ 50 km of main ring and booster