## Slide 1: Summary of IR Optics for Single L* CR
In general: better performance for shorter L* if free to set both QF1 and QD0 positions.
QF1 position fixed by push-pull constraints to ~>9m
  Better FFS performance for longer L* (smaller QF1-QD0 distance)
  Optimal L* ~4m. Choose 4.1m to ensure room with ILD design for BPM d/s QD0 for “IPBPM”
For L*=4.1m considered QF1 position @ 9.5 or 9.1m
  For expected tolerances, negligible tuning performance improvement for 9.1m. Improvements @ 9.1m become a little more pronounced for degraded parameters (e.g. larger than design εx)
  Collimation depth optimal @ 9.5m
  No compelling reason to change from 9.5->9.1m, recommend keeping 9.5m distance.
QF1A
QF1B
QD0A
QD0B
IP
L*=4.1m
L* (QF1) = 9.5m
L(QF1m) 2->1m

## Slide 2: Preparation of New Optics Decks
Have decks for baseline parameters (250, 350, 500 GeV). With various changes from ‘TDR’ lattices for BDS.
Now in process of releasing new complete TDR decks (See M. Woodley talk Thursday).
  After CR2 approval -> need merge changes used for shown simulation studies into official deck.
  Includes some changes required for tuning (e.g. introduction of skew-sextupole magnets).
After FD design is finalized, need to also update extraction line optics based on FD fields and QDEX1 position.