PFA activities @ LLR
E. Becheva, V. Balagura, V. Boudry *,
J.C. Brient, K. Shpak, H. Videau, D. Yu
École polytechnique, Palaiseau
ALCW’2015
KEK
April 2015

---
Tau analysis and ILD optimisation spin-off
1. Optimisation of ILD for various Radius → realistic model
  1. perf on Single particle
  2. with tau events @ 250 GeV
2. Mokka & Simulation
  1. ILD parametrisation
  2. ECAL drivers
3. PFA reconstruction tools:
  1. Particle ID in High Granularity Calorimeters
  2. GARLIC, Pandora, ARBOR comparison: Photon finder → overlay of events Sim / Test beam Data
    1. First step toward combination of tools (part of AIDA-2020)

---
Mokka & Simulation
E. Becheva, V. Boudry, H. Videau, D. Yu
1. Small ILD options studies w reduced RECAL
  1. Some dimensions are esp bad.
  2. Missing elements
    1. dead materials between modules
    2. esp. in endcaps: bad coverage of angles
7. Elements being added: optimal implementation for
   Mokka / G4 ?

---
Being investigated...
Solution 1
Intersection of modules
with ECAL wolume
Solution 2 :
(more work)

---
ILD parametrisation
1. “alternative ILD models” proposed
   (see H. Videau presentation in ILD meeting)
2. ⇒ Implementation of realistic geometry :
  1. Simulation: Global dimensions / # elements → size of elements …
  2. Real model (mechanical): optimal size of wafers → size of elements → size of detector.
    1. mechanics (feasability), physics optim and price
  3. Radius fixed by #of wafers in EndCaps; Barrel Length by # wafers in Barrel
    ⇒ ½ alveola in Barrel or Endcap

---
ILD parametrisation
½ towers are
1 wafer wide
Break of modularity of module(!)/slab/towers etc
… and parameter DB.
 half_Z
R_ECAL 1
R_ECAL 2
5 modules of : (3) + 3 + 2.5 towers
Barrel of 5 modules of : (3) + 3 + 3 towers
Endcap quarter of
2 modules of :
3 + 2.5 towers
Barrel of 5 modules of : (3) + 3 + 3 towers
Endcap quarter of
2 modules of : 3 + 2 towers

---
Simulation modifications
1. ⇒ New ECAL Driver (SEcal06 + DB) to correct defects (mostly in Endcaps).
  1. Missing dead materials, “corners”
  2. Consistant treatment of Barrel/Endcaps
  3. Option to render the 1st Si layer standard
     ⇒ 1 layer of W in front 1st alveola
     ⇒ no preshower;
    1. keep option to have it.
  4. more regular structure:
     n1/2×(W1+[Si+W1+Si]) + n2/2×(W2+[Si+W2+Si])
    1. Now : [Si+W1+Si] + (n1-1)/2×(W1+[Si+W1+Si])
       + W1 + n2/2×([Si+W2+Si] + W2)
  5. For hybrid: alternate Si and Sc alveola [*]
n1
Thin
Layers
n2
Thick
layers
Carbon
Plate
Optional 1st W plate

---
PFA reconstruction: particle ID
1. Implementation of particle ID using the high granlarity of detector
  1. details in "Particle identification in ILD" (Dan Yu) in CALICE session
  1. build upon ARBOR(v6) (branches):
  2. ILD_o2_v06
     (reduced ECAL+SDHCAL)
     {barrel only, yet}
  3. “Standard” & Specific variables
     in a BDT(G)

---
Particle ID (2)
Prelim : Single particle @ 40 GeV
2. Fairly good perf on single particles
   and Tau’s
  1. On-going work (low E, dE/dx, etc…)
  Marlin processor → to be provided as
  generic tool
ε (%)	π+ cut	μ- cut	e- cut
π+	97.93±0.14	0.69±0.08	1.29±0.11
μ-	0.28±0.05	99.83±0.04	0.01±0.01
e-	1.54±0.85	0.01±0.01	98.92±1.01
Prelim :Tau’s single prong

---
PFA reconstruction: merging tools
1. Separation of particles using ARBOR/GARLIC/Pandora
  1. Details in “PANDORA, ARBOR and GARLIC separation power for two overlapping electromagnetic or electromagnetic-hadronic showers” (Kostya Shpak, LLR) in CALICE session.
2. Test of various clustering algorithm and test performances vs overlay:
  1. photon–photons
  2. hadron–photons
3. on
  1. MC and CALICE test beam data
4. with:
  1. PANDORA v00-12
  2. GARLIC 2.11, december edition from D.Jeans
  3. ARBOR from M.Ruan
CALICE – ILD interface

---
Tools for PFA
(event displays in DRUID for 3 algo)

---
Tools for PFA
(event displays in DRUID for 3 algo)

---
1. Caracterisation of ≠ algorithms on same data → weak and strength of each.
2. Next step:
  1. integrate the HCAL for TB
  2. Use garlic as a front-end before Pandora or ARBOR → consistent treatement

---
Perspectives
1. Completion of SECAL06 asap (1,5 month ?)
  1. with tests.
  2. Second priority: Implementation in DDHEP based on existing model.
3. Develop the particle ID tools and integrated them for
  1. consistent treatment of photons & hadrons
     with GARLIC + ARBOR / GARLIC + Pandora