## Slide 1: ILD Integration DHCAL Barrel and Endcaps
Jean-Christophe Ianigro & Imad Laktineh
- IPN Lyon -

## Slide 2: ILD integration
Barrel integration
Endcaps integration

## Slide 3: Barrel integration : design
Stainless steel 1 wheel (8 mod.) 5 wheels (Barrel)
Weight (t): 88 t 440 t
Detectors W. (t): 36.8 t 184 t
Total Weight (t) : 124.8 t 624 t
Ext. Diameter 6770 mm
Int. Diameter 4116 mm
Lenght 4700 mm
Thickness wheel face = 10 mm
Thickness absorbers= 15 mm
Ext. Diameter : 6770 mm
Int. Diameter :4116 mm
Lenght : 940 mm
x8

## Slide 4: Barrel integration : Module building
Building in Industry: 40 parts
Technology adapted to larged skin & repeatable structure
Welding method : Electron Beam Welding
Tight continuous weld
Accuracy and repeatability
Low distortion
Narrow weld and narrow heat affected zone
Filler metal is not required
Module done one by one
49 absorbers plates welded on 2 flanges
Weight = 11 t

## Slide 5: Barrel integration : scenario 1
Wheel Building in Industry / Campus : 8 modules => 5 wheels
Building Method
Step 1 : Modules assembly to wheel
  8 modules in position on specific tool
  welding / screwing and rotation
Step 2 : Wheel on specific tool
Step 3 : Special convoy to Assembly Hall
180°
Wheel weight = 88 t
Road to

## Slide 6: Barrel integration : scenario 2
Wheel Building in Assembly Hall : 8 modules x 5
Building Method
Step 1 : Modules transport by normal truck to Assembly Hall
Step 2 : Wheel structure transport
Step 3 : Modules assembly on the wheel
  8 modules in position on specific tool & screwing
Module weight = 11 t
Road to

## Slide 7: Barrel integration : detectors integration
Barrel Building & GRPC Detectors insertion
5 x Wheels built in assemby hall
368 GRPC insertion for each of the 5 wheels = 1840 GRPC
Connection of gaz, HT, datas and cooling for each GRPC
Services installation on each 8 spaces in zone A, ready to be connected for 5 wheels
Zone A
Common services
Ready to be connected
GRPC insertion
with specific tool
Damper transport structure for GRPC
Notes: 7

## Slide 8: Barrel integration : insertion
Barrel insertion & services connecting
Wheels put on the structure one by one
Barrel with 5 linked wheels on same sub-structure as ECAL (similar to CMS)
Rails inside the yoke
Insertion « push-pull »
Fixation inside the yoke on both sides
Services installation along the yoke to patch pannels
Barrel insertion
Services issues to patch pannels
CMS « enfourneur »
Notes: 8

## Slide 9: End caps integration : 2 endcaps
Endcap
One module
Module Weight : 50 t
Detectors weight : 22.5 t
Total weight : 72.5 t
One endcap made of 4 modules
Endcap Weight : 200 t
Detectors weight : 90 t
Total weight : 290 t
Material : stainless steel
2 endcaps
8 sides -> 16 sides
Encap : 48 detectors
EBW welded structure
Idem barrel
Modules built in Industry

## Slide 10: Barrel integration : scenario
Endcap Building in Assembly Hall : 4 modules x 2
Building Method
Step 1 : Modules transport by normal truck to Assembly Hall
Step 2 : Endcap structure transport
Step 3 : Modules assembly on the structure
  4 modules in position on specific tool & screwing
Module weight = 50 t
Road to

## Slide 11: End caps Integration - Ring
Ring built in Industry :
  Placed around the ECAL endcap
8 modules x 2
1704
2541
1092
Ring weight : 2.3 x 8 = 18.4 t
2xrings
Ring ( 18.4 + 8 ) + Barrel endcap (290 ) = 316.4 t
Screwed on endcap

## Slide 12: End caps integration
One module : 192 GRPC inserted in Assembly Hall
3655
2218
48 detection planes
One detection plane consisted of 4 detectors planes
GRPC plane : S = 8.5 m²
P = 467.5 Kg
P/module = 22.5 t
3153
750
750
933
493

## Slide 13: End caps design - Ring
Ring between barrel and endcap : GRPC insertion
  3 GRPC planes by module 24 / Ring
1298
800
1006
GRPC : S = 2.55 m² P = 140 Kg
P/module = 980 Kg
432
1086
648

## Slide 14: End caps insertion
Endcap + Ring : insertion on tool
Support structure for
One endcap made of 4 modules
Total weight : 290 t
Endcap + Ring
Probably linked to Yoke Endcaps

## Slide 15: Barrel Services integration
Services Connections: Barrel
Cooling for Dif : Blue / Red
  2 loops by module
  Ø14 for principal
  Ø2 for distribution alternative
Gaz For GRPC : green / pink
  2 loops by module
  Ø14 for principal
  Ø4 for distribution alternative
  High Voltage : Brown
  Ø14 for supply
  Data acquisition : Beige
  Ø14 for collecting
  Issues : 8 zones 168 x 47
47
168

## Slide 16: Endcaps Services integration
Services : Endcap+ring
Cooling for Dif : Blue / Red
  2 loops by GRPC
  14 for principal
  Ø2 for distribution alternative
Gaz For GRPC : green / pink
  2 loops by GRPC
High Tension : Brown
  Ø14 for supply
Data acquisition : Beige
  Ø14 for collecting
  Issues : 8 tubes outing 98 x 47

## Slide 17: ILD Integration Resume.
Scenarii
  Modules of Barrel & Endcaps made in industry
  Transport of modules to Assembly Hall
  5 Barrels wheels & 2 Endcap-Ring mounting
  GRPC detectors insertion
  Barrel & Endcaps-Ring insertion with specific tools
Surface needed for operations
  First the barrel & then Endcaps-Ring building and services, one after the other
  1000 m² for assembly of modules, specific structures, Services & GRPC detectors
  Zone for barrel on structure storage : 200 m²
  Time schedule
  Wheel transport & assembly : 1 week by wheel -> 5 weeks for barrel
  GRPC insertion & test : 6 weeks by wheel -> 30 weeks for barrel
  Connecting wheels, test & insertion in Yoke : 4 weeks
  Total time for Barrel = 39 semaines
  Approximately same time for both Endcaps-Ring