Online Monitoring : Detector and Performance check
Towards a 1m3 engineering prototype
- Detector check
  - LED (Gain stability)
  - Pedestal stability
- Online Monitoring
  - Tools and software
- Performance check
  - Physics : Reconstructed
    observables
Picture © Ali
Eldwan Brianne
AHCAL Main Meeting
Hamburg, 17/12/2014

---
Detector check
- Goal : Monitor the gain during running period
- Use of the full integrated LED calibration system :
  - Checks during detector commissioning
  - Check after transfer into the beam area
  - Checks on a daily basis by doing a Pedestal/LED run
1.6 x 0.8 mm² (0603)

---
Gain/Pedestal checks
- Checked Gain between several periods
  - DESY Commissioning / First Period
  - DESY Commissioning / Second Period
  - First Period / Second Period
- Checked Pedestal between
  the 2 periods

---
Gain Correlation
- DESY/First Period
  - Gain stable
  - Shift to the right :
    Temperature changed between Commissioning and October (was hotter during summer)

---
Gain Correlation
- DESY / Second Period
  - Good correlation
  - Still shift to the right – Still with Temperature difference

---
Gain Correlation
- 1st Period / 2nd Period
  - Good correlation also
  - Coherent between the 2 periods
  - Light shift upwards → Need further investigations

---
Pedestal/Gain Stability
- Pedestal/Gain along the November Period
  - Stable Gain and Pedestal during the November Period
  - We have the control of our electronics!!!
- Let's go further → Physics

---
Data Reconstruction
- Current status (Lan's talk) :
- Use of these tools for “Online Monitoring”
  - Run of an automatic shell script that do the reconstruction on the data every X minutes using a local copy of the database
“Semi-Online”
Reconstruction
(Marlin Framework)
Event
Building
Raw Data
Reco Rootfile
Database
Monitoring :
Shower profile, Energy, T0s...
Monitoring :
Rates, Raw ADC/TDC

---
Performance Check
- Needs to look at the useful observables for different types of runs (electrons, muons, pions..)
- Relevant Observables :
  - Energy Sum and profile
  - Shower profiles, Beam profile
  - Noise (Number of Hits over 0.25 & 0.5 MIPs)
  - Temperature Monitoring
  - Lots of others...
- Goal : Check the physics performance during data taking

---
“Online Monitoring” software
- Interfaced with current tools (still in development)
- User-friendly ROOT GUI / Python (Thanks to Shaojun)
- Steerable by xml (File directory, Number of Layers...)

---
Hit Rate
- Hit rate in MIP
  - Hit rate and distribution for each layers (Number of hits over 0.25 & 0.5 MIPs)
  - See directly 'noisy' layers

---
T0s Correlations
- T0s are needed for TDC calibration later on
- Need to monitor them → better event selection
  - In the last Testbeam : 2 T0s on 2 small layers and 2 T0s per big layers
- T0s against each other on the same layer
1 T0 not working on Layer 14
T0s disconnected on Layer 9

---
T0s Difference
- Difference of the TDC of the T0s on the same layer
  - Expect a pic around 0 if the T0s trigger at the same time

---
Energy Sum
- First Check for Energy Sum distribution and per event
  - Give a good idea of the performance of the detector
Run 20323 - Muons

---
Shower profile, radius..
Energy profile for each layer, Cog in x, y, z (energy weighted) and mean shower radius, beam profile.
Run 20249 – Pions

---
Conclusion & Outlook
- Very Stable Gain/Pedestal during TB Periods
- Still some minor bugs to be corrected
- Can be useful for comparing different runs
- Anything can be implemented
- Needs to be tested at the next beam period
- Next steps :
  - Do reconstruction on event by event basis (LCIO Standalone) using the tools we have already
  - Running over only updated events
  - Integrate with EUDAQ?

---
Thank you for your attention