## Slide 1: Tunnel Length Issue
K.Yokoya
2014-1211 ADI
ADI/CFS Informal mtg at KEK on Dec.4

## Slide 2: Physics Issue
TDR Design : Maximum energy ECM=500GeV
  Decided before the discovery of Higgs at ~125GeV
500GeV is close to the threshold of e+ e-  t t H at ECM=475GeV
ECM~550GeV is preferable for measuring top-Yukawa coupling
  The crosssection at 550GeV is factor ~4 larger than at 500GeV
Parameter Group report (Oct.2014)

## Slide 3: Accelerator Issue
The average operation gradient defined as G=31.5MV/m in TDR
 linac length ~11km*2 for 500GeV
Can we guarantee 31.5MV/m?
  Vertical test for XFEL so far shows values somewhat lower than ILC spec 35MV/m
  Moreover, gradient reduction in cryomodule
    Average reduction of first 11 module = ~14% (but only 10 of full production)
If the actual gradient is lower, e.g., by 5%, ttH will be completely missed

## Slide 4
TTC2014@KEK D. Reschke
Note:
Acceptance criterion at lower gradient
Power-limit 31MV/m

## Slide 5: Timing Issue
( L1 + L2 + L3 ) – L4 = n x CDR
TDR values give ( L1 + L2 + L3 ) – L4 = 9 x CDR + 294m
It is possible to adjust the value either by
  Shortening the BDS by ~150m
or by
  Expanding the DR circumference by ~30m
This will nearly keep the TDR layout
But no margin for 500GeV, no way to reach 550GeV

## Slide 6: What if longer linac is needed?
Perhaps, ~10% (sum of physics and accelerator demands) is a reasonable extension
10% fully equipped linac is probably out of concern
  Too expensive O(500M$)
But at least we can prepare additional empty tunnel
With TDR CDR, ( L1 + L2 + L3 ) – L4 = 10 x CDR tells the positron tunnel must be lengthened by DLLinac = CDR /2 – 294m/2 = 1473m = 14% of TDR linac tunnel
This is enough for the timing issue, but the electron tunnel should also be lengthened for ECM issue
  Nearly 3km increase in total

## Slide 7: Another Solution
Keep n=9 and adopt longer CDR
DLe+Linac = 9xDCDR /2 – 294m/2
For example, CDR = 3508m gives DLe+Linac = 1064m = ~10% (DLtotal ~ 2.1km)
This requires 8.3% larger DR
  Slight modification of wiggler length and RF is needed

## Slide 8: How to proceed?
Consensus to increase tunnel length
Some more detail of the design
  Modification of DR if needed
  Where to insert the empty section?
  Cryogenics system
  CFS issues : study started
  Cost estimation
    Empty tunnel ~25M$/km
    Beam line (high energy beam, RTML)
    Dcost of DR
Time line
  Change request early next year
  Final decision by ALCW at KEK in Apr.2015

## Slide 9: Which is better?
DLtotal =3km
  gives larger gradient margin (14%)
DLtotal =2.1km with DCDR =269m (8.3%)
  Requires less increase of tunnel length
  But 8.3% increase of CDR (plus 8% wiggler length and RF power/voltage) may even be more expensive than 1km of linac tunnel
  Redesign of DR needed  manpower ?

## Slide 10: Where should the extra linac tunnel be inserted?
High energy ends of linacs
  Cryogenics station at PM+-8 can be reinforced later
  Additional access tunnel not needed

## Slide 11: SCRF Experts Discussion at KEK after TTC (Dec.5)
Improvement of gradient reduction in cryomodule might be improved
  One of the important topics of TTC
Should wait 1-2 more years for the final decision