## Slide 1: Cavity BPM processing and hardware upgrade plans
24.02.2015
A. Lyapin, S. Boogert, E. Yamakawa

## Slide 2: Aims
Would like to study low-charge and multibunch (multi-train at ATF) operation
Low vs high charge: need to adjust the sensitivity of the system
Multibunch: need to upgrade the processing
Programme primarily supported by CBPM development for light sources, but will have immediate benefit to ATF2 operation (+ CERN/CLIC + e-JADE grants)
Any upgrades should avoid/minimise interruption to ATF2 studies
People:
  Alexey – 2 months from March to May
  Emi – 1 month in April
  Stewart – mainly helping behind the scenes, will be at KEK in April for the Workshop

## Slide 3: Low charge operation
Investigate timing (signal shape change) and other issues when going to lower charge
Locked vs. unlocked operation
Hardware changes may be required:
  Remotely controlled attenuators (we are aiming to provide ~7-8 of HMC800’s, control via RS232/Ethernet)
  Try free-running stable LO and clock generators (find what’s available) – also useful for measuring the dispersion, currently issues due to 714 MHz harmonic changing
BPM
Remote control via RS232/Ethernet

## Slide 4: Multibunch studies
Need to modify processing for multiple bunches
Investigate time of arrival (diode) signals vs bunch charge, distance
Plan: replicate existing processing system, then modify step-by-step running in parallel to existing processing
Hardware: additional processing PC (already at KEK); attenuators may be useful if bunches are offset with respect to each other

## Slide 5: Multibunch processing (1)
Acquire multiple signals in one digitiser reading
Remove residual signal by subtracting raw or processed waveforms
Need arrival time info for subtraction  use diode signal
N. Joshi

## Slide 6: Multibunch processing (2)
Subtraction is done on phasors, phase information is important
Errors in propagating the amplitude and phase degrade the resolution
Frequency differences between the pos and ref cavities and timing drifts, time of arrival detection are important
N. Joshi

## Slide 7: Multibunch investigations
Need at least 3 CBPMs for resolution measurements
Use the same subset for both low-charge and multibunch
Instrument with attenuators 3 CBPMs and a reference (+diode sep?) = 8 channels
Use 1-bit attenuators (still need to choose between 10, 15 and 20 dB)
Scan timing, charge etc
Processing for all CBPMs though, checks with the selected 3

## Slide 8: Summary
Upgrades to the ATF system: new processing and PC, remote controlled attenuators
Will need some beam time for the studies during April-May running, estimating a minimum of:
  2-3 half-shifts (ideally, following BPM calibration) for low-charge
  2-3 full shifts for multibunch