## Slide 1: ILC SRF Technology Development
H. Hayano, KEK
11022015
LCWS15@Whistler Nov2-6

## Slide 2
1. Cavity & Cryomodule
2. Cavity treatment & Instrumentations
3. HLRF and others
4. SRF facility at KEK
Contents
Mainly focused on SRF activities in Japan

## Slide 3
Cavity & Cryomodule

## Slide 4
CM-1
STF Accelerator
CM-2a
Cryomodule development: STF Accelerator
STF cryomodule development history
2011 start construction of STF accelerator(Injector + QB)
2012 Feb-Jun: QB accelerator commissioning
Jul to Mar: experiment of Laser-Compton (QB)
2013 Apr: disassemble Laser-Compton
start installation of CM-1
Sep: two set of 4-cavity train completed
Oct: Cryomodule assembly in STF tunnel
Dec: CM-1 completed
2014 Apr: start CM-2a assembly
Jul: CM-1 and CM-2a connection completed
Oct-Nov: Cool-down test (low power test)
2015 July-Sep.: Coupler room temp. process
Oct-Dec: 2-nd Cool-down test (high power test)
Injector beam operation done
Capture
Cryomodule

## Slide 5
15 cavities
1st Test
13 cavities
2nd Test
5 cavities
3rd Test
3 cavities
4th Test
1st Test
Final
Performance
TDR spec.
35MV/m +/- 20%
Gradient performance of STF Accelerator Cavities
(15 cavities)

## Slide 6
TDR spec.
35MV/m +/- 20%
1pass Ave.
27.9MV/m
Final Ave.
34.2MV/m
When TDR-2-process rule is applied,
13 were passed out of 15,
then 87% yield
We could not identified the reason of bad performance of 12MV/m cavity (MHI-24), because of limited study time.
Gradient Performance Evolution History (15 cavities)

## Slide 7
● 2014 Nov. – 2015 Mar. 4 Cavities were processed and jacketed
name Max. gradient installation
MHI-027 25.8MV/m for CM-2a cryomodule (2-nd VT)
◯ MHI-028 30.0MV/m for CM-2a cryomodule (1-st VT)
MHI-029 26.1MV/m for CM-2a cryomodule (1-st VT)
◯ MHI-030 30.1MV/m for CM-2a cryomodule (1-st VT)
◎(>35MV/m), ◯(>=28MV/m) :ILC spec. clear
MHI Cavity factory adopt new mass-production welding method, below.
- > there was some performance fluctuation
For CM-2a
Cryomodule
replacement
Multiple Cell-EBW
in vertical position
(for industrialization)
Recent 4 Cavities Status
weld
Grade2 Nb
for port pipe
before
after
Reducing # of parts, welding for port pipe
(for industrialization)
4 cavities
in
one welding batch
(for industrialization)
Ave. 28MV/m
MHI
MHI

## Slide 8
● 4 TESLA Cavities were fabricated by Japanese Industries
TB9-TSB01 by Toshiba
TB9-TSB02 by Toshiba
TESLA Cavity Production Study (2013 – 2014)
TB9-MHI01 by MHI
TB9-MHI02 by MHI
● TESLA Cavity stress calculations was done
for Japanese High-pressure-Gas Regulation
Performance Test is under preparation (not yet done)

## Slide 9
Cryomodule development: CM-1 and CM-2a
CM-1: 13m 8cavities＋Q-magnet・BPM
Q-magnet in the center: ILC type cryomodule (2013)
CM-2a: 6m 4cavities: ILC half-size cryomodule (2014)
First Cool-down test: Oct. - Nov. 2014
Coupler warm-temp. RF process: July-Sep. 2015
Second Cool-down test: Oct. - Dec. 2015

## Slide 10
CM-1: 13m 8 cavities ＋ SC Q-magnet・BPM
First ILC-type-B Cryomodule in the world (magnet in the center )
SC Q-magnet + BPM in the center
Study Item: effect on cavity gradient degradation,
conduction-cooled splittable superconducting Q-magnet
Beam position monitor,
alignment preservation,
heat load, etc.
CM-1 ILC-type Cryomodule development

## Slide 11
BPM
SC-Quad
GV
GV
Pump port
Cavity
Cavity
Gas-Return-Pipe
GRP support
CM-1 Center region

## Slide 12
BPM was installed
between Gate-Valves of cavities
Local clean-room in tunnel was used.
KEK-KNU-PNU
L-band Cavity-BPM
0.4 micrometer resolution, QL = 200 -300 (low-Q for multi-bunch detection)

## Slide 13
FNAL-KEK fabrication
yoke
SC coil and case
Simplify cooling channel,
Simplify assembly
Assembly at outside
of clean-room
split
Conduction cooled splittable SC-magnet

## Slide 14
Cavity Frequency change by cool-down;
Good as designed.
CM-2a
10 days to reach 2K
( 3 days stop included )
Cryomodule development: 1st Cool-down Test
CM-1+CM-2a: Cool-down Test :Oct-Nov,2014
Conduction-cooled magnet is
also reached arround below 10K
with some delay.

## Slide 15
BPM
Conduction cooled SC-magnet Test: FNAL-KEK
Conduction cooled quadrupole magnet was fabricated by FNAL,
installed into CM-1 at STF. Test was done in Nov. of 2014, and now in test Oct.-Dec. 2015.
Cooling Characteristics
  Coil temperature: ~ 8.5 K (v.s. < 5 K expected)
  Splice/joint temperature ~ 9.3 K (v.s. < 5 K)
  Thermal load: 2.65 W (v.s. 2.6 W expected)
Excitations
  Current (@ 1.5 A/s) reached: 7 A ( v.s. 50 A expected)
  Recovery time after quench: ~ 10 min.
Reduction of heat-load from current-lead was done in summer 2015.
Coil temp. 8.5K ---> 7.3K improved (Oct. 2015)

## Slide 16
L=100mm W=10mm strip-line
Φ30mm diameter
KEK-TohokuGakuin stripline pickup
Wire-Position Monitor(WPM)
monitoring alignment preservation

## Slide 17
Temperature variation of Gas-Return-Pipe(GRP), Temp. difference GRP top-Bottom
300K -> ~4K
Max Temp diff. between top and bottom ΔT = 55K
GRP Temperature Variation during cool-down
DT
Temp.
CM-1+CM-2a: Cool-down Test :Oct-Nov,2014

## Slide 18
dX
+400µm ~ +900µm
dY
+200µm ~ -500µm
upstream
center
downstream
upstream
center
downstream
GRP bending
GRP movement during cool-down

## Slide 19
Y
X
Meas. dX = 650µm
Meas. dY = -1175µm
X-Tilt = +400µrad
Y-Tilt = -400µrad
Calculation (expected)
Expected dX = 400µm
Expected dY = -1570µm
#1 Cavity (most upstream)
Temp
#1 Cavity movement during cool-down

## Slide 20: Cavity RF performance in CM1/CM2a
Module | CM1 |  |  |  |  |  |  |  | CM2a |  |  | 
Cavity # | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Cavity name | MHI-14 | MHI-15 | MHI-17 | MHI-18 | MHI-19 | MHI-20 | MHI-21 | MHI-22 | MHI-24 | MHI-23 | MHI-25 | MHI-26
Eacc @V.T. [MV/m] | 36.6 (power limit) | 35.7 (Cell#1 Quench) | 38.4 (power limit) | 36.2 (power limit) | 37.2 (Cell#1 Quench) | 35.1 (power limit) | 38.9 (power limit) | 35.8 (power limit) | 12.0 (heavy F.E.) | 35.9 (Cell#3 Quench) | 32.3 (Cell#1 Quench) | 31.6 (Cell#1 Quench)
Eacc @C.T. (short pulse) [MV/m] | >38.6 (test stop) | 36.8 (Quench) | 35.2 (Quench) |  |  |  |  |  |  |  |  | 
Eacc @C.T. (full pulse) [MV/m] | >38.7 (test stop) | 36.7 (Quench) | 35.3 (Quench) |  |  |  |  |  |  |  |  | 
36MV/m
(last week)
Single cavity power test, now under progress
Room-Temperature Coupler Process : July – September 2015
Cavity Process at 2K : October – November 2015

## Slide 21
LLRF Feedback Off
LLRF feedback ON
35MV/m
31.5MV/m
Eacc
Pref
Pfor
Trigger
Waveforms of cavity power test
Eacc
Δf
QL
Δf
L.F.D. compensation by Piezo with F.B. @31.5MV/m

## Slide 22
For more high gradient, high-Q, low-material-cost
JLAB : High gradient study using
Large-grain single-cell cavity
KEK : Large-grain low-RRR Nb single-cell cavity
KEK : theory of multilayer thin-film coating,
start-up of ALD coating experiment
Cornell : Nb3Sn thin-film coated cavity
JLAB : Nb3Sn thin-film coated cavity
.
.
.
FNAL : N-doped cavity and fast-cool-method

## Slide 23
IPAC15, WEPWI013
JLAB study of single-cell cavities
Shape ( LSF, LL, TTF ), Material; Large grain
TTF shape
1.4K
1.8K
2.0K
1012
1011
1010

## Slide 24
多層薄膜の理論的研究
KEK theoretical study of multilayer-thin-film coat
Including surface micro-roughness
350mT
170mT

## Slide 25
Cavity treatment & Instrumentations

## Slide 26
● VEP (Vertical EP) development for EP industrialization
KEK-Marui VEP development
Vertical-EP Development
KEK-Cornell
9-cell cavity VEP with newly
developed Ninja-cathode
BCP at Cornell
(mounted on VEP setup)
Cornell-KEK
Saclay-KEK
KEK-Saclay
VEP at Saclay
Cost effective EP process,
Facility cheaper than horizontal
Way to apply HF-free bipolar-EP

## Slide 27
HF-free Bipolar-EP development
Anodic
( + )
ta
Applied i
Cathodic
( - )
Forward
pulse
tc
ia
Reverse
pulse
ic
Time off
Off-Time “Tuned” to:
Heat dissipation
Replenish reacting species
Remove reaction products
A kind of vertical EP
Use of dilute sulfuric acid only
In future
Faraday Technology, co.
Cornell, KEK, JLAB also started bipolar EP study

## Slide 28
● Weld porosity is a main candidate of defect-quech of cavity!
Weld sample study (JLAB)
SC Cavity: Weld porosity Study by JLAB (1)
Weld Surface
Toward the bulk
porous
Porosity tends to be concentrated
underneath weld surface?
Cross-section of EBW is studied for porosity
SEM inspection
1µm porous
was fond
Hyrox multi-focus
image inspection
30µm porous
were fond
Why weld porosity is happened?
JLAB-KEK
200µm

## Slide 29
JLAB-KEK
A view of HiRox 3D Imaging on
a bubble pit. Diameter ~500mm.
The round up and shining
appearance of bubble pits
imply they are defects of
welding work.
EBW
Cu side
Nb thin-layer side
Pit inside of cupper welding seam, which was found in the study of Nb-Cu cavity in JLAB.
Cutting-out coupon of EBW seam
SC Cavity: Weld porosity Study JLAB-KEK (2)
X-ray transparent image of
Cutting-out coupon of EBW seam
Many pits were found in EBW seam, not other region.
KEK study:
Intentional carbon contamination in EBW seam,
Then, X-ray transparent image EBW seam
No pit was found in 6 EBW seam sample
in various carbon density condition.

## Slide 30
High density distributed sensors on the flexible base, and read-out by multiplexer.
Tool development for heat & FE localization: JLAB-KEK
High density Temperature map and X-ray map for SC-Cavity field test.
For cavity cell
For cavity iris
“At-Cavity” diodes
Hamamatsu S1223-01, 2 each per cavity
“In-Air” GM tubes (10 each)
Wall mount ion chambers
(area monitor for dosimetry)
BL Supply
WG1
WG2
WG3
WG4/5
WG6
WG7
WG8
BL Return
Top Center
F100-1
F100-2
F100-3
F100-4
F100-5
F100-6
F100-7
F100-8
Cavity name
X-ray detectors for FE study in ACCXD cryomodule in JLAB

## Slide 31
HLRF and others

## Slide 32
ILC TDR RF power scheme is planned to install
10MW
Multi-beam klystron (MBK)
10MW MBK is now driven
by bouncer-type modulator.
To be replaced by MARX modulator.
Toshiba MBK
SLAC P2 Marx Modulator
ILC waveguide
HLRF of STF Accelerator

## Slide 33
MARX modulator development at STF
STF has processed to fabricate SLAC P2 MARX modulator
with supply of SLAC drawings and consultant.
Tender for fabrication with SLAC drawing
(under knowledge property contract)
was done in June 2014.
One company won this bid, however,
declined this contract in early 2015.
Development of New-MARX by Japanese company has been started.
4-stage MARX, at first
Waveform of 4-stage MARX
P2 Marx fabrication was suspended.

## Slide 34
ILC-TDR
STF CM-1
Realize TDR waveguide in STF CM-1,
in March 2016.
Waveguide scheme of ILC and STF

## Slide 35
SRF facility at KEK

## Slide 36
STF building
COI: Center-of-Innovation Building
COI building (80m x 30m)
COI building
model facility for ILC cavity & cryomodule assembly & Testing
Building completion : February 2015
COI-budget (2012-2013) : targeting future Compact SC Accelerator business
development by Industry-Academic Collaboration.

## Slide 37
COI: Center-of-Innovation Building Inside
As a model facility for ILC assembly & Testing
Clean-room
Cryomodule Assembly (cantilever)
EP (vertical-EP)
Cavity Testing (4-cavities-test)
He Cryogenics
( Cryomodule Testing : not yet)
First-stage main component installation was done in March - September 2015

## Slide 38
COI: Clean-Room (11.4m x 33.9m)
First-stage clean-room installation was done. 2-nd stage construction will be 2016.

## Slide 39
COI: Cryomodule Assembly Tool
Assembly tool and test cryomodule were assembled in March - May 2015
Collaborated by DESY

## Slide 40
COI: Vertical EP facility
Vertical EP system, limited to water-test function,
were built up in May - September 2015

## Slide 41
COI: Vertical Test Cryostat
4-cavities Vertical Test tools
were assembled in March - August 2015
Collaborated by DESY

## Slide 42
COI: He Cryogenics
Only main cryogenics components were purchased.
(4K Liquefier and Compressor)
4K 600W He Liquefier
He compressor
Build-up of Cryogenic System will be done
in the following 1-2 years.

## Slide 43
Summary of SRF activity of Japan
Cavities & Cryomodules
STF accelerator and ILC-type cryomodule are under progress.
cavity production industrialization is advanced.
Study for more high gradient, high-Q are under progress.
Cavity treatment & Instrumentations
Vertical EP, HF-free bipolar-EP are well advanced.
Instrumentations for cavity quench identification.
HLRF and others
Realization of ILC TDR power scheme
SRF facility
Building-up of ILC-SRF model facility (Japan) has started.
End of slide

## Slide 44
Extra-Slide

## Slide 45
STF accelerator injector completed
in February 2012
STF accelerator injector by “Quantum-beam program”
High-flux X-ray generation by inverse Compton scattering
10mA electron beam （40MeV, 1ms, 5Hz)
Laser accumulator by 4 mirror resonator
head-on collision of beam and laser
Target flux: 1.3 x 1010 photons/sec 1%bandwidth
Capture cryomodule
Collision point
Photocathode RF gun
STF Accelerator Injector
Inv. Compton X-ray experiment in March 2012 to March 2013

## Slide 46
KEK in-house 9-cell cavity; KEK-01
36 MV/m
Deep-drawing HOM-cup
Press form HOM-antenna
Trials of industrial fabrication

## Slide 47
160MHz 5µs Pulse Train
Generator
Signal Selector
1GS/s 14bit ADC
FFT
512 points ADC data
Wire-Position Monitor(WPM) Electronics

## Slide 48
Optics Design of STF Accelerator

## Slide 49
Optics Design considering Future FEL application
BC1
BC2
Space for
Undulator
SC-RF
SC-RF
1GeV
4MeV
Expanded Area plan
Photocathode
RF-gun
Total 135mの
Linac - FEL

## Slide 50
BC1
BC2
1.25mm -> 0.3mm
Energy 45MeV
Energy spread 0.068%
0.3mm -> 0.05mm
Energy 525MeV
Energy spread 0.068%
Single shicane
Double shicane
BC1
BC2
2-stage Bunch Compressor to be installed

## Slide 51
ILC-TDR RF power supply: 10MW-MBK power into 39 cavities
Flexible RF supply by VTO ( Variable-Tap-Off ) to fit cavity each performance.
Phase control for each cavity, QL control by cavity power coupler.
TDR HLRF scheme