## Slide 1: Updated mW Measurement from Threshold Scan Using Polarized e- and e+ at ILC
Graham W. Wilson
University of Kansas
Nov 5th 2015
LCWS2015 Meeting
Whistler, BC, Canada
Old TESLA study re-visited.
(LC-PHSM-2001-09)

## Slide 2: Outline
Give overview of methodology of polarized threshold scan including recent updates.
Address some of the issues related to the machine.
(I will focus the talk on the above – and not motivation, other mW measurements, auxiliary measurements)
See recent talks on sp method (Hamburg-2013), momentum-scale calibration (Fermilab-2014) for absolute s determination, and mW generalities at ALCW2015 and backup slides.

## Slide 3: mW from cross-section close to threshold
Stirling
mW=80.23 GeV
unpolarized
Key: s,s

## Slide 4: ILC Polarized Threshold Scan
GENTLE 2.0
with ILC 161 beamstrahlung*
Each set of curves has mW = 80.29, 80.39, 80.49 GeV.
With |P| = 90% for e-
and |P| = 60% for e+.
- +
+-
0 0
- -
++
LEP
Use (-+) helicity combination of e- and e+ to enhance WW.
Use (+-) helicity to suppress WW and measure background.
Use (--) and (++) to control polarization (also use 150 pb qq events)
Experimentally very robust. Measure pol., bkg. in situ
Example 6 points in s.
78% (-+),
17% (+-) 2.5%(--), 2.5%(++)
Need 10 ppm error on s to target 2 MeV on mW
Notes: Lumi ratios
96.0D0 21.0D0 5*0.0D0 2*3.125D0 = 123.25 95%, 5%
6 –point scan (160.6, 161.2, 161.4, 161.6, 162.2, 170.0)
L ratios 1:5:5:5:1:6

## Slide 5: Counting Experiment
Example: 6 point scan (index i), (90% e-, 60% e+ polarization) with -+, +-, ++ and - - helicity combinations (index k)
Count events in 3 WW candidate categories (lvlv, qqlv, qqqq – index j) with expectation mijk and one Z-like category (radiative return and f fbar) with expectation nik.
96 event counts
Data could also be taken with other helicity combinations (00, -0,+0,0-,0+ ) if warranted. (eg. further checks of polarization model)

## Slide 6: Fit the Event Counts to Model Expectations
Assumes A=1 for WW (actually about 0.996)
Event count expectations:
Signal, background, and Z-control sample spin factors:

## Slide 7: Fit Parameters
(Note: within the SM current uncertainty on aS translates to 0.06 MeV on GW)
NEW
(previously assumed known perfectly)

## Slide 8: Fit Details and Experimental Assumptions
Use Poisson likelihood (also c2 as cross-check)
Include c2 penalty terms to constrain the systematic effects associated with integrated luminosity, signal efficiencies and background asymmetries.
MEASURE background cross-sections
NB. Assumed inefficiency and background is halved with respect to TESLA study – based on ILC style detector

## Slide 9: 4 eqns, 4 unknowns
Using the large statistics of Z-like events (150 pb).
Can use the 4 measured Z-like event counts to determine the 4 related parameters (s, x, y, A).
  Precise determination of the polarization values, x and y, is key to the mW measurement
Suitable event selection for qq+mm+tt should be straight-forward
  Include inclusively full energy events and radiative return
Can also use data with one or both beams depolarized to check further/constrain beam polarization model.

## Slide 10: Systematic on ALRB
For current studies, I have assumed that this can be controlled to 2.5% (lvlv), 1.2% (qqlv) and 0.5% (qqqq).
  Previously this systematic was neglected.
Numbers are based on the expected statistical uncertainty on ALRB for a background side-band with the same statistics of background events as expected for 100 fb-1.
This needs more study to establish that these errors can be achieved. At this point, I am hesitant to assume that these errors will improve with more integrated luminosity.
It is also not at all obvious that the background will only couple to LR and RL chiralities (contributions from two-photon, single-W …)

## Slide 11: Example Fit

## Slide 12: Ensemble Tests
3.65 MeV
3.86 MeV
Use average error from fit in following.
(I just noticed that the empirical error is smaller than the error from the fit … should investigate further)
1000 experiments.

## Slide 13: Results
6-point scan, (90%, 60%)
Other systematics | D MW [MeV]
s | 0.8
BS shape | small ?
Theory | 1 ?
Independent of mZ

## Slide 14: Beamstrahlung Effects
Used Guinea-Pig to simulate beamstrahlung spectrum using scaled ILC TDR parameters.
Energy-loss spectrum fitted with CIRCE1 parametrization.
WW cross-sections from GENTLE2.0/4fan (Bardin, Leike, Riemann) convolved with beam-strahlung.
Red (NoBS). Blue (With BS)
Modest change to threshold shape. Up to 6% reduction, +- 2% in shape.
Unpolarized cross-section
(Mea culpa: my original TESLA study erroneously used cross-section with no BS (bug))

## Slide 15: Details on Guinea-Pig + Circe Settings
Leading to Circe1 parameters of
Guinea-Pig (D. Schulte)
Circe (T. Ohl)
Note: A machine design with higher luminosity and worse beamstrahlung is likely to be preferred for this physics measurement
See backup slides 25&26 for more details

## Slide 16: Sensitivity to mW
Unpolarized cross-sections
No beam-strahlung (0, 0)
With ILC beam-strahlung (0, 0)
Fairly negligible effect of beam-strahlung on statistical sensitivity

## Slide 17: Sensitivity to mW
No beam-strahlung (0,0)
With ILC beam-strahlung (0,0)
With BS (-80%,0)
With BS (-80%,+30%)
With BS (-90%,+60%)
Polarization of electron and positron beams at ILC (necessarily with beamstrahlung) offers MUCH better sensitivity per unit of integrated luminosity than the LEP-like unpolarized case.

## Slide 18: Updated Results
Use re-optimized 2-point “scan”. Working on optimizing this analytically.
Errors on mW (MeV)

## Slide 19: Summary I
Threshold scan can yield a precision measurement of mW at a linear collider with polarized electron AND positron beams.
  Errors at the few MeV level can be envisaged.
  With 100fb-1, find 2.4 (stat.)  3.1 (syst.)  0.8 (s)  theory (MeV)
ILC design can and should evolve to make this feasible (proof of concept is in the TESLA TDR).
  Supported machine parameters would be helpful.
  Better awareness of these issues by LCC management …
Regressing to no positron polarization should be avoided!
  Controlling the background is very challenging without it.
    I am not confident that a useful mW measurement can be made at threshold with no positron polarization. Limited by absolute polarization measurement – 0.5% systematic.
    I am certain that a competitive mW measurement at threshold is very challenging with no beam polarization at all

## Slide 20: Take-Home Messages
ILC has very good prospects for measuring mW with very high precision
  Not much work yet on measurements at standard ILC s values (s  250 GeV). Needs more effort.
  Measurement at threshold expected to be very robust with polarized electrons and polarized positrons (experimentally and theoretically).
Precision mW needs precision s.
  sP method very promising
  Need precise momentum scale.
    J/psi method using Z’s needs 40M Z’s…..
  Error on mW from s knowledge of 0.8 MeV can be targeted.
ILC accelerator
  Need to preserve the option to run with high L and highly polarized electrons AND POSITRONS at WW threshold. No experimental show-stoppers.
    This is a great advantage of ILC over other accelerator concepts.
  We should DEMAND capability for high luminosity for calibration at the Z.
  We should DEMAND capability for reasonable luminosity at the Z with polarized beams for physics.

## Slide 21: Backup Slides

## Slide 22: W Production in e+e-
e+e-  W+W-
etc ..
e+e-  W e n
arXiv:1302.3415
unpolarized cross-sections

## Slide 23: “New” sP In-Situ Beam Energy Method
e+ e-  m +m-(g)
Use muon momenta.
Measure E1 + E2 + |p12| as an estimator of s
(no assumption that m12  mZ)
with J. Sekaric
ILC detector momentum resolution (0.15%), gives beam energy to better than 5 ppm statistical for nominal luminosity. Momentum scale to 10 ppm => 0.8 MeV beam energy error projected on mW (J/psi)
Beam Energy Uncertainty should be controlled for s <= 500 GeV
GWW
preliminary

## Slide 24: mW Prospects
Polarized Threshold Scan (GWW)
Kinematic Reconstruction
Hadronic Mass (GWW, BvD, KT)
Method 1: Statistics limited.
Method 2: With up to 1000 the LEP statistics and much better detectors. Can target factor of 10 reduction in systematics.
Method 3: Depends on di-jet mass scale. Plenty Z’s for 3 MeV.
1
See Snowmass document for more details
1
3
2
Bottom-line: 3 different methods with prospects to measure mW with error < 5 MeV

## Slide 25: ILC Accelerator Features
L ~ (P/ECM) (dE / ey,N) HD
P  fc N
dE  (N2 g2)/( ex,N bx sz) U1 (Yav)
Scope for improving luminosity performance.
Increase number of bunches (fc)
Decrease vertical emittance (ey)
Increase bunch charge (N)
Decrease sz
Decrease bx
Machine design has focused on 500 GeV baseline
3,4,5 => L, BS trade-off
Can trade more BS for more L or lower L for lower BS.
dp/p same as LEP2 at 200 GeV
dp/p typically better than an e+e- ring which worsens linearly with s
Notes: Check.
Eqn 1 is 1.3.4 in Ch 1 of TESLA TDR Part II.
From p57 of my logbook. Seems to be based on TESLA CDR discussion and Yokoya-Chen.
Looks like I missed a factor of gamma in the delta_E term previously.
P= beam power.

## Slide 26: Beamstrahlung
161 GeV
161 GeV
500 GeV
500 GeV
Average energy loss of beams is not what matters for physics.
Average energy loss of colliding beams is factor of 2 smaller.
Median energy loss per beam from beamstrahlung typically tiny compared to beam energy spread.
Parametrized with CIRCE functions.
f d(1-x) + (1-f) Beta(a2,a3)
Define t = (1 – x)1/5
t=0.25 => x = 0.999
In general beamstrahlung is a less important issue than ISR. Worse BS could be tolerated in the WW threshold scan
71%
43%
x >0.9999 in first bin
Scaled energy of colliding beams

## Slide 27: mW Measurement Prospects Near Threshold
Measure at 6 values of s, in 3 channels, and with up to 9 different helicity combinations.
Estimate error of 6 MeV (includes Eb error of 2.5 MeV from Z g) per 100 fb-1 polarized scan (assumed 60% e+ polarization)
Use RR (100 pb) cross-section to control polarization
LEP2 numbers

## Slide 28
Systematics are treated as nuisance parameters that can be fitted. Errors should scale statistically.

## Slide 29: Polarized Threshold Scan Errors
conservative – viewed from + 15 years ....
Non-Ebeam experimental error (stat + syst)
  5.2 MeV
 | Scenario 0 | Scenario 1 | Scenario 2 | Scenario 3
L (fb-1) | 100 | 160*3 | 100 | 100
Pol. (e-/e+) | 80/60 | 90/60 | 90/60 | 90/60
Inefficiency | LEP2 | 0.5*LEP2 | 0.5*LEP2 | 0.5*LEP2
Background | LEP2 | 0.5*LEP2 | 0.5*LEP2 | 0.5*LEP2
Effy/L syst | 0.25% | 0.25% | 0.25% | 0.1%
DmW(MeV) | 5.2 | 2.0 | 4.3 | 3.9

## Slide 30: In-situ Physics Based Beam Energy Measurements
Potential Mass-Scale References for Energy Calibration
Particle | DM/M (PDG) (ppm)
J/psi | 3.6
Upsilon | 27
Z | 23
W | 190
H | 2400
Conventional wisdom has been to use Z’s, but with ILC detector designs J/psi’s look attractive.
Prefer not to use something that one plans to measure better or something that will limit the precision.
Use J/psi from Z for momentum scale.

## Slide 31: Momentum Scale with J/psi
ILD fast simulation
107 Z’s
With 109 Z’s expect statistical error on mass scale of 1.7 ppm given ILD momentum resolution and vertexing based on fast simulation.
Most of the J/psi’s are from B decays. J/psi mass is known to 3.6 ppm. < p > = 20 GeV.
Can envisage also improving on the measurement of the Z mass (23 ppm error)
Double-Gaussian + Linear Fit
c2/dof = 90/93
CDF
(no vertex fit)
s=mZ
Notes: Include mean momentum

## Slide 32: Full Simulation + Kalman Filter
No vertex fit nor constraint
10k “single particle events’’
Work in progress – likely need to pay attention to issues like energy loss model and FSR.
Preliminary statistical precision similar.
More realistic material, energy loss and multiple scattering.
Empirical Voigtian fit.
-46±13 ppm
Need consistent material model in simulation AND reconstruction

## Slide 33: “Calibration” Run at s=mZ for detector p-scale calibration
Assume 2.0 ppm statistical for 109 Z’s.
Asymptotic error of 3.6 ppm driven by J/psi PDG mass uncertainty.
Need at least 40 M hadronic Z’s for 10 ppm
Corresponds to  1.3 fb-1 (L  1.3 × 1033 for 106s) assuming unpolarized beams
If detector is stable and not pushed, pulled and shaken, one could hope that such a calibration could be maintained long term at high energy.
s=91GeV
Plot assumes negligible systematics from tracking modeling …
Notes: The required instantaneous luminosity is about 1/10th of the 250 GeV Luminosity Upgrade when scaled down by a factor of gamma.

## Slide 34: Positron Source
231m undulator
For s  250 GeV, still need a high energy e- beam for adequate e+ production.