## Slide 1: CALICE DAQ TF meeting
Taikan Suehara
(Kyushu University, Japan)

## Slide 2: Topics
News from each technology
Master clock (concluded)
Run/Spill structure
Acquisition cycle
BX synchronization
HDMI connection
busy
TB plan
AOB

## Slide 3: Things to discuss (shown in kickoff)
Common master clock frequency
  To assure simultaneous BX counting
Common BX clock frequency
BUSY treatment
 Common CCC? or just clock synchronization?
High level DAQ software (EUDAQ?)
  Run control, event building, run number, monitoring,…
Common data format (LCIO class)
Partial or optional sharing of firmware and software
etc.

## Slide 4: 2. Master clock (concluded)
Master CCC provides clock to each system
5 MHz base clock (considered BX)
Interface
  Si: LEMO, have to be converted to 50 MHz
  Sc: LEMO or HDMI, 5 MHz OK
  SDHCAL: HDMI, 5 MHz OK
Master CCC
Si CCC
Sc CCC
SDHCAL SDCC

## Slide 5: 3. Run/Spill structure
Definition of run
  Set of acquisition with ‘same’ condition
  Should be maximum O(1 hour) or O(1 day)?
Run number (proposal)
  XXXYYYYY, XXX is the common TB number
Spill (from accelerator)
  in ILC: spill = ‘acquisition cycle’
  in TB: spill corresponds to multiple AC
  Do we need a spill counter? (CCC may be able to count, offline sharing?)

## Slide 6: 4. Acquisition cycle
‘Acquisition Cycle’ or ‘Readout Cycle’
  Term (AC or RC)
  Count – 0 from the beginning of run (or beginning of TB?)
Confirm consistent numbering
  Timestamp in PC? (easy but not accurate)
  Other ideas?

## Slide 7: 5. BX synchronization
Frequency
  Si: 2.5 MHz (can be changed in TB mode???)
  Sc: 250 kHz in TB mode
  SDHCAL: 5 MHz
Dead time exists from ‘start_acq’ to real BX0
  Si – about 452 usec, can be changed by DIF FW
  Sc – about 12 usec in CC
  SDHCAL
  Si-Sc difference calibrated by data analysis

## Slide 8: 5. BX sync. (cont.)
Do we need real ‘synchronization’?
An idea
  ‘Pre-spill’ comes via FAST command
    To prepare power pulsing etc.
  Spill by another FAST command or Analog line
    ‘Ext trigger’ line??
  Anyhow, need FW of every system
    Not easy??

## Slide 9: 6. HDMI connection
Just confirm
  clock (CCCDIF): pin1: +, pin3: -
  ext_trig (CCCDIF): pin15: +, pin16: -
  command (CCCDIF) pin4: +, pin6: -
  busy (DIFCCC) pin7: +, pin9: -
  data (DIFLDA) pin10: +, pin12: -
8b/10b encoding
  Si/SDHCAL: Yes
  Sc: No (will be implemented?)

## Slide 10: 7: busy
Status
  Si: being checked, oscillating
  Sc: OK, not oscillating
  SDHCAL:
Master CCC will collect busy from all to veto the spill (stop/start next AC)
  We may want to add busy from PC as well
  Can individual CCC give busy to master? Si: OK in spec., Sc: SDHCAL:
Oscillating or not oscillating or accept both

## Slide 11: 8: TB plan
SDHCAL in this April-May
  Si may attend, but low probability now
  More in Autumn??
ScCAL in July and August

## Slide 12: 9. AOB