## Slide 1: Phase Monitor Tests – first look.
Jack Roberts

## Slide 2: Overview
All sets of electronics are now nominally identical.
  One exception: noticed 6 dB additional attenuation in LO input to 2nd and 3rd mixer.
  But electronics was not correctly connected when I first checked the signals.
Taken calibrations and resolution measurements with many variations in electronics setup.

## Slide 3: Rough Phase Monitor Electronics Layout
3GHz Shifter
Filter
Amplifier
Monitor V Sum
Multiplier
RF In
LO In
Mixer out
Diode out
10/16 dB
Diode
ADC
Amplifier?
ADC
MIXER
SiS Digitiser

## Slide 4: Setups Tried
Swapping monitors between mixers.
Swapping phase shifters between mixers.
With and without amplifier to SiS digitisers.
With 10dB and 16dB on LO input (for Mixer 2 and 3).
Calibration then data for resolution measurements with all setups.

## Slide 5: Results summary
Resolution is worse than measured last year (~0.7 degrees with “nominal” setup).
Phase jitter from mixers using the 2nd and 3rd shifter is much larger.
Measured phase jitter depends (mostly) on the shifter used, not the monitor or mixer.
Amplifier to SiS digitiser and 10dB/16dB after shifter doesn’t appear to make much difference (at least at current noise level).