## Slide 1: calibrations
IPBPM FILTER TESTS
Siwon Jang
Hoyeong Jeong
Glenn Christian
Talitha Bromwich

## Slide 2: Finding single sample point
Remove pedestals
Find location of max in each pulse for the I signal.
Find mode sample location of the maximum. + 5, so after the peak. Use same sample for I and Q across all pulses.
Find Ref charge peak in the same way. Use this sample number for charge normalisation across all pulses.
Following Michael Davis thesis, 2014

## Slide 3: Calibration calculations
Plot I/q vs Q/q for all pulses
Calculate I' (charge normalised)
Calculate Q' (charge normalised)
Plot I' vs mover voltage
Mover μm/V calibration to change to correct units
Plot Q' vs mover voltage
Following Young-Im Kim thesis, 2012

## Slide 4
IPB_to_elec_A_with_BPF_split_before_2nd_stage_0dB_cal

## Slide 5: Calibration comparisons
Comparison of calibrations with and without 714 MHz BPF
Nominal optics, beam waist (minimum y jitter of 141 nm) centered on IPB.
SIS digitiser gathering data
ICT ~ 4 x 1010
3.5 dB power splitter to IPBY, sending two signals to the channels for A and B on the second stage electronics.
714 MHz +/- 10 BPF added.
Plot the change in calibration constants for both cases choosing different single point sample numbers for the calibration.

## Slide 6: Calibration comparisons
I and Q signals No filter
I and Q signals 714+/- 10 MHz filter before 2nd stage electronics

## Slide 7: Calibration comparisons
No filter
Filter
Plots of the change in calibration constants for both cases choosing different single point sample numbers for the calibration from 0 to 180.