## Slide 1: ATF june summary
Neven & Talitha

## Slide 2: June Shifts
9/6 Tues Swing
10/6 Wed Swing (IPBSM)
12/6 Fri Day
16/6 Tues Swing
18/6 Thur Owl (Siwon’s shift)
18/6 Thur Day (IPBSM)
19/6 Fri Day

## Slide 3: 9/6 Tues Swing
Tightened and checked all connections on 1st and 2nd stage.
Note: no longer a 150 MHz BPF or amplifier before reference enters the limiter – this explains why no longer need for delay cables.
Checked dipole/ref phase with and without 714 MHz BPF on 2nd stage – needs 2m delay cable without BPF.
Movers not working - re-launched IP BPM mover system.
Bug in ATF IPBPM data-saving code – fixed later in week by ATF engineers.

## Slide 4: 10/6 Wed Swing (IPBSM)
Set up upstream feedback in 2-bunch mode using P1, P2 and P3 and FONT5 board #1.
Unable to kick beam – problem isolated to ZPULs.

## Slide 5: 12/6 Friday Day
High-beta (100x1000) optics.
Charge 0.7 x 1010
3 BPM resolution studies without 714 MHz BPF in X and Y.
3 BPM resolution studies with 714 MHz BPF in X and Y.
Discontinuities in mover calibrations – particularly in IPC - saturating? – need to analyze further to see if this data can be useful.

## Slide 6: 3BPM resolution – no BPF
High-beta (100x1000) optics.
Charge 0.7 x 1010
Integration 55 to 62
3BPM resolution – 714 MHz BPF
High-beta (100x1000) optics.
Charge 0.7 x 1010
Integration 55 to 62

## Slide 7: 12/6 Tues Swing
Nominal optics
Charge 0.3 x 1010
Re-calibrate IPC with 714 MHz BPF in X and Y – linear behaviour observed at lower charge.
Install C-band BPFs on between hybrid and variable attenuator inside tunnel on dipole and reference cavities.
Reference not limited properly. Remove C-band BPFs from references.

## Slide 8: C-band BPF on the reference
Not limited properly.
BPFs subsequently removed from the reference.

## Slide 9: 18/6 Thurs Owl (Siwon’s Shift)
Nominal optics. Charge 0.5 x 1010.
Calibration matching in X and Y.
18/6 Thurs Day (IPBSM)
Set up upstream feedback in 2-bunch mode using P1, P2 and P3 and FONT5 board #1. ZPULs replaced with ATF pre-amplifier.
Poor bunch-to-bunch position correlation.

## Slide 10: 19/6 Fri Day
High-beta (100x1000) optics.
Charge 0.3 x 1010 and 0.6 x 1010.
3 BPM resolution studies with C-band BPF in X and Y at different attenuations.

## Slide 11: No BPF – 2m delay cables
Signals out of 2nd stage going into detector.
IPC(X)
Ref(X)

## Slide 12: 714 MHz BPF on 2nd stage
Signals out of 2nd stage going into detector.
IPC(X)
Ref(X)

## Slide 13: C-band BPF before 1st stage
Signals out of 2nd stage going into detector.
IPC(X)
Ref(X)

## Slide 14: IPA(Y)
No BPF 0dB 0.7 x 1010
714 MHz BPF on 2nd stage 0dB 0.7 x 1010
C-band filter before 1st stage 0dB 0.3 x 1010

## Slide 15: Jitter vs Attenuation IPA(Y)
C-band BPF before 1st stage
0.3 x 1010

## Slide 16: Jitter vs Attenuation IPB(Y)
C-band BPF before 1st stage
0.3 x 1010

## Slide 17: Jitter vs Attenuation IPC(Y)
C-band BPF before 1st stage
0.3 x 1010

## Slide 18: Resolution vs Attenuation in Y
Results for 0dB
C-band BPF before 1st stage
0.3 x 1010