## Slide 1: ILC Cryogenics Layout: A draft consensus for the Change Request
CFS and Cryogenics Two-days Workshop at CERN
27 and 28, July, 2015

## Slide 7: Change Request, to be submitted Main Cryogenics Layout on Surface

## Slide 12: Some Comparisons
ILC – TDR Baseline
Main components underground
Features:
Scenic preseravation on surface
No major cryo-transfer-line
Lower cryogenic operational cost because of no 1 km transfer line.
A cost driver: Covern:
  13m(w) x 180m (l) x 10m(h)
  =23,000 m^3
New Baseline in preparation
May components on surface
Features:
Safety
Accessbility in daily operation
No concern for MC vibration
He storage flexibility
Smaller acess tunnel sizee because of no installation of 4.5 K Cryo-plant Under G.
A cost driviers:
Saving caver cost:
   23,000m^3x 0.5 = ~ 11,500 m^3
  200 CHF/m^3 x 2.30E4 = 2.3 MCHF
Additional transfer line cost:
 2 kCHF/m x 1,000 m = 2 MCHF

## Slide 15: Conclusion
It has been a consensus to propose a new baseline cryogenics layout with major components located on surface,
Cost balance is basically neutral (and to be further investigated,
The Change Request can be submitted before LCWS2015.

## Slide 16: Some further discussion after WS

## Slide 19: Comments given after WS
P. Lebrun
A. Yamamoto
D. Delikaris

## Slide 21
Akira Yamamoto