Electron source for Linear Colliders
KURIKI Masao (Hiroshima/KEK)

---
Contents
- Introduction,
- Electron Emission,
- Related Physics Process,
- Electron Gun and its design,
- Electron Source for Linear Colliders,
- Summary

---
Introduction

---
Lepton Collider
e+e- collision is a simple interaction.
The initial states is well defined.
Easy to reconstruct the final states.
This full reconstruction is powerful and essential for e+e- colliders.
e+
X state
e-

---
Hadron collider and Lepton Collider
Hadron Collider
Collision between composite particles (protons).
Initial state is not defined.
Extremely high energy, high event rate, large noise.
Lepton Colliders
Collision between elementary particles (leptons).
The initial state is well defined.
Full reconstruction of events.
u
u
d
u
u
d
e-
e+

---
Well defined initial states
- Electron and position are spin ½ fermions. Two eigen spin states.
- In SU(2)xU(1) gauge theory, these two spin eigen states are different particles which has different weak Iso-spin and hyper charge.
- Ideal well defined initial states means that the beam contains only one spin state.
- Practicaly, the beam should be polarized.
{size 24 color blue {l_L equiv left ( binom{%nu_{eL}}{e_L} right) }} newline {size 24 color blue{ e_R }}
{size 20 color blue {I_W = { size 18 {1 over 2}}, ~Y_W = -1 }} newline {size 20 color blue{I_W = 0, ~ Y_W = -2 }}
{size 24 color blue { P equiv {N_R - N_L } over {N_R + N_L}}}

---
Suppress Background
By righthanded polarzed beam (e-R)

---
Injector
- What is the injector?
  - Generate accelerate-able particle beams;
- What is the accelerate-able beams?
  - Right amount : Charge
  - Right shape : Beam size, emittance, bunch length
  - Right direction: along beam line
  - Right time : timing, phase
Accelerator
Injector
Transport line
IP

---
Electron Gun
- Generate electron beam
  - Right amount : Charge
  - Right shape : Beam size, emittance, bunch length
  - Right direction: beam line
  - Right time : timing, phase
Extraction Field
3.2nC
Beam
Cathode

---
Bunching (1)
- Bunching : Bunch the beam. What is the bunch?
  - Beam : collimated particle flow.
  - Bunch : collimated and clustered particle flow. The length should be short enough comparing to the RF period for uniform acceleration.
Bunch
Beam

---
Bunching (2)
- Bunching: Shorten the longitudinal length of the beam.
    - Right amount : Charge
    - Right shape : Beam size, emittance,bunch length
    - Right direction: beam line
    - Right time : timing, phase
  Bunching
3.2nC

---
Injector Concepts
CW Beam
Long bunch beam
Short bunch beam
Thermionic Cathode
Photo-cathode
Field emitter
Pre-buncher
Sub Harmonic Buncher
Buncher
DC field
RF field
To Acc.
  Bunching
Extraction Field
3.2nC
Cathode

---
Electron Emission

---
Fundamental Process
Field emission
Thermal emission
Thermal emission
e-
e-
e-
e-
e-
e-
Electric field
e-
e-
Secondary electron emissio
Photo-electron emission
e-
e-
e-
e-
e-
laser

---
Electronic States
- Electrons are confined in a well potential.
- At T=0, electrons are in ground states.
- At T>0, some electrons are excited by thermal energy.
Vacuum
(free space)
Well potential
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

---
Electronic States
- Electrons are distributed according to Fermi-Dirac Distribution.
- Fermi energy : the maximum electron energy state at T=0.
- Work-function : height of the vacuum cliff from the Fermi energy.

---
Peaceful Cliff
Vacuum state
Fermi Level
Electrons in grond states

---
Once they are excited....
Some extreme guys are extracted as beam
Fermi Level
Hot Electrons

---
Electronic States (2)
Electron density in a metal is product of state density
D(ε) and distribution function f(ε),
{size 20 color green {n(%epsilon) = D(%epsilon) f(%epsilon) ~~~~~~~~~(1-1) }}
State density in phase space (x, vx) – (x+dx, vx+dvx).... is
{size 20 color green {D(%epsilon)= 2m^2 over h^3 dx dy dz dv_x dv_y dv_z ~~~~~~(1-2)}}
Distribution function f(ε) is given by Fermi-Dirac function
{size 20 color green {{f(%epsilon) = 1 over {func exp left({%epsilon-%mu} over kT right) +1 } ~~~~~~~ (1-3) }}}
Number of electron with energy ε<E is
{size 20 color green {N (%epsilon) = int_0^E f(%epsilon) D(%epsilon) d%epsilon ~~~~~ (1-4)}}

---
Thermal Electron Emission
- If the temperature is sufficiently high, so that electrons are distributed up to more than the vacuum level (E0), the electrons escape out to the outside.
- The gap between the vacuum level and the Fermi energy is Work function, φ, which characterize the thermal emission.
{size 24 { color green {E > E_0 = E_f + %phi }}}

---
Emission Density (1)
Number of emitted electron:
In depth (z-direction)
Kinetic energy for z-direction must be more than vacuum potential energy, μ+Φ
Number of electron emitted from the cathode is give by
{size 20 color green {z <= v_z %DELTA t ~~~~~~~~~~~~~~ size 18(1-5) }}
{size 20 color green {v_z >= v_{vac} equiv sqrt{{2(%mu + %phi)} over m} ~~~~~~~size 18(1-6)}}
{size 20 color green {N = int dx int dy int_0^{v_z %DELTA t} dz int_{-infinity}^{+infinity}dv_x int_{-infinity}^{+infinity}dv_y int_{v_{vac}}^{+infinity}dv_z f(%epsilon) D(%epsilon) ~ size 18(1-7)}}

---
Emission Density (2)
By integrating x, y, z and inserting distribution function,
From this equation, emission density per unit time is obtained
{size 20 color green {N = %DELTA x %DELTA y %DELTA t {2m^3}over{h^3} int_{-infinity}^{+infinity}dv_x int_{-infinity}^{+infinity}dv_y int_{v_{vac}}^{+infinity}dv_z v_z over {func exp left({%epsilon-%mu} over kT right) +1} ~~~size 18 (1-8)}}
{size 20 color green {%sigma equiv N over { %DELTA x %DELTA y %DELTA t}= {2m^3}over{h^3} int_{-infinity}^{+infinity}dv_x int_{-infinity}^{+infinity}dv_y int_{v_{vac}}^{+infinity}dv_z v_z over {func exp left({%epsilon-%mu} over kT right)+1}~~size 18 (1-9)}}

---
Emission Density (4)
Because ε-μ≫kT, f(ε) is approximated as
{size 20 color green {1 over {func exp left({%epsilon-%mu} over kT right)+1} sim func exp{left( {%mu - %epsilon} over kT right) } ~~~~~~~~~~~~~size 18(1-10) }}
The density is simplified as
{size 20 color green {%sigma = {2m^3}over{h^3} int_{-infinity}^{+infinity}dv_x int_{-infinity}^{+infinity}dv_y int_{v_{vac}}^{+infinity}dv_z v_z func exp left({%mu - %epsilon} over kT right) ~~~~size 18(1-11)}}
Replacing the energy with the velocity,
{size 20 color green { %epsilon = m over 2 (v_x^2 + v_y^2 + v_z^2)}}
{size 20 color green {%sigma = {2m^3}over{h^3} func exp{left( %mu over {kT}right)}int_{-infinity}^{+infinity}dv_x int_{-infinity}^{+infinity}dv_y int_{v_{vac}}^{+infinity}dv_z v_z func exp left({- m(v_x^2+v_y^2+v_z^2)} over 2kT right) ~~ size 18(1-12)}}

---
Emission Density (5)
Integral for vx and vy can be performed as
and for vz as
we obtain
Electric current density J is given by
{size 20 color green {int_{-infinity}^{+infinity}dv_x int_{-infinity}^{+infinity}dv_y func exp left({- m(v_x^2+v_y^2)} over 2kT right)={2%pi k T } over m ~~~~ size 18 (1-13)}}
{size 20 color green {int_{v_{vac}}^{+infinity}dv_z v_z func exp left({- mv_z^2} over 2kT right)={{kT}over{m} func exp left( -{mv_{vac}^2}over{2kT}right)} ~~~~ size 18(1-14)}}
{size 20 color green {%sigma = {4%pi m k^2 T^2}over{h^3} func exp left(- {{%phi} over{kT}} right) ~~~~~~~size 18(1-15)}}
{size 20 color green {J = {4%pi e m k^2 T^2}over{h^3} func exp left(- {{%phi} over{kT}} right) ~~~~~~size 18 (1-16) }}

---
Richardson-Dushman Equation
{size 24 color green {J = AT^2 e ^{- {%phi over {kT}}} ~~~~~~~~~~~~size 18 (1-17)}}
{size 20 color green {A={4%pi emk^2} over {h^3}=1.20 times 10^6 [A / m^2 K^2]}}
A : thermionic emission constant
T: Temperature (K)
k : Boltzmann constant ; 1.38E-23 (J/K)
e : electronic charge
m : electron mass
h : Plank constant ; 6.63E-34 (Js)

---
Field Emission (1)
- FE is electron emission observed from cold (not hot) material when a high electric field is applied.
  - Large surface field makes the potential barrier very thin.
  - The tunnel current becomes significant with >1E+8 V/m.

---
Field Emission (2)
{size 24 color green {J=e int_0^infty n(%epsilon_z) P(%epsilon_z) d%epsilon_z ~~~ size 18(1-18)}}
Electron
density
Tunneling
probability
Tunneling Probability by WKB method
{size 20 color green { U(z) = E_0 - eFz }}
{size 20 color green {P(%epsilon_z, F) = func exp left [ - int_0^w sqrt{{8m(2%pi)^2} over h^2 lbrace U(z) - %epsilon_z rbrace} dz right ] }}
{size 20 color green { w = {E_0 - %varepsilon_z} over {eF}}}
{size 20 color green {{} = func exp left [ - {8%pi sqrt{2m}} over{3heF} ( E_0 - %epsilon_z)^{3/2} right ] ~~~~~~size 18 (1-19)}}

---
Field Emission (3)
By Taylor expansion,
In the low temperature limit, the current density is
where ε'=εz-μ.
{size 20 color green {(E_0 -%epsilon_z)^{3/2} = left[ %phi +(%mu - %epsilon_z) right]^{3/2} = %phi^{3/2} + 3 over 2 %phi^{1/2}(%mu - %epsilon_z) ~~~~~ size 18 (1-21)}}
{size 20 color green {J(F) = {4%pi em} over{h^3} int_0^infty d%epsilon_z (%mu-%epsilon_z) func exp left [ - 8%pi sqrt{2m} over {3heF} (E_0- %epsilon_z) right] }}
{size 20 color green {{}= {4%pi em} over{h^3} func exp left(- {8%pi sqrt{2m}} over {3heF} %phi^{3/2} right) int_0^infty d acute %epsilon acute %epsilon func exp left [ - 4%pi sqrt{2m} over {heF}%phi^{1/2} acute %epsilon right] ~~ size 18(1-22)}}
{size 20 color green {J= {e^3 F^2} over {8%pi%phi} func exp left(- {{8%pi sqrt{2m}} over {3heF}} %phi^{3/2} right) ~~~~~size 18 (1-23)}}
(Fowler-Nordheim formula)

---
Fowler-Nordheim Plot
Fowler-Nordheim formula with field enhancement factor κ
{size 22 color green {J={ e^3 %kappa^2 F^2} over{ 8 h %pi %phi }exp(-{{ 8 sqrt{2m}} over { 3 h e %kappa F}%phi^{3/2} }) ~~~~~~ size 18 (1-24)}}
k: local field enhancement by surface condition,
Taking ln(J/F2) and plotting as a function of 1/F,
The gradient gives information on the surface
condition, k.
(RF case)
{size 22 color green {func ln left(J / F^2 right)= func ln left( { e^3 %kappa^2} over{ 8 h %pi %phi } right) - left ({{ 8 sqrt{2m}} over { 3 h e %kappa}%phi^{3/2} }right ) 1 over F ~~~~size 18(1-25)}}
{size 20 color green {func ln left(J / F^{2.5} right)= func ln left( { e^3 %kappa^2} over{ 8 h %pi %phi } right) - left ({{ 8 sqrt{2m}} over { 3 h e %kappa}%phi^{3/2} }right ) 1 over F ~~~~size 18(1-25')}}
1/F
ln(J/F2)

---
Emission Densiy (1)
Photo-electron current density is given by
where P is transition probability by photon excitation. For further manipulation, replacing y=(εz+hν-E0)/kT and δ=h(ν-ν0)/kT,
{size 24 color green {J = {4%pi emkT} over {h^3}P int_{E_0-h%nu}^infty d%epsilon_z ln left[1+func exp(%mu -%epsilon_z) over kT right ] ~~~~size 18 (1-27)}}
{size 20 color green {J = {4%pi emkT} over {h^3}P int_{E_0-h%nu}^infty d%epsilon_z ln left[1+func exp(%mu -%epsilon_z) over kT right ] }}
{size 20 color green {{}= {4%pi em k^2 T^2} over {h^3}P int_0^infty dy ln left[1+func exp(%delta -y ) right ] ~~~~~~ size 18 (1-29)}}

---
Emission Density (2)
{size 24 color green {f(%delta) = int_0^infty dy ln left[1+func e^{%delta -y } right ] ~~~~ size 18 (1-30) }}
(a) δ=h(ν-ν0)/kT <0 (ph. energy is less than FE)
{size 20 color green {f(%delta)= sum from{n=1} to{infty} (-1)^{n-1} {func e^{n%delta}} over n int_0^infty dy func e^{-ny} }}
{size 20 color green {{} = sum from{n=1} to{infty} (-1)^{n-1} {func e^{n%delta}} over {n^2} ~~~~~~~~~~~~size 18 (1-31) }}
since
{size 20 color green { ln (1+ x) = sum from {n=1} to infty (-1)^{n-1} x^n over n~~~~~~~size 18(1-32)}}
{size 20 color green { ln (1+ func e^{%delta -y}) = sum from {n=1} to infty (-1)^{n-1} {func e^{n(%delta -y)}} over n ~~~~~size 18 (1-33)}}

---
Photo-electron Emission
- Electron emission by photo-electron effect.
  - Photons excite electrons into higher energy states.
  - If the states are higher than the vacuum level, the electrons goes to vacuum.
  - Condition for photo-emission is approximately,
{size 24 color green { h%nu > %phi ~~~ size 18 (1-26)}}

---
Emission Density (3)
(b) δ=h(ν-ν0)/kT >0 (ph. energy is more than FE),
(b-1) first integral, w=δ-y
{size 24 color green {f(%delta)= left( int_0^%delta dy + int_%delta^infty dy right) left [ func ln( 1+ func e^{%delta -y} ) right ] ~~~~~~~~ size 18 (1-34)}}
{size 20 color green {int_0^%delta dy func ln( 1+ func e^{%delta -y} )= int_0^%delta dw func ln(1+ func e^{w}) }}
{size 20 color green {{} = int_0^%delta dw left lbrace w + func ln(1+ func e^{-w}) right rbrace }}
{size 20 color green {{} = left [w^2 over 2 right ]_0^%delta + sum from n=1 to infty (-1)^n 1 over n^2 [func e^{-nw}]_0^%delta}}
{size 20 color green {{} = %delta^2 over 2 + %pi^2 over 12 + sum from n=1 to infty (-1)^n func e^{-n%delta} over n^2 ~~~~~size 18 (1-35) }}

---
Emission Density (4)
(b-2) second integral, w=y-δ
the first term of rhs is 0 and the second term is
Finally, sum of (b-1) + (b-2) gives f(δ)
{size 20 color green {int_%delta^infty dy func ln( 1+ func e^{%delta -y} )= int_0^infty dw func ln(1+ func e^{-w}) }}
{size 20 color green { {} = left[ w func ln (1 + func e^{-w}) right]_0^infty + int_0^infty dw {w} over {1+e^w} ~~size 18 (1-36) }}
{size 20 color green { int_0^infty dw {w} over {1+e^w}= %pi^2 over 12 ~~~~~~~~ size 18(1-37)}}
{size 20 color green {f(%delta) = %delta^2 over 2 + %pi^2 over 6 + sum from n=1 to infty (-1)^n func e^{-n%delta} over n^2 ~~~size 18 (1-38) }}

---
Quantum Efficiency
Quantum Efficiency, η, is practically used to qualify the photo-electron emission
With practical units,
{size 24 color green {%eta = {number of photo electrons} over { number of photons} ~~~~~~~size 18 (1-40)}}
{size 24 color green {%eta ["%"] = 124{ J[nA]} over {P[%mu W] %lambda[nm]} ~~~~~size 18 (1-41)}}

---
Fowler Equation
{size 24 color green {J = AT^2 P left lbrace matrix {{sum from{n=1} to{infty} (-1)^{n-1} {func e^{n%delta}} over {n^2}} # %delta < 0 ## {%delta^2 over 2 + %pi^2 over 12 + sum from n=1 to infty (-1)^n func e^{-n%delta} over n^2} # %delta > 0} right rbrace ~~~ size 18 (1-39)}}
{size 20 color green {A = size 22 {4 %pi e mk^2} over {h^3}}}
- Fowler equation gives photo-current spectrum.
- The absolute density is hard to estimate because P depends on the surface condition.

---
Photo-cathode
- Basically, all solid material can be used as photo-cathode.
- The light wave length has to be shorter than the threshold wavelength of the photo-electron effect.
- Metal is popular as photo-cathode for accelerator.
- Semi-conductor is popular as photo-cathode for Photo-tube, since the high QE and operable for wide wavelength region.
- Semi-conductor becomes popular as photo-cathode for accelerator too, because the high QE, longer wavelength, and polarization.
- Insulator is hardly used as photo-cathode because it is operable only with tiny current. Otherwise, it is charged up.

---
Metal Cathode
Vacuum state
- Fermi level is in a band.
- Emission threshold = work function.
- Work-function is in UV.
- QE is generally low,
  0.01% - 0.001 %.
- Temporal response is fast <ps.
- Cu, Mg, Ag, are popular.
Work
function
Fermi level
Density of States
Energy level

---
Semiconductor Cathode
- Fermi level is in a band gap.
- Emission threshold > work function.
- Emission threshold is from VL to UV.
- QE is high for certain material, more than 10%.
- Temporal response is slow > ps.
- Cs2Te, CsK2Sb, NaK2Sb, LaB6, etc.
Vacuum state
Work
function
Fermi level
Emission
threshold
Density of States
Energy level

---
Polarized electron
- Polarized Electron is generated by photo-emission with GaAs semiconductor cathode.
- It is essential for polarization that GaAs is direct transition type semiconductor.
- Transition from the valence band (VB) to conduction band (CB) by circularly polarized photon is spin dependent.
CB
VB

---
Excitation
Transition probability ~ Fermi's golden rule
  - M: Matrix element
  - D: joint density of states of ħω photon
  - f: fermi distribution function
- Considering only near the band gap, the transition probability is proportional to M2.
{color green size 24{W_{i rightarrow f} = {2%pi} over {hbar }M^2 D(hbar %omega)f(E)}}

---
Matrix Element of GaAs
- Band gap of GaAs is Γ point ( k=0).
  - Valence Band:
    - J=|3/2,±3/2> (heavy hole)
    - J=|3/2, ±1/2> (light hole).
  - Conduction Band:
    - J=|1/2,±1/2>
- Matrix Element of transition (Clebsh-Gordon coef.）
  - Heavy hole: /2
  - Light hole: 1/2
Conduction
band
Valence
band
{size 20 color black{sqrt{3} }}

---
Polarization
- Energy and helicity limitation, only two of six transitions are possible.
- Number of excited electron are polarized by 3:1 matrix amplitude.
Right handed polarization
Left handed polarization

---
Polarization Enhancement
- Further enhancement by breaking the degeneration.
- It is achieved by GaAs/GaAsP Strained Super-lattice Crystal.

---
Polarized Electron from GaAs
- Super-lattice structure to break the degeneration.
- The polarization is maximized when the laser wavelength is matched to the band gap.
Strain relaxed
   super-lattice
       24 layer
Buffer layer
Base plate
92% polarization, 1.6% QE

---
NEA surface (1)
- To extract the excited electron in CB to vacuum, surface strucure is important.
- NEA (Negative Electron Affnitiy) surface is artificially made.
- NEA surface : vacuum potential is lower than CB bottom.
e-

---
NEA surface (2)
- NEA surface is made by evaporation of Cs and O2 /NF3 on cleaned GaAs.
- GaAs: chemical etching by H2S04 and treatment by HCl-Isopropanol solution followed by heat cleaning.
- Alternating deposition of Cs and O2/NF3.
- The process should be made
  in extremely low vacuum
  pressure, <5.0E-9Pa.
C. Shonaka

---
Related Physics Process

---
Roll of the field
Electrons in cathode is tightly bond by the potential.
The external field on the cathode surface is important not only to lead the beam, but also to extract the beam from the cathode.
Surface field modifies the work function of cathode.
(Schottky effect)
The emittable current density is limited by the coulomb potential of the beam and the external field.
(Space charge limitation)

---
Schottky Effect (1)
Force by mirror charge
{size 24 color green {F_m(z) = - {1 over{4%pi%epsilon}} {e^2}over {(2z)^2}~~~ size 18 (2-1)}}
Potential of the mirror charge
{size 24 color green {V_m(z) = - {1 over{4%pi%epsilon}} int_z^infty {{e}over {4{z'}^2}}dz' }} newline {size 24 color green {{ }=-{e^2 over {16%pi%epsilon z}} ~size 18(2-2)}}

---
Schottky Effect (2)
Mirror charge potential and external field give
{size 20 color green {V(z) = %phi_0 - e^2 over {16%pi %epsilon z} - e E z ~~~size 18(2-3)}}
{size 20 color black {"at" ~~z_{max} = 1 over 4 sqrt{e over {%pi %epsilon E}}}}
Maximum
{size 20 color green {V_{max} = V_0 - e sqrt{{eE} over {4%pi %epsilon} } ~~size 18(2-4)}}
Effective work function
{size 24 color green {%phi (E) = V_{max} - %mu = %phi_0 - e sqrt{{eE}over {4%pi%epsilon}}~ size 18(2-5)}}

---
Space Charge Limit (2)
Anode
(z=d, V=VA)
Cathode
(z=0, V=0)
Poisson equation is
The current density J is given by the
charge density ρ and velocity v ,
According energy conservation,
{size 24 color green { {d^2 V(z)} over {dz^2} = -{{%rho(z)} over{%epsilon_0}} ~~~size 18(2-7)}}
z
Charge density
r(z)
{size 24 color green {J = -%rho(z) v(z) ~~~size 18 (2-8)}}
{size 24 color green {1 over 2 m v(z)^2 = eV(z) ~~size 18(2-9)}}
{size 24 color green { {d^2 V(z)} over {dz^2} = J over %epsilon_0 sqrt{m over {2e}} V(z)^{-1/2} ~~size 18 (2-10)}}

---
Space Charge Limit
- Electron terminates the electric flux (Gauss's law).
- Electric field is weakened by the space charge.
- When all flux is terminated by the charge, the field at the cathode surface is disappeared (no further emission).

---
SC Limited Current (3)
Multiplying 2(dV/dz) and integrating both sides,
Taking square root of both sides and integrate it again,
Extract J
{size 24 color green {left ( {d V(z)} over {dz} right ) ^2 = 4J over %epsilon_0 sqrt{m over {2e}} V(z)^{1/2}~~~ size 18 (2-11)}}
{size 24 color green {4 over 3 V^{3/4} =sqrt{4J over %epsilon_0} nroot{4}{m over {2e}} z ~~~~~size 18 (2-12)}}
{size 24 color green {J = {4%epsilon_0} over 9 sqrt{{2e} over m} {V(z)^{3/2}} over z^2}}
{size 24 color green {{} = 2.33 times 10^{-6} {V(z)^{3/2}} over z^2~~~~ size 18 (2-13)}}

---
SC Limited Current (3)
Substituting the anode conditions, the space charge limited current density is obtained as
V(z), E(z) , ρ(z) are expressed as a function of z
{size 24 color green {J(V_A, d) = 2.33 times 10^{-6} {V_A^{3/2}} over d^2~~~~ size 18 (2-14)}}
{size 20 color green {V(z) = V_A left ( z over d right)^{3/4} ~~~~~~~~~~~~~~~~~~ size 18 (2-15)}}
{size 20 color green {E(z) = - {{dV(z)} over {dz}} = - {4 over 3} V_A over d^{4/3} z^{1/3}~~~~ size 18(2-16) }}
{size 20 color green {%rho(z) = -{ {4%epsilon_0} over {9}} V_A over d^{4/3} z^{-2/3} ~~~~~~~~~~~ size 18 (2-17)}}

---
Child-Langmuir Law
If the cathode emission density is more than the space charge limit, the current is given by C-L law
V and d : voltage and distance between two electrodes.
S : cathode area
P : perveance defined as;
{size 24 color green {I= 2.33 times 10^{-6} {{S V^{3/2}} over d^2}=PV^{3/2} (A) ~~~~ size 18 (2-18)}}
{size 24 color green {P = 2.33 times 10^{-6} {size 20 S over size 20 d^2} (A V^{-3/2})~~~~ size 18 (2-19)}}

---
DC Gun design (2D SC Limited Flow)
2D case solution for SC limited flow;
{size 20 color green {V(z,y) = V_A {Re[(z+iy)^{4/3} ]} over d^{4/3} }}
y
{size 20 color green {nabla cdot nabla V(z) = 0 }}
{size 20 color green {{} = V_A (z^2+y^2)^{2/3} func cos 4 over 3%theta ~~size 18 (2-22)}}
V=0 equi-potential line:
{size 20 color green {func cos 4 over 3 %theta=0 rightarrow %theta = 3 over 8 %pi }}
z
By setting an electrode (Wehnelt) with this angle, SCL flow is produced.
{size 20 color green {V(z) = V_A left ( z over d right )^{4/3} }}
{size 20 color blue { 3 over 8 %pi }}

---
DC Gun design : Real geometry
By setting Wehnelt and anode electrodes to reproduce the potential, SC limited current is extracted from the cahode.
This is Pierce type gun;
Conventional type,
DC bias voltage,
Thermionic cathode,
Continous beam.
Wehnelt electrode
Anode electrode
{size 24 bold color green { %theta = 3 over 8 %pi }}
Cathode

---
Space Charge Force (1)
 The space charge force causes various beam quality degradations, e.g. bunch lengthening, emittance growth, tune shift, etc. The effect is suppressed by acceleration because it scaled as 1/γ2.
Consider a cylindrical beam with a constant density.
magnetic flux density by the current,
{size 20 color green {E_r = {N e} over { 2%pi a^2%epsilon_0}r ~~~~ size 18 (2-23)}}
{size 20 color green {B(r) = %mu_0 over r int_0^r r'J(r')dr' ~~~~~ size 18 (2-24)}}

---
Space Charge Force (2)
Current density is
The magnetic flux is given as
The Lorentz force to electron is
which is scaled as 1/γ2.
{size 20 color green {J(r) = {Ne} over {%pi a^2} %beta c ~~~~ size 18 (2-25)}}
{size 20 color green {B(r) = {%mu_0 N e %beta c } over {2%pi a ^2} r ~~~~ size 18 (2-26)}}
{size 20 color green {bold F = e bold E + e %beta c bold B = {Ne^2 r} over {2%pi a^2 %epsilon_0}(1-%beta^2)vec {e_r} }}
{size 20 color green { {}= {Ne^2 r} over {2%pi a^2 %epsilon_0 %gamma^2}vec {e_r} ~~~~ size 18 (2-27) }}

---
Beam Emittance
Emittance is defined as area in the phase space where particles occupy. The phase space is defined x and x'=dx/ds
In general, RMS emittance is given as
If there is no correlation between x and x',
p
{size 24 color green { acute x = {dx}over {ds} = v_x over v_s = p_x over p_s sim p_x over p~~~~ size 18 (2-28)}}
px
ps
{size 24 color green { %epsilon_x = sqrt{langle x^2 rangle langle acute x^2 rangle - langle x acute x rangle^2} ~~~~ size 18 (2-29)}}
{size 24 color green { %epsilon_x = sqrt{langle x^2 rangle langle acute x^2 rangle }~~~~~~~~ size 18 (2-30)}}

---
Normalized emittance
In acceleration, transverse momentum px is conserved, but the total momentum p is increased as
The emittance is inversely scaled. To avoid the energy dependence (γβ) on the emittance, the normalized emittance is defined
p1
px
p2
{size 24 color green { p_s = %gamma %beta mc ~~~~ size 18 (2-31)}}
ps
{size 24 color green { %epsilon_{nx} = %gamma%beta %epsilon_x ~~~~ }}
{size 24 color green { ~ = %gamma %beta R over 2 sqrt{ left langle left( {p_x} over {%gamma %beta m c} right) ^2 right rangle} = R over {2mc} sqrt{ langle {p_x} ^2 rangle} ~~~~ size 18 (2-32)}}

---
What is matter on Emittance?
Emittance shows the quality of the beam.
Small emittance beam can be focused down to a small spot size.
Small emittance beam can be extremely parallel.
The shape of the beam depends on the optics, but the emittance is invariant in the frame of linear optics.
Linear
Optics

---
What is the fundamental limit
on the emittance?
Everybody wants small emittance beam, but what is the limit?
One of the limit is the intrinsic emittance which the emitted beam from the cathode already has.
The source of the intrinsic emittance of cathode is thermal energy and laser energy (photo-cathode case).

---
Emittance of Beam from
Thermionic Cathode (1)
Thermionic electron emission density is already obtained
Total transverse energy of emitted electron is obtained with a similar calculation as
The average transverse energy per electron is
{size 20 color green {N = {4%pi m}over{h^3} k^2 T^2 func exp{left( - {%phi over {kT}}right)}~~~~ size 18 (2-33)}}
{size 20 color green {E_t = {4%pi m}over{h^3} int_{%mu+%phi}^infty d%epsilon_z int_0^infty d%epsilon_t %epsilon_t func exp{left ( - {{%epsilon_z+%epsilon_t-%mu} over {kT}} right) }}}
{size 20 color green {{} = {4%pi m}over{h^3} k^3 T^3 func exp{left( - {%phi over {kT}}right)}~~~~ size 18 (2-34) }}
{size 20 color green {langle %epsilon_t rangle = E_t over N = kT~~~~ size 18 (2-35) }}

---
Emittance of Beam from
Thermionic Cathode (2)
{size 20 color green {langle %epsilon_x rangle = {kT}over{2} ~~~~~~~~~~~~ size 18 (2-36) }}
Thermal energy is,
The transverse emittance is
{size 20 color green { %varepsilon_x = sqrt{langle x^2 rangle langle acute x^2 rangle} = 1 over {%gamma%beta m c } sqrt{langle x^2 rangle langle p_x^2 rangle }~~~~ size 18 (2-37) }}
{size 18 color black {langle p_x^2 rangle over {2m} = langle %epsilon_x rangle = {kT} over {2}}}
Substituting the thermal energy , emittance is
{size 20 color green { %varepsilon_x = 1 over {%gamma%beta} sqrt{langle x^2 rangle {kT} over {mc^2}} = 1 over {%gamma%beta} R over 2 sqrt{{kT} over {mc^2}}~~~~ size 18 (2-38) }}
{size 20 color green { %varepsilon_{nx} = %gamma%beta %varepsilon_x=R over 2 sqrt{{kT} over {mc^2}}~~~~~~~~ size 18 (2-39) }}

---
Emittance of Beam from
Photo-cathode (1)
Transverse energy from photo-emission is
With T=0 approximation,
{size 20 color green {E_t = {4%pi m}over{h^3} int_{%mu+%phi-h%nu}^infty d%epsilon_z int_0^infty d%epsilon_t %epsilon_t left [ func exp{left ( {{%epsilon_z+%epsilon_t-%mu} over {kT}} right) } +1 right ]^{-1} ~~~~ size 18 (2-40)}}
{size 20 color green {E_t = {4%pi m}over{h^3} int_{%mu+%phi-h%nu}^%mu d%epsilon_z int_0^{%mu-%epsilon_z} d%epsilon_t %epsilon_t }}
{size 20 color green {{} = {4%pi m}over{h^3} {(h%nu -%phi)^3} over 6 ~~~~~~~~~~~~~~ size 18 (2-41)}}

---
Emittance of Beam from
Photo-cathode (2)
Average of the transverse energy is
The momentum is
Emittance is
{size 20 color green {{} = {4%pi m}over{h^3} {(h%nu -%phi)^2} over 2 ~~~~ size 18 (2-42)}}
{size 20 color green {N = {4%pi m}over{h^3} int_{%mu+%phi-h%nu}^%mu d%epsilon_z int_0^{%mu-%epsilon_z} d%epsilon_t }}
{size 20 color green {%epsilon_{x,y} = E_t over 2N = {h%nu -%phi } over 6 ~~~~~~~~ size 18 (2-43)}}
{size 20 color green {langle p_x^2 rangle = 2m %epsilon_{x,y} = m{h%nu -%phi } over 3 ~~~ size 18 (2-44)}}
{size 20 color green { %varepsilon_x =1 over {%gamma%beta} R over 2 sqrt{{h%nu - %phi} over {3mc^2}}~~~~ size 18(2-45)}}
{size 20 color green { %varepsilon_{nx} = R over 2 sqrt{{h%nu - %phi} over {3mc^2}}~~~~ size 18 (2-46)}}

---
Emittance of Beam from
Photo-cathode (3)
Acounting thermal energy, the transverse energy becomes
The transverse emittance is
{size 24 color green {%epsilon_{x,y} = E_t over 2N = {h%nu -%phi } over 6 + kT over 2 ~~~~~ size 18 (2-47)}}
{size 20 color green { %varepsilon_x =1 over {%gamma%beta} R over 2 sqrt{{h%nu - %phi} over {3mc^2} + kT over mc^2}~~~~~ size 18 (2-48)}}
{size 20 color green { %varepsilon_{nx} = R over 2 sqrt{{h%nu - %phi} over {3mc^2} + kT over mc^2} ~~~~ ~~~~size 18 (2-49)}}

---
Bunch Compression (1)
- In any RF accelerators, the beam should be concentrated in a short period of longitudinal space for small energy spread;
  - E=E0cos(ωt-ks), kds«1 for efficient acceleration.
- Bunch compressor(buncher) shorten the bunch length down to an adequate size for acceleration.

---
Bunch Compression (2)
- There are two ways for bunch compression:
  - Velocity Bunching
  - Magnetic Bunching
- Velocity bunching is effective only for low energy;
  - Some particle source can generate only long bunch or continuous beam.
  - It should be bunched for RF acceleration.
- Magnetic bunching is effective for all energy region.
  - It is employed sometimes to get extremely short buhc after acceleration.
  - It is also used to compensate the bunch lengthning in DR for Linear colliders.

---
Velocity Bunching (1)
- Bunch compression is performed by velocity modulation within a bunch;
  - Bunch head is decelerated.
  - Bunch tail is accelerated.
- Velocity is modulated by energy modulation according to
Velocity is saturated to c at γ>>1. Then, it works only for low energy particle (β<1).
{size 24 color green {c%beta = c sqrt{ 1- 1 over %gamma^2 } ~~~~ size 18 (2-54)}}

---
Velocity Bunching (2)
Energy modulation by RF cavity,
In linear approximation,
Next higher order
{size 24 color green {dE = eV_0 {d sin(%omega t)} over {dt} dt ~~~ size 18 (2-55)}}
{size 24 color green {dE over E_0 sim eV_0 over E_0 %omega dt ~~~~ size 18 (2-56)}}
{size 24 color green {dE_{3} over E_0 sim - {eV_0 over E_0} 1 over 6 (%omega dt)^3 ~ size 18 (2-56')}}

---
Velocity Bunching (3)
{size 24 color green {%tau = L over {c%beta}~~~~ size 18 (2-57)}}
- After energy modulation, drift the beam
- If dτ equals to -dt, all particles are gathered at the bunch center.
- Because all electrons concentrate at t=0 position, RF phase of bunching determines the bunch longitudinal position.
- It works only for low energy.
{size 24 color green {d %tau = - {L over {c %gamma^2 %beta^3}}dE over E}}newline {size 24 color green {~~sim - {L over {c %gamma^2 %beta^3}}{eV_0%omega} over E dt~~ size 18(2-58)}}
eE/e
t
dt
dt

---
Magnetic Bunching (1)
- Energy Modulation : RF cavity.
- Dispersive section : different path for different energy.
- Bunch head (tail) travels longer (shorter) path and bunch length becomes shorter.
By E.S. Kim

---
Magnetic Bunching (2)
- Bunch compression is performed by energy modulation with dispersive path length difference.
  - Chicane, Wiggler, Arc, etc.
- A path length difference by a dispersive section, ∆z is
It works well for any energy particle.
{size 24 color green{ %DELTA z = %eta_l {%DELTA P} over P ~~~~size 18 (2-59) }}
{size 24 color green{ %eta_l = int_L ds %eta over %rho ~~~~size 18 (2-60) }}

---
Common formalism (1)
- Bunching can be formalized with transfer matrix in linear approximation.
- Energy modulation is made by RF (acc- and deceleration).
- Drift space (velocity bunching) or drift through a dispersive section (magnetic bunching) rotates the beam in phase space.
- The bunch rotates 90 deg.
δ(ΔE/E)
z
Drift
Acceleration
Deceleration

---
Common formalism (1)
- Bunching can be formalized with transfer matrix in linear approximation.
- Energy modulation is made by RF (acc- and deceleration).
- Drift space (velocity bunching) or drift through a dispersive section (magnetic bunching) rotates the beam in phase space.
- The bunch rotates 90 deg.
δ(ΔE/E)
z
Drift
Acceleration
Deceleration

---
Common formalism (2)
R-matrices
{size 20 color green {left [ matrix{z(s) ## %delta(s)}right] = left[ matrix{ 1 # R_{56} ## 0 # 1 } right ] left [ matrix{ z(0) ## %delta(0)}right]~~ size 18 (2-60) }}
Drift space:
{size 20 color green {R_{56} =- {L over {%gamma^2 %beta^2}}~~ size 18 (2-61)}}
{size 20 color green {left [ matrix{z(s) ## %delta(s)}right] = left[ matrix{ 1 # R_{56} ## 0 # 1 } right ] left [ matrix{ z(0) ## %delta(0)}right]~~ size 18 (2-62) }}
Dispersive section:
{size 20 color green {R_{56} = %eta_l = int ds %eta over %rho ~~ size 18 (2-63)}}
{size 20 color green {left [ matrix{z(s) ## %delta(s)}right] = left[ matrix{ 1 # 0 ## R_{65} # 1 } right ] left [ matrix{ z(0) ## %delta(0)}right] ~~ size 18 (2-64) }}
RF Energy modulation
{size 20 color green {R_{65}= 1 over z {%DELTA E} over E sim %+- eV_0 over E %omega over {%beta c} ~~~~ size 18 (2-65)}}

---
Common formalism (3)
Total Transfer Matrix of BC section.
Bunching condition : 1+R56R65=0
Velocity bunching:
Magnetic bunching:
{size 20 color green {left [ matrix{z(s_2) ## %delta(s_2)}right] = left[ matrix{ 1 # R_{56} ## 0 # 1 } right ] left[ matrix{ 1 # 0 ## R_{65} # 1 } right ] left [ matrix{ z(s_0) ## %delta(s_0)}right] }}
δ(ΔE/E)
{size 20 color green { { } = left[ matrix{ 1+R_{56}R_{65} # R_{56} ## R_{65} # 1 } right ] left [ matrix{ z(s_0) ## %delta(s_0)}right] ~~ size 18 (2-66) }}
z
R65
{size 20 color green {1+R_{56}R_{65} =1- {L over {%gamma^2 %beta^2}} eV_0 over E %omega over {%beta c}=0 ~~~~ size 18 (2-67)}}
R56
{size 20 color green {1+R_{56}R_{65} =1+ %eta_l eV_0 over E %omega over {%beta c}=0 ~~~~ size 18 (2-68)}}

---
Common formalism (4)
When the bunching condition is satisfied,
The position z(s2) does not depends on z(s0).
This is a good mechanism to stabilize the bunch position.
δ(ΔE/E)
{size 20 color green {{ left[ matrix{z(s_2) ## %delta(s_2)} right] } = left[ matrix{ 0 # R_{56} ## R_{65} # 1 } right ] left [ matrix{ z(s_0) ## %delta(s_0)}right]~~ size 18 (2-68)}}
z
R65
R56

---
Common formalism (5)
Final bunch length after an optimized BC section (1+R56R65=0) is determined by the initial energy spread;
The actual bunch length is also limited
by non-linearity.
{size 24 color green { z_2 = R_{56}%delta_0 ~~~ size 18 (2-69)}}
δ(ΔE/E)
{size 24 color green {z_{nl} = R_{56}{dE_{nl} over E}}}
z

---
Energy Compression
Energy compression is a reverse process of the bunch compression. Bean transfere by dispersive section (R56) and energy modulation (R65) is
Matching condition for energy
compression is
The final energy spread is
{size 20 color green {left [ matrix{z(s_2) ## %delta(s_2)}right] = left[ matrix{ 1 # 0 ## R_{65} # 1 } right ] left[ matrix{ 1 # R_{56} ## 0 # 1 } right ] left [ matrix{ z(s_0) ## %delta(s_0)}right] }}
δ(ΔE/E)
{size 20 color green { { } = left[ matrix{ 1 # R_{56} ## R_{65} # 1+R_{56}R_{65} } right ] left [ matrix{ z(s_0) ## %delta(s_0)}right]~ size 18 (2-71) }}
z
R65
{size 20 color green { 1+R_{56}R_{65} =0 ~~~~ size 18 (2-72)}}
R56
{size 20 color green { %delta(s_2) = z(s_0) R_{65}~~~~ size 18 (2-73)}}

---
Electron Gun

---
Electron Gun

---
Thermionic DC gun
- Thermionic cathode with DC bias.
- It is a conventional gun widely used.
- Continous beam or
- Bunched beam by grid switching, but the bunch length is down to ~1ns.
- Energy at the gun exit is
{size 20 color green {K=(%gamma -1)mc^2 =eV ~~~~~ (3-1)}}

---
Thermionic Gun:
A typical configuration (1)
- The beam emission is controlled by grid bias. The primary bunching and bunch repetition is determined by the grid pulse duration and repetition.
- The bunch length is shortened by bunchers for further acceleration.

---
Thermionic Gun:
A typical configuration (2)
- Electron beam is extracted from thermionic gun continuously.
- RF cavity (Pre-Buncher) modulates the velocity of the electron beam. After some drift, the beam is bunched.
- The bunch repetition is determined by the Pre-Buncher frequency.
- Further bunching is made by SHB and Buncher.

---
Thermionic Cathode
- According to Richardson-Dushman equation, material with low work-function operated at high temperature is favor to generate high density electron beam.
- Practical operation temperature is limited by the operable temperature Te which 10 atomic layers are lost per second at.
- Figure of merit of thermionic cathode is
{size 24 color green { %eta = %phi over T_e ~~~~~ size 18 (3-2)}}

---
Thermionic Cathode
- φ/Te<2.0 is practically used as thermionic cathode.
- Impregnated type BaO cathode is widely used for conventional accelerator.
- CeB6 and LaB6 have advantage for high-brightness beam generation.

---
Photo-Cathode DC Gun (1)
- Electron beam is generated by Photo-emission with laser.
- The bunch structure (repetition and duration) is determined by the laser.
- Beam extraction by a static electric field.
- Beam energy at the gun exit is determined by the bias voltage ,
-V
{size 20 color green {K=(%gamma -1)mc^2 =eV ~~~~ (3-3)}}

---
Photo-Cathode DC Gun (2)
- Because the velocity at the gun exit is slow, the first cavity is “low β cavity”, which synchronizes with the low speed beam.
- Time duration, in which the bunch travels cell length, L, has to be synchronize to the phase advance per cell.
{size 24 color green { L_{cell} = {%DELTA %phi} over {2%pi f} %beta c ~~~~~~ size 18 (3-2)}}

---
Photo-Cathode DC Gun (3)
- In some case, SHB is placed for bunching.
- Low-beta cavity followed by accelerator.

---
HV Operation (1)
- Since the bunch length at the gun exit is determined by the space charge limit, higher voltage operation makes a higher peak current and bunch length can be shorter.
- Short bunch length from gun has merits
  - Simpler bunching section,
  - Energy spread after acceleration is smaller,
For higher voltage operation, dark current by field emission from electrode surface should be suppressed.

---
HV Operation (2)
M. Yamamoto on behalf of F. Furuta

---
HV Operation (3)
- Future light source based on ERL employs PC-DC gun.
- For extremely low emittance, HV operation is essential.
HV terminal
Guard ring
Support rod
Ceramic insulator
Electron
beam
  Anode
 Cathode

---
HV operation (4)
Guard Ring
Segmented Ceremic
- Segmented ceramic.
- Guard ring for FE electron.
- HV conditioning up to 550kV.
- 8 hour stable operation at 500kV without any damage.
- It is a world record of PC DC gun.
FE electron
Support Rod
    Cond. Progress (hour)
R. Nagai, RSI(81)033304(2010)
  Applied voltage (kV)

---
RF Gun (1)
- RF field for beam extraction.
- Electron beam is generated inside of the cavity.
- Laser photo-cathode type is popular.
- Beam from thermionic cathode type has a wide energy spred.

---
RF Gun(2)
- Typical cavity configuration is 1.5 cells.
- TM01, pi-mode.
- Energy at the gun exit is given by
P: RF input power,
R:shunt impedance
{size 20 color green {K=(%gamma -1)mc^2 = int e E(z,t)c%beta(t)dt}}
{size 20 color green {{} = int e sqrt{RP} cos(%omega t - %phi) c%beta(t) dt ~~~~ (3-4)}}

---
Electron source for Linear Colliders

---
ILC Requirements

---
ILC Pulse Structure
Macro Pulse
Micro Pulse

---
Basic Concept
- NEA GaAS cathode with circularly polarized laser is the only solution for polarized electrons.
- Beam extraction by a static electric field (DC photo-cathode gun) because RF gun is not compatible with GaAs cathode.
-V

---
Bunch extraction
Required Laser Pulse Energy
From QE vs Polarization curve, required laser pulse energy is decided.
{size 20 color green {E_L[%mu J] = {124 times Q[nC] }over {%eta["%"] times %lambda[nm]} }}
T. Nishitani et al., J of Appl. Phy. 97,094907(2005)

---
Bunch extraction
Bunch shape
GaAs cathode is only operable in DC bias gun structure. The space charge limit gives possible charge density, J.
Assuming a resonable spot size, the bunch length in time tb is decided to extract 3.2nC bunch charge.
{size 24 color green {J[A/m^2]= 2.33 times 10^{-6} {{ V^{3/2}} over d^2}}}
{size 24 color green { I[A] = JS}}
tb
{size 24 color green {t_b = Q over I}}
S

---
Injector Design
- If the bunch length at gun tb is adequate for RF acceleration, any bunching section is not needed.
- Otherwise, we need a bunching section.
- RF period for the bunching should be long enough comparing to tb for linear modulation.
- RF frequency for the bunching should be harmonics of bunch repetition, i.e. RF of the main linac.
{size 24 color green { T_{bunching} >> t_b}}
{size 24 color green { T_{bunching} = n T_{mainRF}}}
{size 24 color green {n in N}}

---
ILC Electron Source
DC photo cathode gun with GaAs cathode.
Two identical guns are for redundancy.
Buncher for short bunch length.
NC up to 76 MeV followed by SC up to 5 GeV.
Spin rotator and energy compressor

---
Surface Charge Limit (1)
- For Linear colliders, multi-bunch electron beam are generated.
- Anomalous charge limit phenomena is observed (Surface Charge Limit) for high intensity and multi-bunch beam generation.
K. Togawa, NIM A 414 (1998) 431-445
GaAs with a Be-dope 5E+18cm3

---
Surface Charge Limit (2)
- The surface charge limit is caused by Photo-voltage effects;
- Some electrons, Jsurface is captured at BBR(Band Bending Region).
- By the captured electrons, the effective vacuum level is increased.
- Photo-voltage effects decrease size of EA and limit the current.
K. Togawa, NIM A 414 (1998) 431-445

---
Surface Charge Limit (3)
- SCL was compensated by enhancement of the recombination of the captured electron.
- The recombination was boosted by increasing the positive carrier density in VB by high p-doping.
- Finally, 5.0A/cm2 is achieved. It is more than the requirement of ILC gun.
 (a) sample 1b(Na=0.5),
(b) sample 2a(Na=1.0), and
(c) sample 3(Na=2.0). The laser intensity is 1 to 150 W/cm2.
G.A. Mulhollan, Phy. Lett. A 282 (2001)
InGaAsÐAlGaAs SLwith4x1019cm-3

---
Surface Charge Limit (4)
- Super-lattice Cathode has an advantage against SCL.
- Jescape is proportional to the size of NEA.
- The effective size of NEA in Super-lattice cathode is larger than that of bulk-GaAs.
- The escape probability, Jesacape/Jtotal is larger for Super-lattice cathode. SCL current should be higher for Super-lattice cathode.

---
Super-Lattice Cathode
- GaAs/GaAsP super lattice cathode for high polarization (90%) and high QE (0.5%).
- Heavy P (Zn) -doped GaAs surface layer to suppress SCL.
- Cathode is operated in Space charge limit regime.

---
Bunching(1)
- According Child-Langmuir law, peak current of ILC Electron gun (120kV, d~5cm, and 1cm diameter) is ~3A.
- To generate ILC bunch (3.2nC), 1.1ns is necessary.
- It is significantly longer than RF acceleration and should be shorten down to 10ps.
- A special section for this purpose is placed at downstream of Electron gun: Bunching section
- SHB(Sub Harmonic Buncher)
  - 216.7 MHz (1/6 of 1.3 GHz)
  - 433 Mhz (1/3 of 1.3 GHz)
  - Buncher : 1.3 G Hz NC tube.

---
Bunching (2)
- Bunch length is 1ns at the exit of Electron gun.
- Velocity bunching to shorten the bunch length for RF acceleration.
- Acceleration by high gradient RF cavity for the whole bunch, compensates the velocity modulation and the beam becomes rigid.

---
ILC and CLIC comparison
- A similar system to ILC based on Polarized electron source with GaAs cathode is assumed.
- Less bunch charge, but high repetition rate and high average current in a pulse are challenging.

---
Summary
- Fundamentals of electro-emission and electron gun are explained.
- Polarized electron is generated by photo-emission from NEA GaAs cathode with circularly polarized laser.
- ILC and CLIC electron sources are DC bias gun with NEA GaAs.