## Slide 1
Course B: rf technology
Normal conducting rf
Part 3: Linear Collider Hardware
Walter Wuensch, CERN
Ninth International Accelerator School for Linear Colliders
Whistler, British Columbia, Canada
26 October to 6 November 2015

## Slide 2
We will now step back from theory and have a look at specific CLIC hardware.
We have already covered a lot of the theory although there is some more to come.
Still it is a good moment to look at real objects to give a context for all the abstract ideas that you have been seeing.
We will cover:
Accelerating structures
Two-beam concept
PETS (power generating) structures
A little bit about alignment and stabilization
This section will be basically a seminar on the CLIC rf system.

## Slide 3
The CLIC accelerating structure
Now that you have a feeling for the basic mechanisms which underlie high-efficiency acceleration, we will look into the main features of the CLIC rf system.
Let’s start by looking at the CLIC accelerating structure:
The basic component: diamond turned and milled disk. We form a periodic structure by stacking them. The radial lines are damping waveguides
An assembled high-power test structure. Made in a collaboration between CERN, KEK and SLAC.

## Slide 4
Accelerating structure specs.
High-gradient:
100 MV/m loaded gradient
156 (flat top)/240 (full) ns pulse length
Less than 3x10-7 breakdowns/pulse/m
we observe the interrelation

## Slide 5
Accelerating structure specs
Beam dynamics:
5.8 mm diameter minimum average aperture (short range transverse wake)
< 1 V/pC/mm/m long-range transverse wakefield at second bunch (approximately x50 suppression).
but
J. Shi

## Slide 6
Accelerating structure characteristics
Operating frequency: 11.994 GHz
 free space is 25 mm
Operating phase advance: 2/3
CLIC structures are tapered, for reasons of high-gradient performance and wakefield suppression which we will discuss later.
Power flow and beam direction
Number of cells: 26+2
Active length: 230 mm

## Slide 7
Accelerating structure features
Hs/Ea
Es/Ea
Sc/Ea2

## Slide 8
How it looks

## Slide 9
Higher-order mode damping
Cell | First | Middle | Last
Q-factor | 11.1 | 8.7 | 7.1
Amplitude [V/pC/mm/m] | 125 | 156 | 182
Frequency [GHz] | 16.91 | 17.35 | 17.80

## Slide 10
Accelerating structure characteristics cont.
The aperture radii range from 3.15 to 2.35 mm with iris thicknesses of 1.67 to 1.00 mm. The resulting rf parameters are:
 | first | last
vg [%c] | 1.65 | 0.83
R’/Q [kΩ/m] | 14.6 | 17.9
Q | 5536 | 5738
R’ [MΩ/m] | 81 | 103

## Slide 11
The fundamental mode properties are shown in the regular cells.
The traces from top to bottom are:
Sc·50 [W/μm2](pink),
surface electric field [MV/m](green),
accelerating gradient [MV/m](red),
pulse surface temperature rise [K](blue).
Dashed traces are unloaded and solid are beam loaded conditions.
Whole structure properties

## Slide 12
How to make ‘em
Machining: OFHC copper diamond milled and turned disks with micron precision.
+- 5 micron tolerance lines

## Slide 13
Evolution of the micron-precision market
The market for micron precision parts has evolved over the last decades.
Linear colliders are not alone.
1970’s
1980’s
1990’s
2000’s
2010’s
Optical recording
Imaging Optics
Mirror optics
Injection molding of contact lenses
Freeform optics
Optical recording was the driving force to achieve higher accuracies
  Form accuracy: 150 nm  50 nm
  Roughness Ra : 5 nm  2 nm

## Slide 14
Evolution of machining capability
Up to the 1980’s
1980’s - 1990’s
2000’s - 2010’s
Larger machines
Multiple axis ( X/Y/Z and C)
Future ?
Intelligent machines ?
  Robotisation ?
Pallet machining?
  Robotisation ?
First machines at research institutes and universities
Start of industrialization
Optical recording
contact lenses
Single point diamond turning
Up to the 1990’s
1990’s - 2000’s
2010’s
Future ?
Ultra precision diamond milling (lagging more than a decade behind on turning)
Limited to fly cutting
mirror optics
Laser scanner mirrors
First proto type machines
Micro fluidics
Accelerator parts
Milling as add-on on lathes
Lens arrays
Intra ocular lenses

## Slide 15
Bigger structures, same tolerances
  Started at ø35mm – now at ø80mm – in future up to ø200mm ?
Tight accuracy specifications for series manufacturing
  Moulds for DVD optics :
    50 nm form accuracy on ø 2 mm
    equals ratio of 1 / 40000
  CLIC disk -> series part
  2 µm accuracy on ø 80 mm
  equals ratio of 1 / 40000
Current challenges for the basic technology

## Slide 16
High accurate Machining
5-axis CNC turning milling machine
Technical characteristics:
X axis travel 350 mm
Y axis travel 150 mm
Z axis travel 300 mm
B and C axis travel 360 degrees
Swing capacity up to 20‘’
Air bearing Turning spindle 10,000 rpm
Air bearing Milling spindle 60,000 rpm
Precision
34 picometers resolution rules (0.034 nanometers)
Incremental programming 0.01 nanometer
Axial and radial spindle error ≤ 25 nanometers
B axis axial and radial error ≤ 100 nanometers
Shape defect ≤ 0.15 μm on diameter 75 mm
Surface finish Ra ≤ 3.0 nanometers
Machine delivered on january 2011
First structure TD24WFM delivered on novembre 2011.

## Slide 17
High Accuracy Machining
Results :
PV = 0.807 µm
Ra = 0.002 µm
RmS = 1,72 nm
Results :
PV = 0.335 µm
Ra = 0.001 µm
RmS = 1,92 nm
Aluminum mirror for satellite application on its support delivery
Copper disk - accelerating structure

## Slide 18
Métrology mark
Milling surface finish improvement
Results

## Slide 19
Iris machining
The machining of the iris start from diameter 20mm to erase milling perturbation in the center.
The height of the step is about 1µ.
Ra between 2nm to 5nm

## Slide 20: VDL ETG Industry Commitment
Investments in new skills
  H2 bonding
  Micro milling
  Pallet machining
  On machine metrology
Investments in people
  Cooperation programs with schools, universities, institutes
  Internal education
  Career paths
Investments in infrastructure
  Equipment
  New Facility
Guidance is required to steer investments in the right direction

## Slide 21
Accelerating structures – manufacture
TD18#3 at SLAC
TD18#2 at KEK
Stacking disks
Temperature treatment for high-gradient
Structures ready for test

## Slide 22
Diffusion bonding of couplers under H2 at 1 bar
    Done at Thales Electron Devices (TED) – Velizy (France)
    Degreasing and etching at CERN before bonding
    Applied weight: 43 kg equivalent to ~ 0.13 MPa; thermal cycle: flat top at 1035°C during 1h30
    Process validated on a test coupler: observation of crossing grains in the joint plan
    Some deformations observed on the outer faces after bonding : ~0.1 mm -> re-machining done
Coupler
Extremity cell
SEM observation of bonding plan after cutting
Crossing grains
Crossing grains
Thermal cycle
Assembly of couplers in the furnace

## Slide 23
Diffusion bonding of structure under H2 at 1 bar
    Also done at TED with degreasing and etching at CERN before bonding
    Applied weight: 33.7 kg equivalent to ~ 0.08 – 0.12 MPa;
    Same thermal cycle as couplers but with flat top at 1010°C
    No deformations observed on the external diameter after bonding
Disks after etching
Coupler
Assembly of disks in the furnace
Geometrical measurements on external diameter after bonding
Alignment = 9µm for ACS#1 and 12.6 µm for ACS#2
Angle = 90.0514° for ACS#1 and 90.0087° for ACS#2
Structure n°1
Structure n°2

## Slide 24
Assembly of accelerating structure accessories
    Done at Bodycote – Villaz (France) and CERN
    Tuning studs and cooling circuits brazed with copper gold alloy below 1000°C under vacuum
    Good tightness and no drip of alloys observed in the cells
    Assembly test by screwing of WFM waveguides OK
Assembly of WFM waveguides
Assembly of cooling circuits
Assembly of tuning studs
S. Lebet

## Slide 25
Bead-pull and RF tuning of structure n°1
    Done at CERN by Jiaru Shi the 22th of Feb. 2012
    Target frequency: 11991.65 MHz (considering freq. shift due to wire, nitrogen and temperature of 21.6 deg)
    All disks tuned with only one stud used for each disk
    Very successful tuning

## Slide 26
Bead-pull and RF tuning of structure n°2
    Same procedure as structure N1, done the 6th of March 2012
    Disk 13 tuned by -10 MHz (the 4 studs were used), all the other
    disks were tuned +/- 3MHz like structure N1
    Very successful tuning also

## Slide 27: Engineering Design Overview
BEAM
DIRECTION
1st AS
2nd AS
243.701 mm
502.5 mm
COOLING TUBE
VACUUM MANIFOLD
& COOLING SYSTEM
COOLING FITTING
WAVEGUIDE
INTERCONNECTION
WFM WAVEGUIDE
VACUUM FLANGE
BONDED DISC STACK
RF FLANGE
ALIGNMENT
VACUUM PORT
VACUUM PORT
BEAM
DIRECTION
Compact coupler design (already in TD26 CC);
The body of an AS formed by high-precision copper discs joint by diffusion bonding at 1040 °C;
Two AS are brazed together to form a superstructure (SAS);
The SAS has 8 vacuum manifolds and 4 Wakefield Monitor (WFM) waveguides;
The cooling system is integrated into the vacuum manifolds in order to provide a more compact technical solution.
Slide from Anastasiya Solodko

## Slide 28
Average loaded accelerating gradient | 100 MV/m
Frequency | 12 GHz
RF phase advance per cell | 2π/3 rad.
Average iris radius to wavelength ratio | 0.11
Input, Output iris radii | 3.15, 2.35 mm
Input, Output iris thickness | 1.67, 1.00 mm
Input, Output group velocity | 1.65, 0.83 % of c
First and last cell Q-factor (Cu) | 5536, 5738
First and last cell shunt impedance | 81, 103 MΩ/m
Number of regular cells | 26
Structure length including couplers | 230 mm (active)
Bunch spacing | 0.5 ns
Bunch population | 3.72×109
Number of bunches in the train | 312
Filling time, rise time | 67 ns, 21 ns
Total pulse length | 243.7 ns
Peak input power | 61.3 MW
RF-to-beam efficiency | 28.5 %
Maximum surface electric field | 230 MV/m
Maximum pulsed surface heating temperature rise | 45 K
Accelerating structure parameters

## Slide 29: Main Linac Tolerances
Test of prototype shows
  vertical RMS error of 11μm
  i.e. accuracy is approx. 13.5μm
2) Beam-based alignment
Stabilise quadrupole
O(1nm) @ 1Hz
Pre-align BPMs+quads
accuracy O(10μm) over about 200m
3) Use wake-field monitors accuracy O(3.5μm)

## Slide 30: Active Stabilization
 | B10
No stab. | 53%/68%
Current stab. | 108%/13%
Future stab. | 118%/3%
Luminosity achieved/lost [%]
Machine model
Beam-based feedback
Code
Typical quadrupole jitter tolerance O(1nm) in main linac and O(0.1nm) in final doublet
Final Focus QD0 Prototype
Close to/better than target

## Slide 31
Elements of CLIC two-beam

## Slide 32: Two-beam RF components
ON/OFF mechanism
PETS
high-power
as short as possible
low longitudinal and transverse impedance
On/ramp/off
necessary (?) to react to breakdown and/or failure
Choke mode flange
independent alignment of main and drive beam
Accelerating structure
high-gradient
as long as possible
micron precision
transverse wake-field suppression
Waveguide network
high power
precise phase length

## Slide 33
The early days of multi-TeV linear colliders

## Slide 34
 | PETS | Accelerating structure
Aperture radius [mm] | 11.5 | 3.15-2.35
R’/Q [kΩ/m] | 2.2 | 15-18
vg/c | 0.49 | 0.0165-0.0083
Gradient [MV/m] | -6.3 | +100
CLIC two-beam in numbers

## Slide 35
T3P: Wakefield Coupling PETS <-> TD24
PETS
TD24
Combined mesh model with 21M elements (h~0.5mm)
(preliminary coupler geometry)
IWLC10 A. Candel

## Slide 36
PETS
… and Simulation of RF power transfer
T3P models realistic, complex accelerator structures with unprecedented accuracy
Low group velocity requires simulations with 100k time steps
p=1: 15k CPU hours p=2: 150k CPU hours
p=3: 1.5M CPU hours
…

## Slide 37
PETS – specifications
High-power:
135 MW output power
170 (flat top)/240 (full) ns pulse length
<2x10-7 1/pulse/m breakdown rate
Beam dynamics:
Fundamental mode: gives 23 mm diameter aperture which corresponds to a/=0.46 and vg/c=0.49 to give 2.2 kΩ/m, longitudinal impedance
Single bunch transverse wake: < 8 V/pC/mm/m
Long-range transverse wakefield with effective suppression of main HOMs by Qn(1-n)<8 each

## Slide 38
PETS parameters
Aperture, mm | 23
Iris thickness. mm | 2.0
Cell length, mm | 6.253
Phase advance/cell, degrees | 90
Corrugation depth, mm | 4.283
R/Q, Ohm/m | 2290
=Vg/c | 0.453
Q-factor | 7200
Active length, m | 0.213 (34 cells)
RF pulse length, ns | 241
Drive Beam current, A | 101
Output RF power, MW | 133.7
Peak surface electric field, MV/m | 56
Peak surface magnetic field, MA/m | 0.08
Pulsed temperature rise, 0C | 1.8
Breakdown trip rate, 1/pulse/meter | 110-7

## Slide 39
Surface electric field
Surface magnetic field
PETS – fundamental mode characteristics
Beam-driven structure so power rises quadratically with current and length,
135 MW for 100 A beam
213 mm active length
Maximum fields at output with values,
Esurf=56 MV/m
ΔT=1.8 (Hsurf=0.08 MA/m)
Sc=1.2 MW/mm2

## Slide 40
Overmoded couplers for PETS

## Slide 41
PETS – HOM suppression features
ACE3P analysis of HOM properties
GdfidL and ACE3P benchmarking with analysis of PETS HOM properties
PETS for high-power testing with SiC absorbers installed.

## Slide 42
PETS – the high-power testing challenge
To high-power test the PETS in nominal conditions would require a 100 A driving beam.
“Waveguide” test with klystron/pulse compressor
not many 135+ MW X-band power sources – ASTA at SLAC
much harder to run, full fields at input
Beam-based tests with CTF3 4-30 A beam.
1000 mm long PETS
Connect output to input – beam-driven rf resonant ring for lower, <10 A, current
Fields in CLIC and CTF3 at high current
Fields in klystron and recirculation tests

## Slide 43
PETS testing in ASTA
Two klystrons
50 MW@1.5us
SLED II with variable length and iris reflection
Experimental area
Uncompressed arm
Gate valve
Rf Phase
shifter
ASTA layout
PETS waveguide-mode PETS testing is being done at ASTA in SLAC an impressive facility but testing a single object with 135+ MW power is very challenging. The results you will see are a mixture of conditioning of the PETS and ASTA…

## Slide 44
load
Reflection
Transmission
ASTA test PETS version with damping slots and damping material (SiC)
Low RF power measurements
June 2010

## Slide 45
Part of the statistical distribution contributed to the BDR calculation
1.55x107 pulses were accumulated in a 125 hour run.
8 PETS breakdowns were identified giving a breakdown rate of 5.3x10-7/pulse.
Most of the breakdowns were located in the upper tail of the distribution, which makes BDR estimate rather conservative.
During the last 80 hours no breakdowns were registered giving a BDR <1.2x10-7/pulse.
Extraction of PETS breakdown trip rate
1.55x107 pulses

## Slide 46
TBTS is the test area in CLEX, where feasibility of the CLIC two beam acceleration scheme is…already demonstrated (not yet at a nominal 100 MV/m accelerating gradient).

## Slide 47: TBTS: Two Beam Acceleration
Consistency between
produced power
drive beam current
test beam acceleration
Maximum gradient 145 MV/m
CTF3 team
TD24

## Slide 48: Optimization procedure
Bunch population
Structure
parameters
Cell parameters
Bunch
separation
Beam
dynamics
<Ea>, f, ∆φ, <a>, da, d1, d2
N
Ns
Q, R/Q, vg, Es/Ea, Hs/Ea
Q1, A1, f1
η, Pin, Esmax, ∆Tmax
Ls, Nb
rf
constraints
Cost function
minimization
YES
NO
Beam
dynamics

## Slide 49: Beam dynamics input
High-power RF optimum aperture: <a>/λ = 0.1 ÷ 0.12
Why X-band ?
Crossing gives
optimum frequency
FoM =Lbx/N · η
BD
RF
BD optimum aperture:
<a> = 2.6 mm
Lbx/N

## Slide 50: The CLIC Layout
Drive Beam Generation Complex
Main Beam Generation Complex