## Slide 1: Analysis Test Beam Pixel TPC z deformations
Peter Kluit, Michael Lupberger, Jan Timmermans
LC TPC-pixel meeting 28 January 2016

## Slide 2: Chip 10 z deformations
Left bottom residuals xy of right top distribution
Left right the pulls = residual/error
Z beam profile on chip 10
Residual flat
Reason for flatness is that the chip 10 is reference for alignment

## Slide 3: Chip 10 z residual deformations
Spit chip 10 in four zones in y pixels:
0-64, 64-128, 128-192,192-256
Residuals have structure
Left bottom gives the residuals of the 4 zones
Right pulls
Residuals have 30 micron rms and pull 1.2. So add sys error of 15 microns

## Slide 4: Chip 10 z deformations if all z hits used in fit

## Slide 5: Chip 10 z residual deformations if all z hits used in fit
Same observation of additional syst of 15 microns if one studies the zones

## Slide 6: Chip 153 z deformations if all z hits used in fit
Also chip 153 is a reference chip for alignment that gives a flat distribution

## Slide 7: Chip 153 z residual deformations if all z hits used in fit
Similar conclusion as for chip 10. There is additional syst of about 15 microns in the zones

## Slide 8: Chip 1 z deformations if all z hits used in fit
Chip 1 is NOT used as a reference.
Observe a structure in the residuals of 27 microns. The pull is 2.6. So beyond stats.
So 25 microns syst

## Slide 9: Chip 1 residual z deformations if all z hits used in fit
The common shifts shown in previous slide are subtracted
Same conclusion as for chip 10 and 153 of additional sys of 15 microns

## Slide 10: Chip 6 z deformations if all z hits used in fit
Chip 6 has additional syst of 25 microns

## Slide 11: Chip 6 residual z deformations if all z hits used in fit

## Slide 12: Chip 13 z deformations if all z hits used in fit
Chip 13 has
syst of 20 microns

## Slide 13: Chip 13 residual z deformations if all z hits used in fit

## Slide 14: Chip 150 z deformations if all z hits used in fit
Chip 150
Additional syst 70 microns
Quite bad

## Slide 15: Chip 150 residual z deformations if all z hits used in fit

## Slide 16: Chip 141 z deformations if all z hits used in fit
Chip 141
additional sys
35 microns

## Slide 17: Chip 141 residual z deformations if all z hits used in fit

## Slide 18: Chip 138 z deformations if all z hits used in fit
Chip 138 additional syst 22 microns

## Slide 19: Chip 138 residual z deformations if all z hits used in fit

## Slide 20: Overview all chips
chip rms pull rms syst
1 0.0271938 2.61763 0.023225
6 0.0311058 3.60138 0.0287075
10 0.0109067 1.53113 0.00625438
13 0.0247628 3.1621 0.0222863
17 0.0278677 3.43124 0.0255007
22 0.0267972 3.08028 0.0239729
26 0.0259569 2.68479 0.0223558
29 0.0262465 2.43372 0.0218152
66 0.0257813 2.26379 0.0207505
69 0.0257808 1.93203 0.0188741
82 0.0235697 2.51261 0.0198363
85 0.0275432 2.8435 0.0241367
90 0.03673 3.31217 0.033382
93 0.0267364 2.74584 0.0231903
134 0.0418711 3.44197 0.0383368
138 0.0261769 2.87476 0.0230094
141 0.0334069 3.46663 0.0306271
150 0.0444011 3.06263 0.0396674
153 0.0115297 1.38851 0.00554944
systematics
chips 10 and 153
6 microns
All others
19 to 40 microns
Trend chips 90 to 153 worse than others