SiW-ECAL optimisation
Vincent Boudry
for the SiW-ECAL group
ILD SW & Optimisation meeting
DESY, 24/02/2016

---
What is (still) needed for ILD ?
Most studies already done, some needs to be refined:
  1. Radius studies with realistic models	<= issue for cost
    1. Wafers thickness ⇒ Energy resolution
  2. Lateral granularity (cell size)
    1. Dependent on the (HCAL/ECAL correlation) ⊗ SW
  3. Radial granularity (number of layers): to be continued.<= issue for	cost
     What about other correlation ?
1. Threshold studies ?
2. Timing ?
  1. Do we have time for time ?

---
Cost / performance optimisation
Current situation (~correct)
Constly refined
New since Sept 2014
On going
based on V. Balagura review for the CALIIMAX ANR
⚠ on-going work

---
Radius studies
with Jets & Tau’s
1. Latest results from T. H, Tran presented on sept 2015
  1. Paper submitted to EPJC arxiv.org/abs/1510.05224
  2. Using GARLIC and 3 radii, and B Field
    a reduction of the SiW ECAL radius by about 20% and with the same granularity, ILD can still provide a measurement of the π0 mass with a resolution of better than 10% while the tau reconstruction efficiency degrades compared to the baseline design by at most 2%. The improvement of the efficiency does not justify to increase the magnetic field from 3.5 to 4 T.
2. Jet Energy Resolution:

---
Lateral granularity (cell size)
1. (HCAL/ECAL correlation) ⊗ SW:
  (PandoraPFA & AHCAL) vs (ARBOR & SDHCAL)
Threshold &
Dead zone ?
Is a threshold at ½ mip sufficient ?
¼ of mip seems technically feasible...

---
Radius studies with realistic models.
1. Should we restrict to 3 sizes for realistic simulation ?
  SiW-ECAL wafer is a quantum for ILD dimensions	(not true for Scintillator opt.)
    Wafer size standard + Price ⇒ cassettes dimensions
      R from Endcaps,
       𝓏½ from Barrel
  Make things complicated for simulation
  to go in step of 26 or 13 cm (1 cassette, ½ cassette)
    ≠ the standard inner→outer onion construction of dimensions (à la Mokka)
2. ⇒ Cost / Perf optimisation
  1. Wafers thickness ⇒ Energy resolution

---
Realistic parameters: on-going
1. From preliminary mechanical model ⇒ in simulation & cost
2. Reduced radius RINNER= ~1600 and~ 1400mm.
3. Base unit = Wafer size
  1. Largers Wafers: 6” → 8” (OK from HPK, LFoundry); smaller wafers (4”) in 2nd part ?
  2. Wafer side: ~90 → 126–130 mm; Alveola ~200mm→ 253,8 mm – 263mm (132.3mm for single SLAB)
4. Barrel: 5 modules of 3 alveola
  1. LBarrel = 3829mm (Zendcap = 3929mm).
5. Endcaps: Quadrants of 2 modules of 2 and 3 alveola
  1. with R(ECAL Ring) = 40cm + Integer number of Wafers + ½ Wafers
    ⇒ REndcap = 1676mm
6. Nlayers = 22 = 14 + 8 (single and double W thickness)
7. Wafer thickness 500→ ~725μm
  1. Improved σ(Eγ) ∝ 5√t ⇒ ~recovery of Nlayers effect. ⇒ compensation of NLayer loss.
  2. ECAL thickness = 223,85 mm
Preliminary numbers
(and not necessarily consistent)
Enginering plans on-going

---
Geometry studies
Henri Videau
Depth of the calorimeter
as a function of angle
+ L(X0) @ φ=0 @ φ=π/4
Overlap corner
Baseline design

---
Geometry of endcaps
1. Magic numbers for
   limited types of wafers
  1. linked with size of
     the ECAL Ring.
     (⇔ QD0 size)

---
Example of geometry
1. Model 3 (~1400mm)
2. + Model 1 (~1600mm)
HV ©
Preliminary numbers
Enginering plans on-going
2,5 alveoli
3 alveoli
3 alveoli
3 alveoli
2 alveoli
3 alveoli
3 alveoli
2,5 alveoli

---
Internal structure with reduced number of layers
''
HV ©
No more « strange layer »
No pre-sampler
(used for correction
of overlapping region)

---
Simulation modifications
Slide from Sept 2014
1. Cleaning & adapatation of ECAL Mokka drivers:
   [D. Jeans + J. Marshall + E. Becheva + V. Boudry + Dan Yu]
  1. Many cleaning made by D. Jeans ⇒ SECal05
    1. Bugs, improved GEAR output, handling of pre-shower
  2. Documentation being reviewed
  3. TBD: Implementation of SEcal05 in DDHEP
     (based on S. Lu implementation of SEcal04 + tests)
    1. Done for CLICdp by D. Protopopescu & M. Petric
       Needs to be review / adapted for ILD vs SECal04
2. New ECAL Driver (SEcal06) to correct defects (mostly in Endcaps).
  1. Missing dead materials, “corners”
  2. Consistant treatment of Barrel/Endcaps
  3. Better handling of Layers, optionnal pre-shower
Status of Sept 2014

---
Timing ?
1. CMS-HGCAL and ATLAS-HGTD are investigating precise time for vertex separation
  1. 50ps timing precision for single cells
  2. ➘ ~10 ps for EM shower
  3. electronics (CEA / Omega) is being
     developped for this
3. Benefits in terms of PFA ?
  1. Certainly in HCAL
    in SiW-ECAL ?
4. But do we have time for time ?

---
Conclusions
1. Most studies done with «flexible models» of sim.
  1. Fine for barrel, be aware of |cosθ| > 0.7
  2. Correlations and holes to be scanned for… (+ threshold, wafer thickness)
2. Lower radius models being looked at
  1. Engineering “safe” in barrel-endcap region
  2. Larger wafers wrt to baseline,
  3. Thicker wafers
    1. Study of 725μm vs 500μm vs 320μm needs to be completed
  4. Calculations “almost” there…
3. Simulation needs to be adapted (with model in DDSIM)
4. ...Timing...

---
Extras

---
Variation of NLayers
1. Shown @ 6th ILD Optim meeting (16/07/2014) [Internship work of Dan Yu (LLR)]
   https://agenda.linearcollider.org/getFile.py/access?contribId=2&resId=0&materialId=slides&confId=6435
  1. Variation of ECAL's NLayers for R=1450mm, HZBarrel=1848mm
     on ILD_o2_v05
  2. Exact Same procedure
     as previous study
    1. Non-Linearity ≤ 1%
  3. For |cosθ| ≤ 0.7
2. Results
  1. JER + ≤6% @45 GeV

---
 Single jet energy resolution as a function of the thickness of PCB with
embedded electronics.
Single photon energy resolution as a function of the number of silicon
layers for four photon energies.
 Single jet energy resolution (rms90=E ) in the barrel region (j cos j <
 0: 7) as a function of the number of ECAL silicon layers in events e+e-→ ZX → usd
 ILD jet energy resolution in the barrel region j cos j < 0: 7 as a
function of its radius.

---
Guard Ring studies
 An ECAL average signal versus azimuthal angle. The loss in
inter-sensor dead areas is visible (between barrel modules, barrel and endcap
and between the sensors, the latter depends on the guard ring).
 the single jet energy resolution after a simple dependent correction as a function of the guard ring thickness.

---
Resilience

---
Model 3