## Slide 1: Recent Status of 40mm Input Coupler
Kirk
Y. Yamamoto, A. Yamamoto, T. Matsumoto, E. Kako (KEK)
E. Montesino (CERN)

## Slide 2
Ultra-pure water rinsing  assembly work in Class10  Leak check  Low power test  Baking
Cold part #1 has problematic copper plating.
But, as now, it’s not significant in high power test!

## Slide 3
Final low power test at test bench before connecting to waveguide system
S11=-36.6 dB, S21=-0.13 dB
adjustable

## Slide 4
Connection to waveguide system
Pumping starts
(coupler has been under vacuum
after assembly work in clean room)

## Slide 5
Final setup for RF coupler conditioning
We are monitoring RF power, vacuum, temperature for coupler outside, arc sensor output and electron probe output.
Step of RF pulse width: 10μsec  30μsec  100μsec  500μsec  1500μsec  1650μsec (TDR spec.)
Max. Power for each RF pulse width: 1200kW @< 500μsec
800kW @> 500μsec
Arc sensor at warm window
e- probe at cold window

## Slide 6
Signal name | I/L threshold
Pfor@up, Pback@up, Pfor@down | Pfor@up < 1.3 MW, Pback@up < 10 kW
Cold / Warm Vacuum | 1 ~ 2 x 10-4 [Pa] (4 x 10-4 [Pa] @temporary)
Arc #1, #2 @waveguide | 2000/6500, 2000/7000
Arc Up, Arc Down | 2000/6090, 2000/6550
Electron peak-hold #1, #2 | 
Electron charge #1, #2 | 
Temperature #1 ~ #12 | 
VSWR @up, down | < 1.4
Cooling water | < ?
List of Signals and I/L level

## Slide 7
Arc #1
Arc up
Arc down
Arc #2
e− #1
(peak, Q)
e− #2
(peak, Q)
Pforward
Pforward
Pbackward
Pbackward
Cooling water @Dummy Load
Warm Vac
Cold Vac
upstream
downstream

## Slide 8
History of RF Conditioning @Test Bench
Date | Content | Result
12/Jan |  | 
15/Jan | Klystron #2 ON, RF ON, Power meter setting | 27.9 kW @10μsec/5Hz
18/Jan |  | 43.0 kW @10μsec/5Hz
19/Jan |  | 61.0 kW @10μsec/5Hz
20/Jan |  | 149 kW @10μsec/5Hz
21/Jan | Arc I/L ON | 207 kW @10μsec/5Hz
22/Jan |  | 312 kW @10μsec/5Hz
25/Jan |  | 500 kW @10μsec/5Hz
26/Jan |  | 861 kW @10μsec/5Hz
27/Jan | 10μsec/5Hz finished | 1200 kW (1hour keep) @10μsec/5Hz
28/Jan |  | 1211 kW (1hour keep) @30μsec/5Hz
29/Jan | 30μsec/5Hz finished | 1215 kW @100μsec/5Hz
1/Feb | 100μsec/5Hz finished | 1216 kW (1hour keep) @100μsec/5Hz, 604 kW @500μsec/5Hz
2/Feb | 500μsec/5Hz finished | 1200 kW (1hour keep) @500μsec/5Hz
3/Feb | Fan x 2 ON | 818 kW (1hour keep) @1500μsec/5Hz
4/Feb | Fan x 4 ON, 1500μsec/5Hz finished | 607 kW @1650μsec/5Hz
5/Feb |  | 708 kW (1hour keep) @1650μsec/5Hz

## Slide 9
Chart: net time [h:m]
1500[μsec] | 0.27778
500[μsec] | 0.33403
100[μse] | 0.25764
30[μsec] | 0.29375
10[μsec] | 2.4528
Preliminary
1650μsec/700kW (final goal)

## Slide 10
Trend Graph for Coupler Conditioning under 500μsec/5Hz
Preliminary
Pforward
Pbackward
VACwarm
VACcold
Electron #1
Electron #2
Pforward
Pbackward
1200kW
1200kW
Interlock level
Interlock level

## Slide 11
Pulse width : 500[μsec]
Rep. rate : 5 [Hz]
Down data
Scattered Plot for Coupler Conditioning under 500μsec/5Hz
Preliminary
Interlock level
Interlock level

## Slide 12
30 μsec / 5 Hz
1650 μsec / 5 Hz

## Slide 13
Summary of STF-2 coupler conditioning at test bench
Chart: 
| 11&12 | 13&14 | 15-17&16-18 | 17-15&18-16 | 21&22 | 23&24
10[µsec] | 1.0729 | 3.0632 | 1.1722 | 2.0653 | 1.3563 | 0.76458
30[µsec] | 0.15278 | 0.16528 | 0.32292 | 0.20347 | 0.15278 | 0.17083
100[µsec] | 0.19028 | 0.12986 | 0.14861 | 0.14306 | 0.125 | 0.080556
500[µsec] | 0.21528 | 0.19167 | 0.15417 | 0.086806 | 0.18194 | 0.12083
1500[µsec] | 0.23681 | 0.11319 | 0.13264 | 0.10069 | 0.22083 | 0.10069
44:50
87:55
46:20
62:23
48:53
29:42

## Slide 14
Incoming inspection
After rinsing
After RF conditioning (Today!)
These are not same photos!