## Slide 1: Questions from CRWG (Central Region Working Group)
K. Yokoya
2016.2.25 ADI

## Slide 2: Auxiliary Positron Source
Couple of choices have to be made for the work of CRWG
One of them is the parameters of the “Auxiliary Positron Source” (Let’s abbreviate as APS)
It is to provide a (weak) positron beam for the time when the undulator positron source is not available
Its specification in TDR is poor (10 lines in vol.3 part.2 p.91)
  500MeV S-band NC linac
  Single bunch (intensity ~1%)
    This presumably means 0.01/1312 = 10-5 of the nominal intensity
  8 SLAC-type 3m-structures, 4 RF stations, each with a 100MW modulator, 50kW klystron and SLED
  Location: side-by-side with the photon line from undulator. Share the target with the undulator source.
  Length ~40m

## Slide 3: Roles of the APS
Commissioning of positron DR, RTML, ML, BDS
  Commissioning of DR can start 1.5 years earlier than ML (TDR vol.3 part.2 p.245). No undulator source available at that time.
KAS (Keep Alive Source)
  Keep DR etc tuned while the electron ML is in (long) shutdown (due to any reason)
  Really needed?
Positron beam for detector calibration at Z-pole
  Does not require 10Hz operation
  Parameter Group (led by Jim Brau) is making an inquiry to the detector groups on the calibration demand
    Time scale: Santander WS
  Presumably, the APS is too weak even for calibration.
APS is not needed when we start with e-driven positron source, so this question is not necessary. But CRWG will concentrate on undulator scheme.

## Slide 5: Question A
How high an intensity of the APS required for commissioning (and KAS)?
  Bunch charge, number of bunches

## Slide 6: Possible intensity of APS
Should not invest much money
But please forget about the specification in TDR for now
Bunch intensity can be >1% ?
Can store more bunches in DR by repeated use of S-band pulse (ignore 5Hz for commissioning)
  But 5GeV booster SC linac can work only at 5Hz (10Hz?)
Many bunches in single S-band pulse may require additional injection kicker to DR (space?)

## Slide 7: Commissioning
Check items
  Basic check of hardware (such as magnet polarity)
  Check of injection/extraction kickers
  Fine tuning for low emittance
  Instability such as e-cloud
  Beam loading
  Scrubbing of vacuum chamber
  else
Obviously, for some of these items, we must wait for completion of electron ML and the undulator source

## Slide 8: Question B
Can the APS be replaced with an electron source? (in particular for the DR)
  Hardware possibilities
    Add an electron gun just before 5GeV booster of positron
    Or use the normal electron source and add an injection line to positron DR
  Sense of circulation in DR
    Normal direction in positron DR (requires magnet polarity change) or the opposite direction (requires injection line and, if also used for RTML commissioning, extraction line)
  Can be full intensity if strongly desired
  May be useful if somebody want electron-electron collision

## Slide 9: Deadline of the Answers
No rigorous deadline, but we will be happy if we can get answers by CRWG meeting on Mar.15 (if not Mar.1)