タイトル
Photon Dump Design of ILC Positron Source
ECFA LC 2016, 31 May-4 June, 2016, Santander, Spain
Masao KURIKI

---
概要
Introduction
- Photon beam power from undulator is 320kW.
- Only 21kW is absorbed by the production target and other photon goes to the dump.
- Photon beam size is determined by L/γ (Drift length and gamma factor) resulting <1.0mm.
- 300kW photon flux in 1mm should be absorbed safely with the dump.
- The power is almost same as that in other dump (e.g. 400kW tune up dump), but instantaneous temperature rise could be critical.

---
長期目標

---
現在状況
Photon Dump Design
- 10 cm diameter with 100 cm long pressurised (12 bar) water vessel with a Ti window, with a radioactive-water processing system (TDR).
- 300 kW continuously (2 × 1017 photons/sec of 10 MeV average energy produced with a 3 μrad angular spread.)
- 500 + 150 m photon drift gave 1mm spot size.
- Ti window is 0.5 kW/cm2 425 C for one train (2600).
- The water temperature rise would be 190 C.
- 10cm steel and 40 cm concrete shield is enough for shielding, because absorbed power is less than the tune up dump.

---
現在までの発展
Photon Dump Geometry
Water circulation and processing
  3.0 kg/s
40cm concrete
10cm iron
Beam pipe
Water in Ti Vessel
2m
1.1m

---
代替案

---
推薦
3.0kg/s for the photon dump (1/50 of the main dump)

---
Summary
- 300kW photon dump is required to absorb the photon from undulator.
- 10 cm diameter with 100 cm long pressurized (12 bar) water vessel with a Ti window, with a radioactive-water processing system.
- 425 C temperature rise for Ti window for one train (2600) is expected.
- The water temperature rise would be 190 C.
- Water processing system is 50 times less than that for the main dump.