A Positron Capture Simulation
for the E-driven ILC Positron Source
Masao KURIKI (Hiroshima University)

---
Introduction
- Electron driven ILC Positron Source is considered to be a technical backup of the undulator ILC Positron source.
- It is designed based on NC accelerators operated in 300Hz.
- In the first simulation done by T. Omori, T. Tahakashi, et al.
  - Positron generation was simulated with GEANT4.
  - The positron capture is evaluated only with the capture linac up to 250 MeV.
  - Constant gradient 20MV/m is assumed and the beam-loading effect is not considered at all.

---
Second simulation was done by Y. Seimiya, M. Kuriki,et al.
  - It was a start to end simulation including Chicane, booster, ECS, etc.
  - The lattice for each sections was designed.
  - The gradient is constant and the beam loading is not considered at all.
  - In the capture Linac (up to 250 MeV), SW L-band (2a=40mm, E0=25MV/m) has been assumed.
The capture efficiency is re-evaluated assuming a realistic and conservative RF configuration including the beam loading effect.

---
The Second Simulation
DR Acceptance
{size 24 color green { left( z over 0.035 right)^2 + left( %delta over 0.0075 right)^2 < 1 }}
{size 24 color green {%gamma A_x + %gamma A_y < 0.07}}
The typical yield was 1.25.
Electron intensity is normalized
giving 3.0e+10 positron /bunch
In DR dynamic aperture.

---
The Simulation
- Input particle distribution was made by GEANT 4 with 1000 incident electrons (macro particle) on the target.
- Electron Driver : 4.8GeV with s=3.5mm
- Target : t=16mm

---
The booster and ECS were simulated with simple transformation.
Particles hitting physical aperture were removed from the simulation.
The yield is evaluated for particles arrived at the ECS exit with the DR acceptance.
Parameter	Value	Unit
Drive Beam Energy	4.8	GeV
Target material	W-Re
Target thicknesss	16	mm
Beam Size (rms)	3.5	mm
AMD peak field	5.0	T
RAMD (smallest aperture of AMD, 2a)	16.0	mm
Average gradient (MV/m)	6.4 – 27.8	MV/m
Accelerator Aperture (2a)	60	mm
Solenoid	0.5	T
Booster	Hybrid (L-band + S-band)

---
L-band SW structure
- The L-band SW structure designed by J. Wang (SLAC) for the undulator capture section is used.
- 2 of 1.27 m 11 cells L-band TW driven by 50 MW RF unit (10% loss by WG).
- It has a large aperture (2a=60mm) which is optimized for the positron capture.

---
Beam Loading Compensation
- The beam-loading decreases the accelerator gradient which is proportional to the beam current.
- It is quite serious in the capture section because both electron and positron contribute to the loading.
- Static beam-loading : the field is decreased. We need more input power to recover it, otherwise, we have to be patient with the low-field.
- Transient beam-loading : the field is gradually decreased by the effect during the pulse. It causes the energy spread.

---
Single Cell Model : Simple, but not realitic
- The field in SW accelerator
- The voltage becomes constant if
{size 24 color green { V(t) = { 2 sqrt{%beta P_0 r L }} over {1+%beta} left( 1 - e^{- {t over T_0}} right) - {rIL} over {1+%beta} left (1-e^{- {{t-t_b} over T_0}} right) }}
{size 24 color green { T_0 = {2Q} over {%omega (1+%beta)}}}
RF
Beam Loading
{size 24 color green { t_b = -T_0 ln left( I over 2 sqrt{rL over {%beta P_0} }right)}}
{size 24 color green { V_0= { 2 sqrt{%beta P_0 r L }} over {1+%beta} left( 1 - I over 2 sqrt{rL over {%beta P_0} } right) }}

---
Multi-Cell Model
- The beam loading is completely corrected by adjusting the beam timing in the single cell model.
- It is not true for multi-cell model, where the field is a linear sum of modes with different time constants.
- Because the real tube is a multi-cell, the gradient and the beam loading compensation should be examined with this model.

---
Multi-Cell Model : More realistic
Time differential of the energy of the center cell,
Power flow to next cells
Input Power
Beam loading
WG loss
Power loss
Power flow from next cells

---
Time differential of the voltage
For the intermediate cells,
For the end cells,

---
11 linear simultaneous differential equations

---
A can be diagonalized with a orthgonal matrix R as
Because B is diagonal, the equation for V' is simply expressed as 11 independent linear differential equations,

---
The solution for V' is
The solution for V is expressed as a linear sum of the solution for V'
Amplitude for each modes and cells; two modes are dominant (beta=9)

---
Model Comparison
No big difference on the no-load voltage, but 30 % less on the heavyly loaded voltage,
The beam loading compensation works well.

---
The field gradient (E MV/m) is obtained by assuming
  - L=1.27 m (11 cells, L-band SW)
  - R=34e+6 Ohm/m
  - P0=22.5 MW (50MW at klystron, 5MW wave guide loss)
30.6MV for 0A (b=1)
21.2MV for 0.5A(b=2)
14.7MV for 1.0A(b=3)
10.4MV for 1.5A(b=6)
7.3MV for 2.0A(b=9)

---
TM010 mode
Acceleration and
 deceleration
Focusing and
defocusing

---
Capture Strategy
Initial beam is placed at zone 2.
  - e+: dec. and focus.
  - e- : acc and defocus.
Particles are slipped to zone 3 where
  - e+ : acc. and focus.
  - e- : dec. and defocus.
e+ (e-) is continuously (de-) focused.
zone2
zone4
zone3
zone1

---
Beam Loading Current
- Beam loading current
- In the first simulation, the beam loading current is fixed at 1.5A.
- The beam loading current is obtained as a function of t and s and the function is introduced in the next simulation.
- Iterations.
- By changing the drive beam from 6 GeV to 4.8GeV, the beam loading current and the yield is doubled.
{size 24 color green { I_BL= 1 over t_b sum q_i cos left( %omega t_i - k z_i right) }}
6GeV, 4.0mm, Single Cell
Total
e+
e-
4.8GeV, 3.5mm, Multi-Cell

---
Booster
- Booster is simulated as energy enhancement with the following formula,
- Particles with large actions (gAx and gAy) are removed. The threshold is determined to reproduce the tracking simulation done by Y. Seimiya.
{size 24 color green { dE_i = eV_0 cos left( %phi_0 - k z_i right) }}

---
Energy Compressor
- The booster linac consists from L-band and S-band RF accelerators.
- DR longitudinal acceptance (±35mm in z, ±0.75% in dE/E) which are too wide in z and too narrow in dE/E.
- Energy compressor makes a good matching to the acceptance.
- Energy Compressor consists from a dispersive section with a momentum compaction and RF tubes.
V
RF tubes
t
Chicane

---
- Matrix representation: momentum compation
  RF cavity
- Transfer matrix of EC section
- With a matching condition,
ECS acceptance
0.015
DR acceptance
0.015

---
Particle Gymnastic
- Positron is captured at acc. and focusing phase, but with a large energy spread due to the low gradient.
- To suppress the energy spread induced by the booster RF which is dominant after the booster, the chicane is optimized.
- Finally, ECS improves much the yield.
Before chicane
Before ECS
After ECS
After chicane

---
Yield
6GeV Driver, Single Cell model
- The yield is obtained as a function of the initial phase.
- The yield is more than 3, but the IBL is more than 3A which is not manageable
- dg is around 100 (~20%) and some particle loss in booster which is not accounted in the current simulation, is expected.
- The feasibility of the E-driven scheme will be clear with a full simulation with the particle tracking in booster.
4.8GeV Driver, Multi Cell model

---
Summary
- The positron yield is evaluated by assuming a realistic RF unit and a realistic RF model.
- Comparing the previous study based on the single cell model, the yield is better with a higher loading current.
- Transverse motion in the booster and ECS is considered and a tracking simulation is has to be made to estimate the exact yield.