Readout ASIC for LumiCal - FLAME
Marek Idzik on bahalf of AGH-UST
22nd HWG Meeting 25 May 2016

---
Infrastructure for forward calorimeter
Goal in AIDA-2020
For very compact calorimeter we will use already developed precise mechanical frame and precise tungsen plates. We are developing new compact detector module comprising:
A very thin (<1 mm) new sensor board needed
using existing silicon sensors
A thin (<4.5 mm) new readout board with SystemOnChip (SoC) type ultra-low power readout ASICs
New readout ASICs needed – this presentation !
New FPGA based readout board needed

---
New readout ASIC for LumiCal
FLAME – FcaL Asic for Multiplane rEadout
Present ASICs – old technology, high power, non-radhard, limited functionality
FLAME: 16-channel ultra-low power readout ASIC in CMOS 130 nm, FE&ADC in ech channel, fast serialization and data transmission, all functionalities in single ASIC

---
FLAME – FcaL Asic for Multiplane rEadout
Channel architecture
Analogue front-end comprising:
Charge sensitive preamplifier with variable gain
High gain – MIP sensitivity for calibration
Low gain – for shower development (up to 6 pC)
Differential CR-RC shaper with 50ns peaking time
Krummenacher feedback and pedestal trim DAC
10-bit multichannel SAR ADC
Sampling rate up to 40 MSps
DNL, INL < 0.75 LSB
ENOB > 9
Ultra low power consumption
(below 1 mW per channel at 40 MSps)

---
FLAME - FcaL Asic for Multiplane rEadout
Design status in TSMC 130 nm CMOS
Prototype ASIC comprising 8 almost fully functional FLAME channels:
Front-end with variable gain charge preamplifier and differential CR-RC shaper, Tpeak = 50ns
10-bit multichannel SAR ADC
Old backend – same as already presented for ADC prototype
Prototype serializer ASIC comprising:
Fast, ultra low power, ultra low jitter multi-phase PLL
Fast serializer 22b → 1b
Fast SST driver

---
FLAME
8-channel FLAME v0 prototype
8-channel FLAME v0 prototype:
Charge sensitive preamplifier:
Cdet ≈ 5 – 50 pF
Variable gain (calibration and physic mode)
ENC ≈ 950 e- at Cdet = 20 pF in calibration mode
Differential first order shaper (Tpeak ≈ 50 ns)
Front-end power consumption ≈ 1.2 mW per channel
10-bit SAR ADC
INL, DNL < 0.5
ENOB > 9.5
Power consumption ≈ 660 μW at 40 MSps
2600 μm x 2000 μm
Prototypes already in Krakow
Test setup under preparation...

---
FLAME
Serializer prototype
FLAME serializer prototype:
Ultra low power, ultra low jitter multi-phase PLL
Output frequency range 150-450 MHz
22 phases for serializer
22b → 1b serializer with fast SST driver (3.3 – 9.9 Gbps)
Power consumption < 20 mW at 9.9 Gbps
Test data generator
22-bit pseudo-random counter for eye diagram analysis
220-bit preset pattern (via slow control) – constant during transmission – one complete FLAME package
1250 μm x 1250 μm
Prototypes already in Krakow
Test setup under preparation,
First measurements showed basic functionality