## Slide 1: IP region beam jitter
N. Blaskovic
G. Christian, N. Blaskovic, T. Bromwich & R. Ramjiawan
FONT, John Adams Institute, Oxford University

## Slide 2: Introduction
Data taken on 14 June with nominal optics
2 bunch mode
Charge ~ 0.25 x 1010
Used stripline BPMs (P1, P2 & P3)
  Measured resolution ~ 0.7 um
Used IP BPMs (IPA, IPB & IPC)
  40 dB attenuation for large dynamic range
  Measured resolution ~ 4 um
N. Blaskovic

## Slide 3
N. Blaskovic
Measured jitter
~13 um jitter at IPB & IPC

## Slide 4: Propagate to IP
P2 & P3 positions propagated to IP using transfer matrices
Reproduces jitter of ~13 um at IPB & IPC
N. Blaskovic

## Slide 5
N. Blaskovic
IPB
IPC

## Slide 6: Angular beam jitter
Measured jitter is ~13 um at IPB and IPC
True jitter is ~12 um if resolution is ~4 um
As IPB & IPC are each ~8 cm from IP, this corresponds to an IP y’ jitter of ~150 urad
N. Blaskovic

## Slide 7: Angular beam jitter
Tauchi-san:
  Vertical emittance: 9 or 15 pm
  Vertical beta function: 100 um
  If angular jitter is 20 % of angular divergence, expect 60 or 77 urad y’ jitter (respectively)
Kubo-san:
  Fitted IP y’ jitter: 67 urad (ECFA LC 2016)
Our measurement of ~150 urad: too large?
  No beam tuning before shift?
N. Blaskovic