## Slide 1
Course B: rf technology
Normal conducting rf
Part 3: High-Gradient Acceleration
Walter Wuensch, CERN
Tenth International Accelerator School for Linear Colliders
Teijin Academy at Mt. Fuji, Japan
8 to 19 December 2016

## Slide 2
Now – acceleration with high gradient!
"Mavericks and surfer" by Brocken Inaglory. Licensed under CC BY-SA 3.0 via Commons - https://commons.wikimedia.org/wiki/File:Mavericks_and_surfer.jpg#/media/File:Mavericks_and_surfer.jpg

## Slide 3
We have studied the properties of electromagnetic fields in rf structures and the interaction of a beam with those fields.
The underlying equations are Maxwell’s equations and the Lorentz force – linear equations!
When we raise the power we put in a structure, increasing the surface fields, we encounter a whole range of new phenomena.
These phenomena include field emission and vacuum arcing and pulsed surface heating which, in various combinations, affect the beam and can damage a structure.
They limit the high-gradient performance of CLIC structures!

## Slide 4
Today we will study these high-power, and high-gradient, phenomena.
We need to approach the subject in a very different way than the earlier sections since it involves the interplay of many different areas of physics including:
Electromagnetism
Material science
Plasma physics
Field and photo emission
And much of our understanding is still phenomenological so you need to learn a lot about the experiments.

## Slide 5
Introduction
rf system hardware
rf signals
Conditioning
Gradient and pulse length dependencies
Geometrical dependence
Dynamics of high-surface fields
Outline

## Slide 6
Some (round) numbers to keep in mind:
Accelerating gradient - 100 MV/m
Input power - 50 MW
Pulse length - 180 ns
Pulse energy of 12 J.

## Slide 7
Vacuum arc, aka breakdown

## Slide 8
incident power
transmitted
power
reflected power
incident
transmitted
reflected
Envelope of rf pulse

## Slide 9
incident power
transmitted
power
reflected power
incident
transmitted
reflected
Suppression of transmission and reflection due to breakdown

## Slide 10
Testing experimental set-up
and infrastructure

## Slide 11
The basic layout of an rf system
Transmitted
Incident
Reflected
splitter
load
directional coupler
klystron
accelerating structure

## Slide 12
This klystron modulator unit feeds
this accelerating structure.

## Slide 13
Klystron-based X-band test stands
around the world
XBox-1: 50 MW, 50 Hz
XBox-2: 50 MW, 50 Hz
XBox-3: 50 MW, 400 Hz!
NEXTEF
KEK
ASTA
SLAC

## Slide 14
Gallery
Bunker
Clockwise from top-left:
Modulator/klystron (50MW, 1.5us pulse)
Pulse compressor (250ns, ratio 2.8)
DUT + connections
Acc. structure (TD26CC)
Typical test stand Layout

## Slide 15
System Layout and diagnostics

## Slide 17: Accelerating Structure Diagnostics
CLIC Accelerating Structure
RF Hybrid
RF Load
RF Load
RF Load
Asymmetric Reflection
Incident power
Reflected Power
Transmitted Power
Ion gauge readout
Ion gauge readout
50 dB directional coupler
Upstream Faraday cup signal
Downstream Faraday cup signal
RF Power From Klystron
WR90 Waveguide
Input coupler
Output coupler
Beam-pipe
Beam-pipe

## Slide 18: Accelerating Structure Diagnostics
Faraday Cup
Directional coupler
Ion Gauge
Structure output couplers
RF Load
Structure input couplers
Temperature probe
RF hybrid splitter
(behind metal support)
Ion Pump
Vacuum valve
Ion Gauge

## Slide 19: Operator display

## Slide 20
Pulsed dc system at CERN. Simple system which allows high-gradient test of electrodes using short dc pulses.
Reproduces very well pulsed rf behaviour.
I will refer to pulsed dc results a number of times in the coming slides.
copper electrode
vacuum chamber

## Slide 21
Marx generator – up to 3 kHz!
Pulsed dc system

## Slide 22
Signals and detection of breakdown
aka vacuum arc

## Slide 23: BD Detection: Normal Pulse
Transmitted pulse follows the incident pulse but with ~4dB of attenuation.
Reflected signal is ~20dB lower than incident pulse.
Only a few mV seen on the faraday cups. DC2-Upstream sees 1/10 of the signal compared to downstream.

## Slide 24: BD Detection: Breakdown
Transmitted pulse drops as the arc is established.
Reflected power increases to the same order as the incident pulse.
Faraday cup voltages are saturated: 100-1000x increase in charge emitted.
We can use the difference in time between the transmitted power falling and the reflected power increasing to find the BD cell location.
The phase of the reflected signal is used to pinpoint cell location.
Wilfrid Farabolini

## Slide 25: 51+52 Normal pulse #36
Incident
(F)
F RsX10 Tr
FC-UP FC-Mid Threshold
Last pulse
Last pulse but one
Difference between the two
Dashed lines = Analysis threshold
T. Higo, KEK
Test of TD18 structure
Reflected
(Rs)
Transmitted
(Tr)

## Slide 26: 51+52 typical BD pulses #72 Reflected RF back from klystron again
T. Higo, KEK
Test of TD18 structure

## Slide 27
From CERN XBoxes

## Slide 28
What is happening during breakdown and why does it interrupt power?
We’ll come back to this question but for now:
A field emission site, suddenly evolves and creates a local plasma. This plasma spot interacts with the fields and the copper surface and results in massively higher current emission. This current,
pico or nano amp for field emission
tens or hundreds of amps for arcing
creates something like a short circuit for the incoming rf.

## Slide 29
I will now show an animation of a breakdown simulation by Kyrre Sjobaek, done for his PhD.
It is a simulation of the onset of breakdown, starting from field emission and going through the formation of a plasma, a plasma sheath and dramatically rising emitted current.
The code is ArcPIC and simulates a 20 micron wide dc gap.

## Slide 31
Breakdown rate
BDR (BreakDown Rate) is the fraction of pulses which have a vacuum arc. Arc currents and lost acceleration result in lost luminosity on that pulse.
CLIC specification:
3x10-7 1/pulse/m
At 50 Hz, per structure:
1 BD every 3 days
Per facility:
1 BD someplace every 2 seconds

## Slide 32
Performance summary at CLIC specifications

## Slide 33
Breakdowns in more detail

## Slide 34
Breakdown position determination using timing and phase.

## Slide 35
Important dependencies
Over many experiments, rf and pulsed dc, we have observed that the BDR (BreakDown Rate) depends on the rf pulse parameters - both gradient and pulse length.
The approximate behaviour is given by:
This is a crucial dependency.
I’ll first show you some data from which we extract this dependency, then a bit of theory which may explain it.

## Slide 36: Relevant data points of BDR vs Eacc
Steep rise as Eacc, 10 times per 10 MV/m, less steep than T18
TD18
T. Higo, KEK

## Slide 37: TD18_#2 BDR versus width at 100MV/m around 2800hr and at 90MV/m around 3500hr
Similar dependence at 90 and 100 if take usual single pulse?
TD18
T. Higo, KEK

## Slide 39
soft Cu
hard Cu
From master’s thesis of Laura Mercade Morales

## Slide 41
V. Dolgashev, EAAC2015

## Slide 42
Long term operation and conditioning

## Slide 43: Conditioning data
Xbox-1: TD26CC#1 full conditioning history
An automatic conditioning algorithm was enable to keep a constant BDR while increasing the power.
Measurement
BDR = 2e-6 bpp at 100MV/m 250ns

## Slide 44
Conditioning
Accelerating structures do not run right away at full specification – pulse length and gradient need to be gradually increased while pulsing. Typical behaviour looks like this:
4 million pulses per day at 50 Hz
Pulse length steps
BDR falls during flat E run

## Slide 45: Cavity Conditioning Algorithm
Automatically controls incident power to structure.
Short term: +10kW steps every 6 min and -10kW per BD event.
Long Term: Measures BDR (1MPulse moving avg.) and will stop power increase if BDR too high.

## Slide 46: Conditioning data
Xbox-1: TD26CC#1 full conditioning history
An automatic conditioning algorithm was enable to keep a constant BDR while increasing the power.
Measurement
BDR = 2e-6 bpp at 100MV/m 250ns

## Slide 47: Scaling: description of conditioning state
BDR= 7e-5 bpp
2e-5 bpp
2e-6 bpp
CONDITIONING
BDR measure
Raw data full history
Equivalent gradient curve with constant pulse length of 250ns since the beginning
TD26CC#1 scaled gradient
Equivalent gradient curve with constant pulse length of 250ns and constant BDR of 2e-5 bpp since the beginning

## Slide 48: Collection of conditioning histories
CLIC damped (TD) structures
TD26CC (XBOX-1)
TD24R05 (XBOX-1)
TD24R05#4 (NEXTEF)
TD24R05#2 (NEXTEF)

## Slide 49
Scaled gradient vs cumulative number of PULSES
Scaled gradient vs cumulative number of BREAKDOWNS
Comparing conditioning
Pulses
Breakdowns
Alberto Degiovanni, Walter Wuensch, and Jorge Giner Navarro, Comparison of the conditioning of high gradient accelerating structures, Phys. Rev. Accel. Beams 19, 032001 (2016) - Published 4 March 2016

## Slide 50
Important question:
What is happening during conditioning?
Hope is the surface getting better?
Those really long runs you saw effectively cost a lot of money!
hard copper
heat treated copper
Pulsed dc system electrode

## Slide 51: High-Gradient and Breakdown rate limits
Scaled BDR
Limiting quantities must be studied: gradient, Sc, peak E and H field, pulsed surface heating…
The trend at higher number of pulses might reach a limit in BDR
New CLIC TD structure upcoming tests will confirm these results
High repetition DC systems provide considerable new data to study conditioning phenomenology and operation dependencies.
TD26CC
TD24R05#4
TD24R05#2

## Slide 52
Breakdown statistics
rf
dc
KEK

## Slide 53
soft Cu
hard Cu
From master’s thesis of Laura Mercade Morales

## Slide 54
Processed for 1744 hours.
KEK

## Slide 55
    Quantifying geometrical dependence of high-power performance

## Slide 56
There is a strong interplay between the rf design of accelerating structures and the overall performance of the collider for example:
Group velocity, beam loading and all that affect rf-to-beam efficiency
Another important dependency comes through wakefields, which affect emittance growth. We will look into wakefields tomorrow.
But rf geometry has an extremely strong influence on accelerating gradient and BDR.
In fact the three areas – rf-to-beam efficiency, wakefields and high-gradient performance – interact in a complex way overall accelerator optimization.
A crucial question becomes can we quantify the dependence of achievable gradient on rf geometry?
Importance of geometric dependence

## Slide 57
Performance summary at CLIC specifications

## Slide 58
Can we quantify the dependence of achievable accelerating gradient on the geometry?
Where does such a geometrical dependency come from?
Trying to understand, derive and quantify geometrical dependence has been a significant effort because an essential element of the overall design and optimization of the collider.
We are now going to focus on the limit coming from breakdown. There is another limit from pulsed surface heating which I will come back to later.
The big questions

## Slide 59
The basic element is to express our high-power limits as a function of the unperturbed fields inside our structures – like the electric field limit in dc spark.
So first we are going to make sure that we have a feel for how those fields vary as a function of geometry.
We use a specific example of iris variation for a fixed phase advance in a travelling wave structure.
The basic approach

## Slide 60: Field distribution
Simulation in HFSS12
Field values are normalized to accelerating gradient, Eacc=100MV/m
Frequency: 11.424GHz
Phase advance per cell: 120 degree
Iris radius: 3mm
vg /c= 1.35%
Electric field (V/m)
Magnetic field (A/m)
Poynting vector (W/m2)

## Slide 61: Parameters v.s. iris
Chart: 
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9
vg /c | 9.8162e-05 | 0.00075834 | 0.0027293 | 0.0067777 | 0.013511 | 0.023253 | 0.036139 | 0.052019 | 0.070677 | 0.091722 | 0.1148 | 0.13944 | 0.16525 | 0.1919 | 0.21899 | 0.24626 | 0.27348
Chart: 
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9
Esurfmax/Eacc | 1.8016 | 1.7843 | 1.8563 | 1.9458 | 2.0452 | 2.1058 | 2.1958 | 2.297 | 2.3963 | 2.5077 | 2.6096 | 2.7692 | 2.8643 | 3.0208 | 3.1547 | 3.3227 | 3.48
Chart: 
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9
Hsurfmax/Eacc (A/V) | 0.0022276 | 0.0022831 | 0.0023565 | 0.0024452 | 0.0025463 | 0.0026578 | 0.0027777 | 0.0029039 | 0.0030353 | 0.0031702 | 0.0033085 | 0.0034489 | 0.0035918 | 0.0037356 | 0.003881 | 0.0040272 | 0.0041746
Chart: 
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9
R/Q (linac Ohm) | 191.1082 | 181.4019 | 169.4077 | 156.0806 | 142.3092 | 128.6343 | 115.5578 | 103.3543 | 92.1715 | 82.0482 | 72.954 | 64.8557 | 57.6619 | 51.2941 | 45.6678 | 40.7015 | 36.32
R/Q = V2acc/(ωU)
Simulation in HFSS12
Iris thickness: 1.66mm
Frequency: 11.424GHz
Phase _adv/cell: 120 degree

## Slide 62
Trying to achieve these specifications has resulted over the years in the test of many structures of diverse rf design.
The preparation and testing conditions of the test structures which were built were not always the same – these processes also evolved over the period the structures were being developed.
But the wide variety of structure geometries were tested under reasonably similar conditions.
So we have used this unique set of data to try to understand and then quantify the geometrical dependency of gradient.

## Slide 63: Maximum surface electric and magnetic fields
Es = 250 MV/m or higher has been achieved in several cases: very low or zero group velocity
Waveguide
damped

## Slide 64
What do can make out of this mess?
My personal conclusion from looking at data like this, was that a something else is important, beyond E and B surface fields.
This something felt like it had to be related to the power flowing through the structure. In particular some kind of power density, since larger apertures generally support larger powers.
This is reasonable when you think about what we know about breakdown.
Field emission is pico or nano amps. Breakdowns in rf and dc produce 10’s, 100’s even kA of current.
A lot of power is needed to accelerate so much current. The breakdown must need to be “fed” with the necessary power so power density is crucial.

## Slide 65
W. Wuensch
Observations about RF Breakdown from the CLIC High Gradient Testing Program
CERN-AB-2006-085; CLIC-Note-700.- Geneva : CERN, 2006 - 8 p. - Published in : AIP Conf. Proc.: 877 (2006) , pp. 15-21
global power flow

## Slide 66
A. Grudiev, S. Calatroni, and W. Wuensch,
New local field quantity describing the high gradient limit of accelerating structures,
Phys. Rev. ST Accel. Beams 12, 102001 (2009)

## Slide 67
This has resulted in the development of two power-density based design criteria:
global power flow
local complex power flow
Hs/Ea
Es/Ea
Sc/Ea2
There is no proof (yet) but rather the general set of physical arguments plus reasonably good consistency with measurements.

## Slide 68: Power flow related quantities: Sc and P/C
Sc = 4 - 5 MW/mm2
P/C = 2.3 – 2.9 MW/mm

## Slide 69: Summary on the high-power RF constraints
RF breakdown and pulsed surface heating constraints used for CLIC_G design (2007):
Esmax < 250 MV/m
Pin/Cin·(tpP)1/3 = 18 MW·ns1/3/mm
ΔTmax(Hsmax, tp) < 56 K
Optimistic RF breakdown and pulsed surface heating constraints for BDR=10-6 bpp/m:
Esmax ·(tpP)1/6 < 250 MV/m · (200ns)1/6
Pin/Cin·(tpP)1/3 < 2.8 MW/mm · (200ns)1/3 = 17 [Wu]
Scmax ·(tpP)1/3 < 5 MW/mm2 · (200ns)1/3
and
ΔTmax(Hsmax, tp) < 50 K
Depending on degree of our optimism a safety margin has to be applied.
Varying RF constraints in the optimization how much money one can save by being optimistic.
A. Grudiev

## Slide 70: Optimization procedure
Bunch population
Structure
parameters
Cell parameters
Bunch
separation
Beam
dynamics
<Ea>, f, ∆φ, <a>, da, d1, d2
N
Ns
Q, R/Q, vg, Es/Ea, Hs/Ea
Q1, A1, f1
η, Pin, Esmax, ∆Tmax
Ls, Nb
rf
constraints
Cost function
minimization
YES
NO
Beam
dynamics

## Slide 71: Simplified Parameter Diagram
Drive Beam Generation Complex
Pklystron, Nklystron, LDBA, …
Main Beam Generation Complex
Pklystron, …
Two-Beam Acceleration Complex
Lmodule, Δstructure, …
Idrive
Edrive
τRF
Nsector
Ncombine
fr
N
nb
ncycle
E0
fr
Parameter Routine
Luminosity, …
Ecms, G, Lstructure
Variable | Meaning | Current value
Idrive | Drive beam current | 101A
Edrive | Drive beam energy | 2.37GeV
τRF | Main linac RF pulse length | 244ns
Nsector | Number of drive beam sectors per linac | 4
Ncombine | Combination number | 24
fr | Repetition rate | 50Hz
N | Main beam bunch charge in linac | 3.72e9
nb | MB bunches per pulse | 312
ncycle | Spacing between MB bunches | 6 cycles
E0 | MB energy at linac entrance | 9GeV
Ecms | Centre-of-mass energy | 500GeV
G | Main linac gradient | 100MV/m

## Slide 72
A few more words of background.
A number of effects which emerge at high-power and high-gradient.
These include:
Breakdown or vacuum arc – This is essentially the same phenomenon you all know from daily life, sparking and arcing, but in vacuum. This is the main effect limiting gradient in CLIC.
Pulsed surface heating – Surface currents cause pulsed temperature rises, consequently cyclical stress which breaks up the surface and induces breakdown.
Electromigration – This is a new area of investigation in which rf currents directly affect the crystal structure of the copper surface.
Dark currents – Field emission currents are captured by the rf and can be accelerated over longer distances.
Dynamic vacuum – Field emission currents desorbs gasses which cause pressure rises during the rf pulse.
Multipactor – not really a problem at the highest gradients.

## Slide 73
A closer look at the dynamics of Breakdown!
From pA to kA and from Angstroms to 100s of m to mms.

## Slide 74
An overview of the breakdown process
Vacuum
Copper

## Slide 75
Actually real surfaces are imperfect
Vacuum
Copper

## Slide 76
And the material below the surface isn’t perfect either
Vacuum
Copper
slip planes
voids and inclusions
vacancies
dislocations

## Slide 77
Add an external electric field, around 200 MV/m. Surface charges re-arrange themselves in fs. Surface experiences εE2 tensile force.
Vacuum
Copper
dislocations
slip planes
voids and inclusions
vacancies
εE2 tensile force

## Slide 78
Field emission current flows from metal into vacuum (Fowler-Nordheim) from local areas (O[10 nm]) of geometrical field enhancement and low local work function. There is a local field enhancement β of around 50-100. The total current from something like 0.1 mm2 is a nanoAmp.
Vacuum
Copper
dislocations
slip planes
voids and inclusions
vacancies
εE2 tensile force

## Slide 79
The external electric field causes the tensile stress and field emission current causes thermal induces stresses so the material imperfections and surface features evolve – plastic deformation.
Vacuum
Copper
dislocations move
slip planes move
voids and inclusions
evolve
vacancies move
εE2 tensile force

## Slide 80
Vacuum
Copper
εE2 tensile force
dislocations move
slip planes move
voids and inclusions
evolve
vacancies move
The external electric field causes the tensile stress and field emission current causes thermal induces stresses so the material imperfections and surface features evolve – plastic deformation.

## Slide 81
All the while, neutral copper atoms are coming off the surface field assisted evaporation.
The details of this process is process is a fundamental open question.
Vacuum
Copper
Cu
Cu
Cu
Cu
Cu
Cu
Cu
Cu
εE2 tensile force
dislocations move
slip planes move
voids and inclusions
evolve
vacancies move

## Slide 82
The copper atoms are ionized by the field emission current. the positively charged ions head to the surface and the electrons add to the emission current.
Vacuum
Copper
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
εE2 tensile force
dislocations move
slip planes move
voids and inclusions
evolve
vacancies move

## Slide 83
The copper ions hit the surface and sputter more copper in addition to that produced at by the original emission process.
Vacuum
Copper
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
Cu
Cu
Cu
Cu
εE2 tensile force
dislocations move
slip planes move
voids and inclusions
evolve
vacancies move

## Slide 84
One of these emission points, on some rf or dc pulse, at some point passes a threshold and the process runs away. We will now switch to a computer simulation of the run-away process.
Vacuum
Copper
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
Cu+
Cu
Cu
Cu
Cu
εE2 tensile force
dislocations move
slip planes move
voids and inclusions
evolve
vacancies move

## Slide 86
It all starts with field emission

## Slide 87
The surface potential used for solving the Fowler-Nordheim equation
V(z)=
{
-Wa for z<0
-eEz-e2/4z for z>0

## Slide 88
The Fowler-Nordheim equation
(approximate, practical form)
Units: [I]=A, [E]=MV/m, [Ae]=m2, []=eV and []=dimensionless
Values:  = 4.5 eV for copper

## Slide 89
The Fowler-Nordheim equation
Analyzing real data
-
You will have the opportunity to analyze a real set of data tonight for homework!

## Slide 90
Field emitter observed in Chamonix, France. MeVArc mini-school on rf acceleration.

## Slide 91: Electron emission
Copper surface
typical picture 
geometric perturbations (b)
Fowler Nordheim Law (RF fields):
High field enhancements (b) can field emission.
Low work function (f0) in small areas can cause field emission.
oxides
alternate picture 
material perturbations (f0)
inclusions
peaks
grain
boundaries
cracks
(suggested by Wuensch and colleagues)
(b, f0, Ae, E0)
IFN

## Slide 92: Schottky Enabled Photo-electron Emission Measurements
Experimental parameters
  work function of copper = f0 = 4.65 eV
  energy of l=400nm photon = hn= 3.1 eV
  Laser pulse length
    Long = 3 ps
    Short = 0.1 ps
  Laser energy ~1 mJ (measured before laser input window)
  Field (55 – 70 MV/m)
ICT
g
e-
First results
from Tsinghua
Data 2010-10-04
Should not get
photoemission

## Slide 93: Long Laser Pulse (~ 3ps) E=55 MV/m@ injection phase=80  55sin(80)=54
Q(pC)
laser energy (mJ)
photocathode input window
First results
from Tsinghua
Data 2010-10-04
Q I
single photon emission

## Slide 95
Identification of a nanometer-sized field emitter.
Laser-induced asymmetric faceting and growth of nano-protrusion on a tungsten tip
Hirofumi Yanagisawa, Vahur Zadin, Karsten Kunze, Christian Hafner, Alvo Aabloo, Dong Eon Kim, Matthias F. Kling, Flyura Djurabekova,Q1 5 Jürg Osterwalder and Walter Wuensch
Accepted for publication in APL Photonics
arXiv1605.05393

## Slide 96
Hardware status and evolution:
plane cathode, tip anode
Plane cathode, typically 12 mm diameter disk sample. Tip anode, 1 mm radius hemispherical tip. Moveable anode with capacitive gap-height control. Gaps typically 10-50 μm.

## Slide 97: What are the field emitters? Why do we look for dislocations?
The dislocation motion is strongly bound to the atomic structure of metals. In FCC (face-centered cubic) the dislocation are the most mobile and HCP (hexagonal close-packed) are the hardest for dislocation mobility.
A. Descoeudres, F. Djurabekova, and K. Nordlund, DC Breakdown experiments with
cobalt electrodes, CLIC-Note XXX, 1 (2010).

## Slide 98
Pulsed surface heating.
Fatigue process driven by pulsed resistive wall losses

## Slide 99: Pulsed surface heating limit
Cell # (cell #1 is a input matching cell):
4
5
6
7
8
9
10
11
12
13
15
14
17
?16?
Images courtesy of M. Aicheler: http://indico.cern.ch/getFile.py/access?contribId=0&resId=1&materialId=slides&confId=106251
18
Last
regular
cell: 19
It seems that cell #10 (regular cell #9 ~ middle cell) exhibits the level of damage which could be considered as a limit.
A. Grudiev
TD24

## Slide 100
Fundamental physics of high fields on metal surfaces
High-gradient rf design
Fabrication of prototypes and technology optimization
High-gradient testing
High-power test stands